## Slide 1: COMP 4611 Design and Analysis of Computer Architectures Final Exam Review
Notes: Please if anyone has additional comments please speak up

## Slide 2: IA-64 Bundles
Bundle == The “VLIW” Instruction
  Templates define the types of instructions in a bundle
    5-bit template encoding
    also encodes “stops”
  Three 41-bit instructions
  Instructions in consecutive bundles can be connected together and executed simultaneously
128 bits per bundle
  average of 5.33 bytes per instruction
    x86 only needs 3 bytes on average

## Slide 3: Bundle Templates
Not all combinations of A, I, M, F, B, L and X are permitted
Group “stops” are explicitly encoded as part of the template
  can’t stop just anywhere
Some bundles identical
except for group stop

## Slide 4
MEM
MEM
INT
INT
FP
FP
B
B
B
128-bit instruction bundles from I-cache
S2
S1
S0
T
Fetch one or more bundles for execution
(Implementation, Itanium® takes two.)
Try to execute all instructions in
parallel, depending on available units.
Retired instruction bundles
Processor
Explicitly Parallel Instruction Computing (EPIC)
functional units
MEM
MEM
INT
FP
FP
B
B
B
Notes: How are instructions executed by the machine.
The goal is to schedule bundles so that most of the excution units have work to do.
Itanium(Merced) pulls in 2 bundles at a time and tries to execute them.
Subsequent implementation will have more execution units

## Slide 5: Loop-Level Parallelism (LLP) Analysis
Loop-Level Parallelism (LLP) analysis focuses on whether data accesses in later iterations of a loop are data dependent on data values produced in earlier iterations.
e.g. in for (i=1; i<=1000; i++)
x[i] = x[i] + s;
The computation in each iteration is independent of the previous iterations and the loop is thus parallel. The use of x[i] twice is within a single iteration.
    Thus loop iterations are independent from each other
Loop-carried Dependence: A data dependence between different loop iterations (data produced in earlier iteration used in a later one) – limits parallelism.
Instruction level parallelism (ILP) analysis, on the other hand, is usually done when instructions are generated by the compiler.

## Slide 6: Memory System
Main memory generally uses Dynamic RAM (DRAM),
which uses a single transistor to store a bit, but requires a periodic data refresh (~every 8 ms).
Cache uses SRAM: Static Random Access Memory
  No refresh (6 transistors/bit vs. 1 transistor/bit for DRAM)
Size: DRAM/SRAM ­ 4-8, Cost & Performance: SRAM/DRAM ­ 8-16
Performance metrics
  Latency is concern of cache
  Access time: The time it takes between a memory access request and the time the requested information is available to cache/CPU.
  Cycle time: The minimum time between unrelated requests to memory (greater than access time in DRAM to allow address lines to be stable)‏
  Memory bandwidth: The maximum sustained data transfer rate between main memory and cache/CPU.

## Slide 7: Memory Technology
SRAM
  Requires lower power to retain bit than DRAM
  Requires 6 transistors/bit
DRAM
  Must be re-written after being read
  Must also be periodically refeshed
    Every ~ 8 ms
    Each row can be refreshed simultaneously
  One transistor/bit
  Address lines are multiplexed:
    Upper half of address: row access strobe (RAS)
    Lower half of address: column access strobe (CAS)

## Slide 8: Conventional DRAM Organization
d x w DRAM:
  dw total bits organized as d supercells of size w bits
cols
rows
0
1
2
3
0
1
2
3
internal row buffer
16 x 8 DRAM chip
addr
data
supercell
(2,1)
2 bits
/
8 bits
/
memory
controller
(to CPU)

## Slide 9: Memory Technology
Amdahl:
  Memory capacity should grow linearly with processor speed
  Unfortunately, memory capacity and speed has not kept pace with processors
Some optimizations:
  Multiple accesses to same row
  Synchronous DRAM
    Added clock to DRAM interface
    Burst mode with critical word first
  Wider interfaces
  Double data rate (DDR)
  Multiple banks on each DRAM device

## Slide 10: Memory Performance Gap

## Slide 11: How to make memory system better?
Programmers want unlimited amounts of memory with low latency
Fast memory technology is more expensive per bit than slower memory
Solution: organize memory system into a hierarchy
  Entire addressable memory space available in largest, slowest memory
  Incrementally smaller and faster memories, each containing a subset of the memory below it, proceed in steps up toward the processor
Temporal and spatial locality insures that nearly all references can be found in smaller memories
  Gives the illusion of a large, fast memory being presented to the processor

## Slide 12: Memory Hierarchy Design
Memory hierarchy design becomes more crucial with recent multi-core processors:
  Aggregate peak bandwidth grows with # cores:
    Intel Core i7 can generate two references per core per clock
    Four cores and 3.2 GHz clock
      25.6 billion 64-bit data references/second +
      12.8 billion 128-bit instruction references
      = 409.6 GB/s!
    DRAM bandwidth is only 6% of this (25 GB/s)
    Requires:
      Multi-port, pipelined caches
      Two levels of cache per core
      Shared third-level cache on chip
High-end microprocessors have >10 MB on-chip cache
  Consumes large amount of area and power budget

## Slide 13: Memory Hierarchy
The idea is to build a memory subsystem that consists of:
  Very small, very fast, very expensive memory “close” to the processor.
  Larger, slower, but more affordable memory “further away” from the processor.
  Hence, provide the appearance of virtually unlimited memory while minimizing delays to the processor.
The memory hierarchy is organized into levels of memory with the smaller, more expensive, and faster memory levels closer to the CPU: registers, then primary Cache Level (L1), then additional secondary cache levels (L2, L3…), then main memory, then mass storage (virtual memory).

## Slide 14: Levels of The Memory Hierarchy
Part of The On-chip CPU Datapath
16-256 Registers
One or more levels (Static RAM):
Level 1: On-chip 16-64K
Level 2: On or Off-chip 128-512K
Level 3: Off-chip 1M-64M
Registers
Cache
Main Memory
Magnetic Disc
Optical Disk or Magnetic Tape
Farther away from
The CPU
Lower Cost/Bit
Higher Capacity
Increased Access
Time/Latency
Lower Throughput
DRAM, RDRAM
16M-16G
Interface:
SCSI, RAID,
IDE, 1394
4GB-2TB

## Slide 15: Memory Hierarchy Basics
When a word is not found in the higher level, a miss occurs:
  Fetch word from lower level in hierarchy, requiring a higher latency reference
  Also fetch the other words contained within the block
    Takes advantage of spatial locality
  Place block into cache in any location within its set, determined by address
    block address MOD number of sets

## Slide 16: Memory Hierarchy Operation
If an instruction or operand is required by the CPU, the levels of the memory hierarchy are searched for the item starting with the level closest to the CPU (Level 1 cache):
  If the item is found, it’s delivered to the CPU resulting in a cache hit.
  If the item is missing from an upper level, resulting in a miss, the level just below is searched.
  For systems with several levels of cache, the search continues with cache level 2, 3 etc.
  If all levels of cache report a miss then main memory is accessed.
    CPU « cache « memory: Managed by hardware.
  If the item is not found in main memory resulting in a page fault, then disk (virtual memory), is accessed for the item.
    Memory « disk: Managed by hardware and the operating system.

## Slide 17: Memory Hierarchy Basics
n sets => n-way set associative
  Direct-mapped cache => one block per set
  Fully associative => one set
Writing to cache: two strategies
  Write-through
    Immediately update lower levels of hierarchy
  Write-back
    Only update lower levels of hierarchy when an updated block is replaced
  Both strategies use write buffer to make writes asynchronous

## Slide 18: Memory Hierarchy Basics
Miss rate
  Fraction of cache access that result in a miss
Causes of misses
  Compulsory
    First reference to a block
  Capacity
    Blocks discarded and later retrieved
  Conflict
    Program makes repeated references to multiple addresses from different blocks that map to the same location in the cache

## Slide 19: Memory Hierarchy Basics
Note that speculative and multithreaded processors may execute other instructions during a miss
  Reduces performance impact of misses

## Slide 20
Impact on Performance
Suppose a processor executes at
  Clock Rate = 200 MHz (5 ns per cycle)
  CPI = 1.1
  50% arith/logic, 30% ld/st, 20% control
Suppose that 10% of memory operations get 50 cycle miss penalty
CPI = ideal CPI + average stalls per instruction = 1.1(cyc) +( 0.30 (datamops/ins) x 0.10 (miss/datamop) x 50 (cycle/miss) ) = 1.1 cycle + 1.5 cycle = 2.6
58 % of the time the processor is stalled waiting for memory!
a 1% instruction miss rate would add an additional 0.5 cycles to the CPI!

## Slide 21: Memory Hierarchy: Motivation The Principle Of Locality
Programs usually access a relatively small portion of their address space (instructions/data) at any instant of time (loops, data arrays).
Two types of locality:
  Temporal Locality: If an item is referenced, it will tend to be referenced again soon.
  Spatial locality: If an item is referenced, items whose addresses are close by will tend to be referenced soon .
The presence of locality in program behavior (e.g., loops, data arrays), makes it possible to satisfy a large percentage of the program’s data accesses (both instructions and operands) using memory levels closer to the CPU.
Address Space
0
2n - 1
Probability
of reference

## Slide 22: Memory Hierarchy: Terminology
A Block: The smallest unit of information transferred between two levels.
Hit: Item is found in a block in the upper level (example: Block X)
  Hit Rate: The fraction of memory accesses found in the upper level.
  Hit Time: Time to access the upper level which consists of
    memory access time + time to determine hit/miss
Miss: Item needs to be retrieved from a block in the lower level (Block Y)
  Miss Rate = 1 - (Hit Rate)
  Miss Penalty: Time to replace a block in the upper level +
    Time to deliver the block to the processor (or the further-upper-level)
Hit Time << Miss Penalty
Lower Level
Memory
Upper Level
Memory
To Processor
From Processor
Blk X
Blk Y

## Slide 23: Caching in a Memory Hierarchy
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Larger, slower, cheaper storage
device at level k+1 is partitioned
into blocks.
Data is copied between
levels in block-sized transfer units
8
9
14
3
Smaller, faster, more expensive
device at level k caches a
subset of the blocks from level k+1
Level k:
Level k+1:
4
4
4
10
10
10

## Slide 24: General Caching Concepts
Request
14
Request
12
Program needs object d, which is stored in some block b.
Cache hit
  Program finds b in the cache at level k. E.g., block 14.
Cache miss
  b is not at level k, so level k cache must fetch it from level k+1. E.g., block 12.
  If level k cache is full, then some current block must be replaced (evicted). Which one is the “victim”?
    Placement policy: where can the new block go? E.g., b mod 4
    Replacement policy: which block should be evicted? E.g., LRU
9
3
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Level
k:
Level
k+1:
14
14
12
14
4*
4*
12
12
0
1
2
3
Request
12
4*
4*
12

## Slide 25: Cache Design & Operation Issues
Q1: Where can a block be placed in cache? (Block placement strategy & Cache organization)
  Fully Associative, Set Associative, Direct Mapped.
Q2: How is a block found if it is in cache? (Block identification)
  Tag/Block.
Q3: Which block should be replaced on a miss? (Block replacement)
  Random, LRU.
Q4: What happens on a write? (Cache write policy)
  Write through, write back.

## Slide 26: Cache Organization & Placement Strategies
Placement strategies or mapping of a main memory data block onto cache block frame addresses divide cache into three organizations:
Direct mapped cache: A block can be placed in one location only, given by:
(Block address) MOD (Number of blocks in cache)
  Advantage: It is easy to locate blocks in the cache (only one possibility)
  Disadvantage: Certain blocks cannot be simultaneously present in the cache (they can only have the same location)

## Slide 27: Cache Organization: Direct Mapped Cache
0
0
0
0
1
0
0
1
0
1
0
1
0
0
1
0
1
1
0
1
1
0
0
0
1
1
0
1
0
1
1
1
0
0
1
1
1
1
0
1
0
0
0
C
a
c
h
e
M
e
m
o
r
y
0
0
1
0
1
0
0
1
1
1
0
0
1
0
1
1
1
0
1
1
1
A block can be placed in one location only, given by:
(Block address) MOD (Number of blocks in cache)
In this case: (Block address) MOD (8)
32 memory
blocks
cacheable
8 cache block
frames
(11101) MOD (1000) = 101

## Slide 28: Direct Mapping
0xF0
11111
11111
0xAA
0x0F
00000
00000
0x55
0
1
0
00001
0
1
0
1
0x0F
00000
00000
0x55
11111
0xAA
0xF0
11111
Tag
Index
Data
Direct mapping:
  A memory value can only be placed at a single corresponding location in the cache

## Slide 29: Cache Organization & Placement Strategies
Fully associative cache: A block can be placed anywhere in cache.
  Advantage: No restriction on the placement of blocks. Any combination of blocks can be simultaneously present in the cache.
  Disadvantage: Costly (hardware and time) to search for a block in the cache
Set associative cache: A block can be placed in a restricted set of places, or cache block frames. A set is a group of block frames in the cache. A block is first mapped onto the set and then it can be placed anywhere within the set. The set in this case is chosen by:
(Block address) MOD (Number of sets in cache)
  If there are n blocks in a set the cache placement is called n-way set-associative, or n-associative.
  A good compromise between direct mapped and fully associative caches (most processors use this method).

## Slide 30: Set Associative Mapping (2-Way)
0xF0
1111
1111
0xAA
0x0F
0000
0000
0x55
0
1
0x0F
0x55
0xAA
0xF0
Tag
Index
Data
00
01
10
0001
10
11
0000
0000
1111
1111
Way 1
Way 0
Set-associative mapping:
  A memory value can be placed in any block frame of a set corresponding to the block address

## Slide 31: Fully Associative Mapping
0xF0
1111
1111
0xAA
0x0F
0000
0000
0x55
0x0F
0x55
0xAA
0xF0
Tag
Data
000110
000001
000000
111110
111111
0xF0
1111
1111
0xAA
0x0F
0000
0000
0x55
0x0F
0x55
0xAA
0xF0
000110
000001
000000
111110
111111
Fully-associative mapping:
  A block can be stored anywhere in the cache

## Slide 32: Types of Caches: Organization
Type of cache | Mapping of data from memory to cache | Complexity of searching the cache
Direct mapped (DM) | A memory value can be placed at a single corresponding location in the cache | Easy search mechanism
Set-associative (SA) | A memory value can be placed in any of a set of locations in the cache | Slightly more involved search mechanism
Fully-associative (FA) | A memory value can be placed in any location in the cache | Extensive hardware resources required to search (CAM)
DM and FA can be thought as special cases of SA
  DM  1-way SA
  FA  All-way SA

## Slide 33: Cache Organization Example

## Slide 34: Cache Organization Tradeoff
For a given cache size, there is a tradeoff between hit rate and complexity
If L = number of lines (blocks) in the cache, L = Cache Size / Block Size
How many places Name of Number of Sets for a block to go cache type
1 Direct Mapped L
n n-way associative L/n
L Fully Associative 1
Number of comparators needed to compare tags

## Slide 35: Locating A Data Block in Cache
Each block in the cache has an address tag.
The tags of every cache block that might contain the required data are checked in parallel.
A valid bit is added to the tag to indicate whether this cache entry is valid or not.
The address from the CPU to the cache is divided into:
  A block address, further divided into:
    An index field to choose a block set in the cache.
    (no index field when fully associative).
    A tag field to search and match addresses in the selected set.
  A block offset to select the data from the block.
Block Address
Block
Offset
Tag
Index

## Slide 36: Address Field Sizes
Block Address
Block
Offset
Tag
Index
  Block offset size = log2(block size)
Index size = log2(Total number of blocks/associativity)
Tag size = address size - index size - offset size
Physical Address Generated by CPU
Mapping function:
Cache set or block frame number = Index =
= (Block Address) MOD (Number of Sets)
Number of Sets

## Slide 37: Locating A Data Block in Cache
Increasing associativity shrinks index, expands tag
  Block index not needed for fully associative cache
Block
Offset, m bits
Block Address
Tag – r bits
Index – k bits
2k addressable blocks in the cache
2m bytes in a block
Tag to identify a unique block

## Slide 38: 4KB Direct Mapped Cache Example
A
d
d
r
e
s
s
(
s
h
o
w
i
n
g
b
i
t
p
o
s
i
t
i
o
n
s
)
2
0
1
0
B
y
t
e
o
f
f
s
e
t
V
a
l
i
d
T
a
g
D
a
t
a
I
n
d
e
x
0
1
2
1
0
2
1
1
0
2
2
1
0
2
3
T
a
g
I
n
d
e
x
H
i
t
D
a
t
a
2
0
3
2
3
1
3
0
1
3
1
2
1
1
2
1
0
1K = 1024 Blocks
Each block = one 32b word
Cache for a
232 bytes = 4 GB
memory space
Mapping function:
Cache Block frame number =
(Block address) MOD (1024)
Index field
Tag field
Block offset
= 2 bits
Block Address = 30 bits
Tag = 20 bits
Index = 10 bits

## Slide 39: 64KB Direct Mapped Cache Example
A
d
d
r
e
s
s
(
s
h
o
w
i
n
g
b
i
t
p
o
s
i
t
i
o
n
s
)
1
6
1
2
B
y
t
e
o
f
f
s
e
t
V
T
a
g
D
a
t
a
H
i
t
D
a
t
a
1
6
3
2
4
K
e
n
t
r
i
e
s
1
6
b
i
t
s
1
2
8
b
i
t
s
M
u
x
3
2
3
2
3
2
2
3
2
B
l
o
c
k
o
f
f
s
e
t
I
n
d
e
x
T
a
g
3
1
1
6
1
5
4
3
2
1
0
4K= 4096 blocks
Each block = four words = 16 bytes
Can cache up to
232 bytes = 4 GB
of memory
Mapping Function: Cache Block frame number = (Block address) MOD (4096)
Larger blocks take better advantage of spatial locality
Index field
Tag field
Word select
Block Address = 28 bits
Tag = 16 bits
Index = 12 bits
Block offset
= 4 bits

## Slide 40: Cache Organization: Set Associativity
T
a
g
D
a
t
a
T
a
g
D
a
t
a
T
a
g
D
a
t
a
T
a
g
D
a
t
a
T
a
g
D
a
t
a
T
a
g
D
a
t
a
T
a
g
D
a
t
a
T
a
g
D
a
t
a
E
i
g
h
t
-
w
a
y
s
e
t
a
s
s
o
c
i
a
t
i
v
e
(
f
u
l
l
y
a
s
s
o
c
i
a
t
i
v
e
)
T
a
g
D
a
t
a
T
a
g
D
a
t
a
T
a
g
D
a
t
a
T
a
g
D
a
t
a
F
o
u
r
-
w
a
y
s
e
t
a
s
s
o
c
i
a
t
i
v
e
S
e
t
0
1
T
a
g
D
a
t
a
O
n
e
-
w
a
y
s
e
t
a
s
s
o
c
i
a
t
i
v
e
(
d
i
r
e
c
t
m
a
p
p
e
d
)
B
l
o
c
k
0
7
1
2
3
4
5
6
T
a
g
D
a
t
a
T
w
o
-
w
a
y
s
e
t
a
s
s
o
c
i
a
t
i
v
e
S
e
t
0
1
2
3
T
a
g
D
a
t
a

## Slide 41: Direct-Mapped Cache Design
41
CACHE SRAM
ADDR
DATA[31:0]
0x00001C0
0xff083c2d
0
1
0x0000000
0x00000021
1
0x0000000
0x00000103
0
0
1
0
0x23F0210
0x00000009
1
Tag
V
Data
=
0
3
0x0000000
DATA[58:32]
DATA[59]
DATA
HIT
ADDRESS
=1
Tag (27-bit)
Cache
Index (3-bit)
Byte Offset (2-bit)
32-bit architecture, 32-bit blocks, 8 blocks
Block Address
Block
Offset
Tag
Index

## Slide 42: 4KB Four-Way Set Associative Cache: MIPS Implementation Example
42
A
d
d
r
e
s
s
2
2
8
V
T
a
g
I
n
d
e
x
0
1
2
2
5
3
2
5
4
2
5
5
D
a
t
a
V
T
a
g
D
a
t
a
V
T
a
g
D
a
t
a
V
T
a
g
D
a
t
a
3
2
2
2
4
-
t
o
-
1
m
u
l
t
i
p
l
e
x
o
r
H
i
t
D
a
t
a
1
2
3
8
9
1
0
1
1
1
2
3
0
3
1
0
Index
Field
Tag
Field
1024 block frames
1 block = one 32b word
4-way set associative
256 sets
Cache for a
232 bytes = 4 GB
memory space
Block Address = 30 bits
Tag = 22 bits
Index = 8 bits
Block offset
= 2 bits
Mapping Function: Cache Set Number = (Block address) MOD (256)

## Slide 43: Fully Associative Cache Design
43
tag 11110111
data 1111000011110000101011
=
Key idea: set size of one block
  1 comparator required for each block
  No address decoding
  Practical only for small caches due to hardware demands
tag 00011100
data 0000111100001111111101
=
=
=
=
=
tag 11111110
tag 00000011
tag 11100110
tag 11110111
data 1111000011110000101011
data 0000000000001111111100
data 1110111100001110000001
data 1111111111111111111111
tag in 11110111
data out 1111000011110000101011

## Slide 44: Fully Associative
44
Fully Associative Cache with N block frames
  0 bit for cache index
  Compare the tags of all cache entries in parallel
  Example: Block Size = 32 B blocks, we need N 27-bit comparators
:
Cache Data
Byte 0
0
4
31
:
Cache Tag (27 bits long)
Valid Bit
:
Byte 1
Byte 31
:
Byte 32
Byte 33
Byte 63
:
Cache Tag
Byte Select
Ex: 0x01
X
X
X
X
X
:
Notes: 44

## Slide 45: Unified vs. Separate Level 1 Cache
45
Unified Level 1 Cache
A single level 1 cache is used for both instructions and data.
Separate instruction/data Level 1 caches (Harvard Memory Architecture):
The level 1 (L1) cache is split into two caches, one for instructions (instruction cache, L1 I-cache) and the other for data (data cache, L1 D-cache).
Control
Datapath
Processor
Registers
Unified
Level
One
Cache
L1
Control
Datapath
Processor
Registers
L1
I-cache
L1
D-cache
Unified Level 1 Cache
Separate Level 1 Caches
(Harvard Memory Architecture)

## Slide 46: Why have separate caches?
Bandwidth: lets us access instructions and data in parallel (less structural hazards)
Most programs don’t modify their instructions
  I-Cache can be simpler than D-Cache, since instruction references are never writes
Instruction stream has high locality of reference, can get higher hit rates with small cache
  Data references never interfere with instruction references

## Slide 47: Cache Replacement Policy
When a cache miss occurs the cache controller may have to select a block of cache data to be removed from a cache block frame and replaced with the requested data, such a block is usually selected by one of two methods (for direct mapped cache, there is only one choice):
  Random:
    Any block is randomly selected for replacement providing uniform allocation.
    Simple to build in hardware.
    The most widely used cache replacement strategy.
  Least-recently used (LRU):
    Accesses to blocks are recorded and the block replaced is the one that was not used for the longest period of time.
    LRU is expensive to implement, as the number of blocks to be tracked increases, and is usually approximated.

## Slide 48: LRU Policy
48
A
B
C
D
MRU
LRU
LRU+1
MRU-1
Access C
C
A
B
D
Access D
D
C
A
B
Access E
E
D
C
A
Access C
C
E
D
A
Access G
G
C
E
D
MISS, replacement
needed
MISS, replacement
needed
Notes: 48

## Slide 49: Cache and Memory Performance Average Memory Access Time (AMAT), Memory Stall cycles
The Average Memory Access Time (AMAT): The average number of cycles required to complete a memory access request by the CPU.
Memory stall cycles per memory access: The number of stall cycles added to CPU execution cycles for one memory access.
For an ideal memory: AMAT = 1 cycle, this results in zero memory stall cycles.
Memory stall cycles per memory access = AMAT -1
Memory stall cycles per instruction =
Memory stall cycles per memory access
x Number of memory accesses per instruction
= (AMAT -1 ) x ( 1 + fraction of loads/stores)
Instruction Fetch

## Slide 50: Cache Performance Unified Memory Architecture
For a CPU with a single level (L1) of cache for both instructions and data and no stalls for cache hits:
Total CPU time = (CPU execution clock cycles +
Memory stall clock cycles) x clock cycle time
Memory stall clock cycles =
(Reads x Read miss rate x Read miss penalty) +
(Writes x Write miss rate x Write miss penalty)
If write and read miss penalties are the same:
Memory stall clock cycles = Memory accesses x Miss rate x Miss penalty
With ideal memory

## Slide 51: Cache Performance Unified Memory Architecture
CPUtime = Instruction count x CPI x Clock cycle time
CPIexecution = CPI with ideal memory
CPI = CPIexecution + MEM Stall cycles per instruction
CPUtime = Instruction Count x (CPIexecution +
MEM Stall cycles per instruction) x Clock cycle time
MEM Stall cycles per instruction =
MEM accesses per instruction x Miss rate x Miss penalty
CPUtime = IC x (CPIexecution + MEM accesses per instruction x
Miss rate x Miss penalty) x Clock cycle time
Misses per instruction = Memory accesses per instruction x Miss rate
CPUtime = IC x (CPIexecution + Misses per instruction x Miss penalty) x
Clock cycle time

## Slide 52: Memory Access Tree For Unified Level 1 Cache
CPU Memory Access
L1 Miss:
% = (1- Hit rate) = (1-H1)
Access time = M + 1
Stall cycles per access = M x (1-H1)
L1 Hit:
% = Hit Rate = H1
Access Time = 1
Stalls= H1 x 0 = 0
( No Stall)
L1
AMAT = H1 x 1 + (1 -H1 ) x (M+ 1) = 1 + M x ( 1 -H1)
Stall Cycles Per Access = AMAT - 1 = M x (1 -H1)
M = Miss Penalty
H1 = Level 1 Hit Rate
1- H1 = Level 1 Miss Rate

## Slide 53: Cache Impact On Performance: An Example
Assuming the following execution and cache parameters:
  Cache miss penalty = 50 cycles
  Normal instruction execution CPI ignoring memory stalls = 2.0 cycles
  Miss rate = 2%
  Average memory references/instruction = 1.33
CPU time = IC x [CPI execution + Memory accesses/instruction x Miss rate x
Miss penalty ] x Clock cycle time
CPUtime with cache = IC x (2.0 + (1.33 x 2% x 50)) x clock cycle time
= IC x 3.33 x Clock cycle time
Lower CPI execution increases the impact of cache miss clock cycles

## Slide 54: Cache Performance Harvard Memory Architecture
For a CPU with separate or split level one (L1) caches for
instructions and data (Harvard memory architecture) and no
stalls for cache hits:
CPUtime = Instruction count x CPI x Clock cycle time
CPI = CPIexecution + Mem Stall cycles per instruction
CPUtime = Instruction Count x (CPIexecution +
Mem Stall cycles per instruction) x Clock cycle time
Mem Stall cycles per instruction = Instruction Fetch Miss rate x Miss Penalty + Data Memory Accesses Per Instruction x Data Miss Rate x Miss Penalty

## Slide 55: Memory Access Tree For Separate Level 1 Caches
CPU Memory Access
L1
Instruction
Data
Data L1 Miss:
Access Time : M + 1
Stalls per access:
% data x (1 - Data H1 ) x M
Data L1 Hit:
Access Time: 1
Stalls = 0
Instruction L1 Hit:
Access Time = 1
Stalls = 0
Instruction L1 Miss:
Access Time = M + 1
Stalls Per access:
%instructions x (1 - Instruction H1 ) x M
Stall Cycles Per Access = % Instructions x ( 1 - Instruction H1 ) x M + % data x (1 - Data H1 ) x M
AMAT = 1 + Stall Cycles per access

## Slide 56: Cache Write Strategies

## Slide 57: Cache Read/Write Operations
57
Statistical data suggest that reads (including instruction fetches) dominate processor cache accesses (writes account for 25% of data cache traffic).
In cache reads, a block is read at the same time while the tag is being compared with the block address (searching). If the read is a hit the data is passed to the CPU, if a miss it ignores it.
In cache writes, modifying the block cannot begin until the tag is checked to see if the address is a hit.
Thus for cache writes, tag checking cannot take place in parallel, and only the specific data requested by the CPU can be modified.
Cache is classified according to the write and memory update strategy in place: write through, or write back.

## Slide 58: Cache Write Strategies
58
Write Though: Data is written to both the cache block and the main memory.
  The lower level always has fresh data; an important feature for I/O and multiprocessing.
  Easier to implement than write back.
  A write buffer is often used to reduce CPU write stall while data is written to memory.
Processor
Cache
Write Buffer
DRAM

## Slide 59: Write Buffer for Write Through
59
A Write Buffer is needed between the Cache and Memory
  Processor: writes data into the cache and the write buffer
  Memory controller: write contents of the buffer to memory
Write buffer is just a FIFO queue:
  Typical number of entries: 4
  Works fine if: Store frequency (w.r.t. time) << 1 / DRAM write cycle
Processor
Cache
Write Buffer
DRAM
Notes: 59

## Slide 60: Cache Write Strategies
60
Write back: Data is written or updated only to the cache block.
  Writes occur at the speed of cache
  The modified or dirty cache block is written to main memory later (e.g., when it’s being replaced from cache)
  A status bit called a dirty bit, is used to indicate whether the block was modified while in cache; if not the block is not written to main memory.
  Uses less memory bandwidth than write through.

## Slide 61: Write misses
61
If we try to write to an address that is not already contained in the cache; this is called a write miss.
Let’s say we want to store 21763 into Mem[1101 0110] but we find that address is not currently in the cache.
When we update Mem[1101 0110], should we also load it into the cache?
Index
Tag
Data
V
Address
...
110
...
1
00010
123456
Data
6378
...
1101 0110
...

## Slide 62: No write-allocate
62
With a no-write allocate policy, the write operation goes directly to main memory without affecting the cache.
This is good when data is written but not immediately used again, in which case there’s no point to load it into the cache yet.
Index
Tag
Data
V
...
110
...
1
00010
123456
Address
Data
21763
...
1101 0110
...
Mem[1101 0110] = 21763

## Slide 63: Write Allocate
63
A write allocate strategy would instead load the newly written data into the cache.
If that data is needed again soon, it will be available in the cache.
Index
Tag
Data
V
Address
...
110
...
1
11010
21763
Data
21763
...
1101 0110
...
Mem[214] = 21763

## Slide 64: Memory Access Tree, Unified L1 Write Through, No Write Allocate, No Write Buffer
64
CPU Memory Access
L1
Read
Write
L1 Write Miss:
Access Time : M + 1
Stalls per access:
% write x (1 - H1 ) x M
L1 Write Hit:
Access Time: M +1
Stalls Per access:
% write x (H1 ) x M
L1 Read Hit:
Access Time = 1
Stalls = 0
L1 Read Miss:
Access Time = M + 1
Stalls Per access
% reads x (1 - H1 ) x M
Stall Cycles Per Memory Access = % reads × (1 - H1 ) × M + % write × M
AMAT = 1 + % reads × (1 - H1 )× M + % write × M

## Slide 65: Memory Access Tree Unified L1 Write Back, With Write Allocate
65
CPU Memory Access
L1
Read
Write
L1 Write Miss
L1 Write Hit:
% write x H1
Access Time = 1
Stalls = 0
L1 Hit:
% read x H1
Access Time = 1
Stalls = 0
L1 Read Miss
Stall Cycles Per Memory Access = (1-H1) × ( M × % clean + 2M × % dirty )
AMAT = 1 + Stall Cycles Per Memory Access
Clean
Access Time = M +1
Stall cycles = M x (1-H1 ) x
% reads x % clean
Dirty
Access Time = 2M +1
Stall cycles = 2M x (1-H1) x
%read x % dirty
Clean
Access Time = M +1
Stall cycles = M x (1 -H1) x
% write x % clean
Dirty
Access Time = 2M +1
Stall cycles = 2M x (1-H1) x
%write x % dirty

## Slide 66: 2 Levels of Cache: L1, L2
66
CPU
L2 Cache
Main Memory
Hit Rate= H1, Hit time = 1 cycle
(No Stall)
Hit Rate= H2, Hit time = T2 cycles
Memory access penalty, M
L1 Cache

## Slide 67: Miss Rates For Multi-Level Caches
67
Local Miss Rate: This rate is the number of misses in a cache level divided by the number of memory accesses to this level. Local Hit Rate = 1 - Local Miss Rate
Global Miss Rate: The number of misses in a cache level divided by the total number of memory accesses generated by the CPU.
Since level 1 receives all CPU memory accesses, for level 1:
  Local Miss Rate = Global Miss Rate = 1 - H1
For level 2 since it only receives those accesses missed in level 1:
  Local Miss Rate = Miss rateL2= 1- H2
  Global Miss Rate = Miss rateL1 x Miss rateL2
  = (1- H1) x (1 - H2)

## Slide 68: 2-Level Cache Performance Memory Access Tree
68
CPU Memory Access
L1 Miss:
% = (1-H1)
L1 Hit:
Stalls= H1 x 0 = 0
(No Stall)
L2 Miss:
Stalls= (1-H1)(1-H2) x M
L2 Hit:
(1-H1) x H2 x T2
Stall cycles per memory access = (1-H1) × H2 x T2 + (1-H1)(1-H2) × M
AMAT = 1 + (1-H1) × H2 × T2 + (1-H1)(1-H2) × M
L1
L2
T2: L2 cache hit time in cycles

## Slide 69: 2-Level Cache Performance
69
CPUtime = IC x (CPIexecution + Mem Stall cycles per instruction) x C
Mem Stall cycles per instruction = Mem accesses per instruction x Stall cycles per access
For a system with 2 levels of cache, assuming no penalty when found in L1 cache:
Stall cycles per memory access =
[miss rate L1] x [ Hit rate L2 x Hit time L2
+ Miss rate L2 x Memory access penalty) ] =
(1-H1) x H2 x T2 + (1-H1)(1-H2) x M
L1 Miss, L2 Hit
L1 Miss, L2 Miss:
Must Access Main Memory

## Slide 70: 3 Levels of Cache
70
CPU
L2 Cache
L3 Cache
Main Memory
L1 Cache
Hit Rate= H1, Hit time = 1 cycle
Hit Rate= H2, Hit time = T2 cycles
Hit Rate= H3, Hit time = T3
Memory access penalty, M

## Slide 71: 3-Level Cache Performance Memory Access Tree CPU Stall Cycles Per Memory Access
71
CPU Memory Access
L1 Miss:
% = (1-H1)
L1 Hit:
Stalls= H1 x 0 = 0
( No Stall)
L2 Miss:
% = (1-H1)(1-H2)
L2 Hit:
(1-H1) x H2 x T2
Stall cycles per memory access = (1-H1) x H2 x T2 + (1-H1) x (1-H2) x H3 x T3 + (1-H1)(1-H2) (1-H3)x M
AMAT = 1 + Stall cycles per memory access
L3 Miss:
(1-H1)(1-H2)(1-H3) x M
L3 Hit:
(1-H1) x (1-H2) x H3 x T3
L1
L3
L2

## Slide 72: 3-Level Cache Performance
72
CPUtime = IC x (CPIexecution + Mem Stall cycles per instruction) x C
Mem Stall cycles per instruction = Mem accesses per instruction x Stall cycles per access
For a system with 3 levels of cache, assuming no penalty when data found in L1 cache:
Stall cycles per memory access =
[miss rate L1] x [ Hit rate L2 x Hit time L2
+ Miss rate L2 x (Hit rate L3 x Hit time L3
+ Miss rate L3 x Memory access penalty) ] =
(1-H1) x H2 x T2 + (1-H1) x (1-H2) x H3 x T3
+ (1-H1)(1-H2) (1-H3)x M
L1 Miss, L2 Hit
L2 Miss, L3 Hit
L1 Miss, L2 Miss:
Must Access Main Memory

## Slide 73: Reduce Miss Rate
73
Notes: 73

## Slide 74: Reducing Misses (3 Cs)
74
Classifying Misses: 3 Cs
  Compulsory—The first access to a block is not in the cache, so the block must be brought into the cache. These are also called cold start misses or first reference misses. (Misses even in infinite size cache)
  Capacity—If the cache cannot contain all the blocks needed during the execution of a program, capacity misses will occur due to blocks being discarded and later retrieved. (Misses due to size of cache)
  Conflict—If the block-placement strategy is not fully associative, conflict misses (in addition to compulsory and capacity misses) will occur because a block can be discarded and later retrieved if too many blocks map to its set. These are also called collision misses or interference misses. (Misses due to associativity and size of cache)
Notes: 74

## Slide 75: 3Cs Absolute Miss Rates
75
2:1 cache rule
2:1 cache rule: The miss rate of a direct mapped cache of size N is about the same as a 2-way set associative cache of size N/2.
Cache Size (KB)
Miss Rate per Type
0
0.02
0.04
0.06
0.08
0.1
0.12
0.14
1
2
4
8
16
32
64
128
Conflict
1-way
2-way
4-way
8-way
Capacity
Compulsory

## Slide 76: How to Reduce the 3 Cs Cache Misses?
76
Increase Block Size
Increase Associativity
Use a Victim Cache
Use a Pseudo Associative Cache
Hardware Prefetching
Notes: 76

## Slide 77: Pros and cons – Re-visit cache design choices
77
Larger cache block size
Pros
  Reduces miss rate
Cons
  Increases miss penalty
Important factors deciding cache performance: hit time, miss rate, miss penalty

## Slide 78: Pros and cons – Re-visit cache design choices
78
Bigger cache
Pros
  Reduces miss rate
Cons
  May increases hit time
  My increase cost and power consumption

## Slide 79: Pros and cons – Re-visit cache design choices
79
Higher associativity
Pros
  Reduces miss rate
Cons
  Increases hit time

## Slide 80: Pros and cons – Re-visit cache design choices
80
Multiple levels of caches
Pros
  Reduces miss penalty
Cons
  Increases cost and power consumption

## Slide 81: Multilevel Cache Design Considerations
Design considerations for L1 and L2 caches are very different
  Primary cache should focus on minimizing hit time in support of a shorter clock cycle
    Smaller cache with smaller block sizes
  Secondary cache (s) should focus on reducing miss rate to reduce the penalty of long main memory access times
    Larger cache with larger block sizes and/or higher associativity

## Slide 82: Reducing Miss rate with programming
j=0
i=0
j=0
i=0
Examples:
  cold cache, 4-byte words, 4-word cache blocks
int sumarrayrows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}
int sumarraycols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}
Miss rate =
～1/N
～ 100%
Miss rate =

## Slide 83: Reducing Miss Penalty
83
Notes: 83

## Slide 84: The cost of a cache miss
For a memory access, assume:
  1 clock cycle to send address to memory
  25 clock cycles for each DRAM access (clock cycle 2ns, 50 ns access time)
  1 clock cycle to send each resulting data word
This actually depends on the bus speed
Miss access time (4-word block)
  4 x (Address + access + sending data word)
  4 x (1 + 25 + 1) = 108 = 108 cycles for each miss
Notes: 84

## Slide 85: Memory Interleaving
85
Interleaving
Default
Begin accessing one word, and while waiting, start accessing other three words (pipelining)
CPU
Cache
Memory
4 bytes
Bus
Bus
CPU
Cache
Memory2
4 bytes
Memory1
Memory3
Memory0
Bus
Bus
Bus
Bus
Bus
Requires 4 separate memories, each 1/4 size
Must finish accessing one word before starting the next access
(1+25+1)x4 = 108 cycles
1
25
1
30 cycles
1
25
1
1
25
1
1
25
1
Spread out addresses among the memories
Interleaving works perfectly with caches
Sophisticated DRAMs provide support for this
Notes: 85

## Slide 86: Cache Optimization
Six basic cache optimizations:
  Larger block size
    Reduces compulsory misses
    Increases capacity and conflict misses, increases miss penalty
  Larger total cache capacity to reduce miss rate
    Increases hit time, increases power consumption
  Higher associativity
    Reduces conflict misses
    Increases hit time, increases power consumption
  Higher number of cache levels
    Reduces overall memory access time
  Giving priority to read misses over writes
    Reduces miss penalty
  Avoiding address translation in cache indexing
    Reduces hit time

## Slide 87: Ten Advanced Optimizations
1. Small and simple first level caches
  Critical timing path:
    addressing tag memory, then
    comparing tags, then
    selecting correct set
  Direct-mapped caches can overlap tag compare and transmission of data
  Lower associativity reduces power because fewer cache lines are accessed

## Slide 88: L1 Size and Associativity
Access time vs. size and associativity

## Slide 89: Way Prediction
2. To improve hit time, predict the way to pre-set mux
  Mis-prediction gives longer hit time
  Prediction accuracy
    > 90% for two-way
    > 80% for four-way
    I-cache has better accuracy than D-cache
  First used on MIPS R10000 in mid-90s
  Used on ARM Cortex-A8
Extend to predict block as well
  “Way selection”
  Increases mis-prediction penalty

## Slide 90: Pipelining Cache
3. Pipeline cache access to improve bandwidth
  Examples:
    Pentium: 1 cycle
    Pentium Pro – Pentium III: 2 cycles
    Pentium 4 – Core i7: 4 cycles
  Increases branch mis-prediction penalty
  Makes it easier to increase associativity

## Slide 91: Nonblocking Caches
4. Allow hits before previous misses complete
  “Hit under miss”
  “Hit under multiple miss”
  In general, processors can hide L1 miss penalty but not L2 miss penalty

## Slide 92: Multibanked Caches
5. Organize cache as independent banks to support simultaneous access
  ARM Cortex-A8 supports 1-4 banks for L2
  Intel i7 supports 4 banks for L1 and 8 banks for L2
  Interleave banks according to block address

## Slide 93: Critical Word First, Early Restart
6. Critical word first
  Request missed word from memory first
  Send it to the processor as soon as it arrives
Early restart
  Request words in normal order
  Send missed word to the processor as soon as it arrives
  Effectiveness of these strategies depends on block size and likelihood of another access to the portion of the block that has not yet been fetched

## Slide 94: Merging Write Buffer
7. When storing to a block that is already pending in the write buffer, update write buffer (write merging)
  Reduces stalls due to full write buffer
  Do not apply to I/O addresses
No write merging
Write merging

## Slide 95: Compiler Optimizations
8. Loop Interchange
  Swap nested loops to access memory in sequential order
  Blocking
    Instead of accessing entire rows or columns, subdivide matrices into blocks
    Improves locality if a block can fit in the cache

## Slide 96: Hardware Prefetching
9. Fetch two blocks on miss (include next sequential block)
Pentium 4 Pre-fetching

## Slide 97: Compiler Prefetching
10. Insert prefetch instructions before data is needed
  Non-faulting: prefetch doesn’t cause exceptions
  Register prefetch
    Loads data into register
  Cache prefetch
    Loads data into cache
  Combine with loop unrolling and software pipelining

## Slide 98: Summary

## Slide 99: Virtual Memory
Originally invented to support program sizes larger than then-available physical memory
  later on it finds applications in multi-programming and virtual machines
Virtual memory is as large as the address space allowed by the ISA…but
  only a portion of the address space resides in physical memory at any given time
  the rest is kept on disks and brought into physical memory as needed

## Slide 100: Virtual Memory
Address translation
Program “sees” entire VM address space
Program is run in physical memory which is typically smaller than the address space
Pages of address space are swapped in/out of disk storage as needed
Strictly speaking VM is required to overcome limitation on the size of physical memory
  but VM is extended in a natural way to support multiprogramming & memory protection
  There are machines where the physical memory space is larger than the virtual memory space (e.g., PDP-11)
Disk
Physical memory
Virtual memory
Address
translation

## Slide 101: Advantages of Virtual Memory
Abstraction of large and flat memory
  program has a consistent view of a contiguous memory, even though physical memory is scrambled
  Allows multiprogramming
  relocation: allows the same program to run in any location in physical memory
Protection
  different processes are protected from each other
  different pages can have different behavior (read-only; user/supervisor)
    kernel code/data protected from user programs
Sharing
  can map same physical memory to multiple processes (shared memory)

## Slide 102: How VM Works
On program startup
  OS loads part of the program into RAM; this includes enough code to start execution
  if program size exceeds allocated RAM space the remainder is maintained on disk
During execution
  if program needs a code/data not resident in RAM, it fetches the segment from disk into RAM
  if there is not enough room in RAM, some resident code/data is evicted from memory to make room
  if evicted contents are “dirty”, they are written to disk

## Slide 103: VA-to-PA Address Translation
Processor
0x00
0x04
0x04
0x00
0x08
0x12
0x12
Disk
Sw R1, 0(R4)
add R1, R2, R4
Sub R8, R2, R1
BNEZ R5, 0x64
0x00
0x04
0x08
0x12
Disk
Virtual
address
VA
PA
Main memory
Programs use virtual addresses (VA) for data & instructions
VA translated to physical addresses (PA)
  Usually organized in pages (paging) or segments
  Paging systems use a “page table” for the translation
Instruction/data fetched/updated in memory
Page table

## Slide 104: Page Table
Virtual page number
Page offset
0
11
12
31
Physical page number
Page offset
0
11
12
23
Page table
Memory organized in pages (similar to blocks in cache)
Page size is usually 4-8 Kbytes
Virtual address
Physical address

## Slide 105: VA to PA Translation
Page offset
Virtual address space
Physical address space
Page frame
Virtual page number
Page offset
0
11
12
63
Page table maps the base address of virtual and physical page frames
Page offset need not be used in VA=>PA translation because virtual and physical block sizes are the same
Page
Table
Page offset

## Slide 106: Multiprogramming View of VM
VA 1
VA 1
VA 1
Program 1
Program 2
Program 3
Page Table 1
1
2
3
Page Table 2
1
2
3
4
Page Table 3
1
2
3
4
Physical Memory
Each application has a separate page table
Page table contains an entry for each page
Page tables are identified by the base pointers maintained by OS for individual processes
Page table
base pointer 3
Page table
base pointer 2
Page table
base pointer 1

## Slide 107: Page Fault
How is it known whether the page is in memory?
  Maintain a valid bit per page table entry
  valid bit is set to INVALID if the page is not in memory
  valid bit is set to VALID if the page is in memory
Page fault occurs when a page is not in memory
  fault results in OS fetching the page from disk into DRAM
  if DRAM is full, OS must evict a page (victim) to make room
  if victim is dirty OS updates the page on disk before fetch
  OS changes page table to reflect turnover
After a page fault and page-fetching, execution resumes at the instruction which caused the fault

## Slide 108: VM => PM Translation
Each program memory reference requires two memory accesses: one for VM => PM mapping and one for actual data/instruction
  must make page table lookup as fast as possible
Page table too big to keep in fast memory (SRAM) in its entirety
  store page table in main memory
  cache a portion of the page table in TLB (Translation Look-Aside Buffer)
Virtual page number
Page offset
0
11
12
31
Physical page number
Page offset
0
11
12
24
Page table
Virtual address
Physical address

## Slide 109: Speeding Up Address Translation: Translation Lookaside Buffer (TLB)
TLB: A small and fast on-chip memory structure used for address translations.
If a virtual address is found in TLB (a TLB hit), the page table in main memory is not accessed.
1
1
1
1
0
1
1
0
1
1
0
1
1
1
1
1
0
1
Physical Memory
Disk Storage
TLB (on-chip)
128-256 Entries
Physical Page
Address
Virtual Page
Number
Page Table
(in main memory)
Physical Page
or Disk Address
Tag
Valid
Valid
128-256
TLB Entries

## Slide 110: Translation Look-Aside Table (TLB)
Processor
TLB
Memory
TLB maintains a list of most-recently used pages
Similar to instruction & data cache
  virtual address is used to index into the TLB
  TLB entry contains physical address
  takes ~ 1 clock cycle
What if VM=>PM lookup and data/instruction lookup takes more than 1 clock cycle?
  To avoid TLB lookup, remember the last VM => PM translation
  if same page is referenced, TLB lookup can be avoided

## Slide 111: TLB and Context Switch
In multi-programming we need to use TLB for the active process
  What to do with TLB at context switch?
Too costly to clear TLB on every context switch
Keep track of PTE in TLB per process using ASID

## Slide 112: TLB Organization
Additional info per page
  Dirty: page modified (if the page is swapped out, should the disk copy be updated?)
  Valid: TLB entry valid
  Used: Recently used or not (for selecting a page for eviction)
  Access: Read/Write
  ASID:Address Space ID
Tag

## Slide 113: Virtual Machines
Supports isolation and security
Sharing a computer among many unrelated users
Enabled by raw speed of processors, making the overhead more acceptable
Allows different ISAs and operating systems to be presented to user programs
  “System Virtual Machines”
  SVM software is called “virtual machine monitor” or “hypervisor”
  Individual virtual machines run under the monitor are called “guest VMs” or “guest OSes”

## Slide 114: I/O Performance Measures
I/O bandwidth (throughput) – amount of information that can be input (output) and communicated across an interconnect (e.g., a bus) to the processor/memory (I/O device) per unit time
  How much data can we move through the system in a certain time?
  How many I/O operations can we do per unit time?
I/O response time (latency) – the total elapsed time to accomplish an input or output operation
  An especially important performance metric in real-time systems
Many applications require both high throughput and short response times

## Slide 115: Hard Disk Performance
Platter
Arm
Actuator
Head
Sector
Inner
Track
Outer
Track
Disk Latency = Seek Time + Rotation Time + Transfer Time + Controller Overhead
Seek Time depends on the moving distance and moving speed of arms
Rotation Time depends on how fast the disk rotates and how far sector is from head
Transfer Time depends on data rate (bandwidth) of disk and size of request
Controller
Spindle

## Slide 116: Disk Access Time
+ Rotational delay
+ Transfer time
Seek time
Disk access time =
+ Other delays
Disk platter
Disk arm
Disk head
block x
in memory
I want
block X

## Slide 117: Communication of I/O Devices and Processor
How does the processor command the I/O devices?
  Special I/O instructions
    Must specify both the device (port number) and the command
  For example:
  inp reg, port ; registerport
  out port, reg ; portregister
Physical
address space
each device gets
one or more
addresses
I/O address space

## Slide 118: Communication of I/O Devices and Processor
How does the processor command the I/O devices?
  Memory-mapped I/O
    Portions of the memory address space are assigned to I/O devices
    Read and writes to those memory addresses are interpreted as commands to the I/O devices
    Load/stores to the I/O address space can only be done by the OS
each device gets
one or more
addresses
Physical address space

## Slide 119: Communication of I/O Devices and Processor
How does the I/O device communicate with the processor?
  Polling – the processor periodically checks the status of an I/O device to determine its need for service
    Processor is totally in control – it also does all the work
    Can waste a lot of processor time due to speed differences
  Interrupt-driven I/O – the I/O device issues an interrupt to the processor to indicate that it needs attention

## Slide 120: Direct-Memory Access (DMA)
Interrupt-driven IO relieves the CPU from waiting for every IO event
But the CPU can still be bogged down if it is used in transferring IO data.
  Typically blocks of bytes.
For high-bandwidth devices (like disks) interrupt-driven I/O would consume a lot of processor cycles

## Slide 121: DMA
DMA – the I/O controller has the ability to transfer data directly to/from the memory without involving the processor

## Slide 122: RAID
To increase the availability and the performance (bandwidth) of a storage system, instead of a single disk, a set of disks (disk arrays) can be used.
Similar to memory interleaving, data can be spread among multiple disks (striping), allowing simultaneous access to the data, improving the throughput and latency besides availability.
However, the reliability of the system drops (n devices have 1/n the reliability of a single device).

## Slide 123: Dependability Measures
Reliability: mean time to failure (MTTF)
Service interruption: mean time to repair (MTTR)
Mean time between failures
  MTBF = MTTF + MTTR
Availability = MTTF / (MTTF + MTTR)
Improving Availability
  Increase MTTF: fault avoidance, fault tolerance, fault forecasting
  Reduce MTTR: improved tools and processes for diagnosis and repair

## Slide 124: Array Reliability
Reliability of N disks = Reliability of 1 Disk ÷N
  50,000 Hours ÷ 70 disks = 700 hours
Disk system Mean Time To Failure (MTTF): Drops from 6 years to 1 month!
Disks without redundancy are too unreliable to be useful!

## Slide 125: RAID
A disk array’s availability can be improved by adding redundant disks:
  If a single disk in the array fails, the lost information can be reconstructed from redundant information.
This leads to a technology known as RAID - Redundant Array of Inexpensive Disks.
  Depending on the number of redundant disks and the redundancy scheme used, RAIDs are classified into levels.
  At least 6 levels of RAID (0-5) are accepted by the industry.
  Level 2 is not commercially available

## Slide 126: RAID-0
stripe 12
stripe 8
stripe 4
stripe 0
stripe 13
stripe 9
stripe 5
stripe 1
stripe 14
stripe 10
stripe 6
stripe 2
stripe 15
stripe 11
stripe 7
stripe 3
Striped, non-redundant
  Parallel access to multiple disks
  Excellent data transfer rate
  Excellent I/O request processing rate (for large stripes) if the controller supports independent Reads/Writes
  Not fault tolerant (AID)
Typically used for applications requiring high performance for non-critical data (e.g., video streaming and editing)

## Slide 127: RAID-1 - Mirroring
Called mirroring or shadowing, uses an extra disk (mirror) for each disk in the array
  costly form of redundancy (but some FS, e.g., GFS, makes 3 copies)
Whenever data is written to one disk, the data is also written to the mirror: good for reads (lower latency), fair for writes
If a disk fails, the system goes to the mirror and gets the desired data.
Fast, but very expensive.
Typically used in system drives and critical files
  Banking, insurance data
  e-commerce servers
stripe 3
stripe 2
stripe 1
stripe 0
stripe 3
stripe 2
stripe 1
stripe 0

## Slide 128: RAID-4 - Block-interleaved Parity
In RAID 3, every read or write needs to go to all disks since bits are interleaved among the disks.
Performance of RAID 3:
  Only one request can be serviced at a time
  Poor I/O request rate
  Excellent data transfer rate
  Typically used in large I/O request size applications, such as imaging or CAD
RAID 4: If we distribute the information block-interleaved, where a disk sector is a block, then for normal reads different reads can access different segments in parallel. Only if a disk fails will we need to access all the disks to recover the data.

## Slide 129: RAID-4: Block Interleaved Parity
block 0
block 4
block 8
block 12
block 1
block 5
block 9
block 13
block 2
block 6
block 10
block 14
block 3
block 7
block 11
block 15
P(0-3)
P(4-7)
P(8-11)
P(12-15)
Allow for parallel access by multiple I/O requests
Doing multiple small reads is now faster than before.
A write, however, is a different story since we need to update the parity information for the block.
Large writes (full stripe), update the parity:
P’ = d0’  d1’  d2’  d3’;
Small writes (eg. write on d0), update the parity:
P = d0  d1  d2  d3
P’ = d0’  d1  d2  d3 = d0’  d0  P;
However, writes are still very slow since parity disk is the bottleneck.

## Slide 130: RAID-4: Small Writes

## Slide 131: RAID-5 - Block-interleaved Distributed Parity
RAID 5 distributes the parity blocks among all the disks.
0
4
8
12
20
. . .
1
5
9
16
21
. . .
2
6
13
17
22
. . .
3
10
14
18
23
. . .
7
11
15
19
. . .
P4
P3
P2
P1
P0
P5
RAID 5
Why is this helpful?

## Slide 132: RAID-5 - Block-interleaved Distributed Parity
This allows some writes to proceed in parallel
  For example, writes to blocks 8 and 5 can occur simultaneously.

## Slide 133: RAID-5 - Block-interleaved Distributed Parity
However, writes to blocks 8 and 11 cannot proceed in parallel.

## Slide 134: Performance of RAID-5 - Block-interleaved Distributed Parity
Performance of RAID-5
  I/O request rate: excellent for reads, good for writes
  Data transfer rate: good for reads, good for writes
  Typically used for high request rate, read-intensive data lookup
  File and Application servers, Database servers, WWW, E-mail, and News servers, Intranet servers
Widely used.

## Slide 135: RAID-6 – Row-Diagonal Parity
To handle 2 disk errors
  In practice, another disk error can occur before the first problem disk is repaired
Use p-1 data disks, 1 row-parity disk, 1 diagonal-parity disk
If any two of the p+1 disks fail, data can still be recovered
Data Disk 0 | Data Disk 1 | Dada Disk 2 | Dada Disk 3 | Row Parity Disk | Diagonal Parity Disk
0 | 1 | 2 | 3 | 4 | 0
1 | 2 | 3 | 4 | 0 | 1
2 | 3 | 4 | 0 | 1 | 2
3 | 4 | 0 | 1 | 2 | 3

## Slide 136: Dependability
Notes: 136

## Slide 137: Definitions
Examples on why precise definitions so important for reliability
Is a programming mistake a fault, error, or failure?
  Are we talking about the time it was designed or the time the program is run?
  If the running program doesn’t exercise the mistake, is it still a fault/error/failure?
If an alpha particle hits a DRAM memory cell, is it a fault/error/failure if it doesn’t change the value?
  Is it a fault/error/failure if the memory doesn’t access the changed bit?
  Did a fault/error/failure still occur if the memory had error correction and delivered the corrected value to the CPU?

## Slide 138: IFIP Standard terminology
Computer system dependability: quality of delivered service such that reliance can be justifiably placed on the service
Service is observed actual behavior as perceived by other system(s) interacting with this system’s users
Each module has ideal specified behavior, where service specification is agreed description of expected behavior
A system failure occurs when the actual behavior deviates from the specified behavior
failure occurred because an error, a defect in module
The cause of an error is a fault
When a fault occurs it creates a latent error, which becomes effective when it is activated
When error actually affects the delivered service, a failure occurs (time from error to failure is error latency)

## Slide 139: Why multi-core ?
Difficult to make single-core clock frequencies even higher
Deeply pipelined circuits:
  Heat problems
  Clock problems
  Efficiency (Stall) problems
Doubling issue rates above today’s 3-6 instructions per clock, say to 6 to 12 instructions, is extremely difficult
  issue 3 or 4 data memory accesses per cycle,
  rename and access more than 20 registers per cycle, and
  fetch 12 to 24 instructions per cycle.
Many new applications are multithreaded
A general trend in computer architecture is to shift towards more parallelism through more processors or processor cores
Notes: 139

## Slide 140: Thread-Level Parallelism (TLP)‏
This is parallelism on a more coarse scale
Server can serve each client in a separate thread (Web server, database server)‏
A computer game can do AI, graphics, and sound in three separate threads
Single-core superscalar processors cannot fully exploit TLP
Multi-core architectures are the next step in processor evolution: explicitly exploiting TLP
Notes: 140

## Slide 141: TLP
Thread-Level parallelism
  Have multiple program counters
  Uses MIMD model
  Targeted for tightly-coupled shared-memory multiprocessors
For n processors, need n threads
Amount of computation assigned to each thread = grain size
  Threads can be used for data-level parallelism, but the overheads may outweigh the benefit

## Slide 142: How to exploit TLP?
Execute instructions from multiple threads on a single processor
  Coarse-grain, fine-grain, SMT (Simultaneous Multi-Threading)
Execute multiple threads on multiple processors
  “Anything that can be threaded today will map efficiently to multi-core”
Notes: 142

## Slide 143: SMT – Simultaneous Multi-Threading
A variation on multithreading that uses the resources of a multiple-issue, dynamically scheduled processor (superscalar) to exploit both program ILP and thread-level parallelism (TLP)
With register renaming and dynamic scheduling, multiple instructions from independent threads can be issued in one cycle without regard to dependencies among them
Need separate rename tables (ROBs) for each thread
Need the capability to commit from multiple threads (i.e., from multiple ROBs) in one cycle
Notes: 143

## Slide 144: TLP a 4-issue superscalar processor
Thread A
Thread B
Thread C
Thread D
Time
Issue slots
SMT
Fine MT
Coarse MT
Notes: 144

## Slide 145: Multiprocessing
Multiprocessing (Parallel Processing): Concurrent execution of tasks (programs) using multiple computing, memory and interconnection resources.
  Use multiple resources to solve problems faster
Provides an alternative to faster clock for performance
  Assuming a doubling of effective processor performance every 2 years, 1024-Processor system (assuming linear performance gain) can get you the performance that it would take 20 years for a single-processor system to deliver
Using multiple processors to solve a single problem
  Divide problem into many small pieces
  Distribute these small problems to be solved by multiple processors simultaneously

## Slide 146: Multiprocessing
For the last 30+ years multiprocessing has been seen as the best way to produce orders of magnitude performance gains.
  Double the number of processors, get (theoretically) double performance (less than 2 times the cost).
It turns out that the ability to develop and deliver software for multiprocessing systems induces impediment to wide adoption.

## Slide 147: Performance Potential: Another View
Gustafson view
  Parallel portion increases as the problem size increases
    Serial time fixed (at s)
    Parallel time proportional to problem size (true most of the time)
    Gustafson’s Law: Speedup(N) = N - (N-1)
      N: number of processors,  : weight of non-parallelizable part
Old Serial: SSPPPPPP
6 processors: SSPPPPPP
PPPPPP
PPPPPP
PPPPPP
PPPPPP
PPPPPP
Hypothetical Serial:
SSPPPPPP PPPPPP PPPPPP PPPPPP PPPPPP PPPPPP
  Speedup(6) = (8+5*6)/8 = 4.75
     =? in this calculation?
  Speedup(N) = N(1- ) + ; Speedup'()  !!!!
This means we can achieve higher speedup by processing larger problems.

## Slide 148: A Few Types
Symmetric multiprocessors (SMP)
  Small number of cores
  Share single memory with uniform memory latency
Distributed shared memory (DSM)
  Memory distributed among processors
  Non-uniform memory access/latency (NUMA)
  Processors connected via direct (switched) and non-direct (multi-hop) interconnection networks

## Slide 149: Flynn’s Taxonomy of Computing
SISD (Single Instruction, Single Data):
  Typical uniprocessor systems that we’ve studied throughout this course.
  Uniprocessor systems can time share and still be SISD.
SIMD (Single Instruction, Multiple Data):
  Multiple processors simultaneously executing the same instruction on different data.
  Specialized applications (e.g., image processing).
MIMD (Multiple Instruction, Multiple Data):
  Multiple processors autonomously executing different instructions on different data.
  Keep in mind that the processors are working together to solve a single problem.
  This is a more general form of multiprocessing, and can be used in numerous applications

## Slide 150: SIMD Systems
Processor
Memory
P
M
P
M
P
M
P
M
P
M
P
M
P
M
P
M
P
M
P
M
P
M
P
M
P
M
P
M
P
M
P
M
von Neumann Computer
Some Interconnection Network
One control unit
Lockstep
All Ps do the same or nothing

## Slide 151: MIMD Architecture
151
Unlike SIMD, MIMD computer works asynchronously.
    Shared memory (tightly coupled) MIMD
    Distributed memory (loosely coupled) MIMD
Processor
A
Processor
B
Processor
C
Data Input
stream A
Data Input
stream B
Data Input
stream C
Data Output
stream A
Data Output
stream B
Data Output
stream C
Instruction
Stream A
Instruction
Stream B
Instruction
Stream C

## Slide 152: MIMD Shared Memory Systems
Interconnection Networks
M
M
M
M
P
P
P
P
P
P
C
P
C
P
C
P
C
M
M
M
M
Global Memory
P
C
P
C
P
C
One global memory
Cache Coherence
All Ps have equal access to memory

## Slide 153: Cache Coherent NUMA
Interconnection Network
M
C
P
M
C
P
M
C
P
M
C
P
Each P has part of the shared memory
Non uniform memory access

## Slide 154: MIMD Distributed Memory Systems
Interconnection Networks
M
M
M
M
P
P
P
P
1110 1111
1010 1011
0110 0111
0010 0011
1100 1101
1000 1001
0100 0101
0000 0001
LAN/WAN
No shared memory
Message Passing
Topology

## Slide 155: Cluster Architecture
M
C
P
I/O
OS
M
C
P
I/O
OS
M
C
P
I/O
OS
Middleware
Programming Environment
Interconnection Network
Home cluster

## Slide 156: Grids
Internet
Dependable, consistent, pervasive, and inexpensive access to high end computing.
Geographically distributed platforms.

## Slide 157: SIMD
Notes: 157

## Slide 158
158
SIMD Parallel Computing
It can be a stand-alone multiprocessor
Or
Embedded in a single processor for specific applications (MMX)

## Slide 159: SIMD Multiprocessing
159
Traditional vector computers are typical SIMD systems
In the late 80s and early 90s, many SIMD machines were commercially available (e.g., Connection machine has 64K ALUs, and MasPar has 16K ALUs)
GPU revives the SIMD computation, and is widely used in high-performance computers
SPMD—Single Program, Multiple Data

## Slide 160: Shared Memory Multiprocessor
160
Memory
Disk & other IO
Registers
Caches
Processor
Registers
Caches
Processor
Registers
Caches
Processor
Registers
Caches
Processor
Interconnect
Memory: centralized with Uniform Memory Access time (“uma”) and bus interconnect, I/O
Examples: Sun Enterprise 6000, SGI Challenge, Intel SystemPro
Notes: 160

## Slide 161: Cache Coherence Problem
161
Processor 3 does not see the value written by processor 0
X:42
R: X
$
MEM
P0
$
P1
$
P2
$
P3
X:42
X:17
W: X = 17
R: X
X:42

## Slide 162: Write Through does not help
162
Processor 3 sees 42 in cache (does not get the correct value (17) from memory.
X:42
R: X
$
MEM
P0
$
P1
$
P2
$
P3
X:42
X:17
W: X = 17
R: X
X:42
X:17
R: X

## Slide 163: Cache Coherence
Coherence
  All reads by any processor return the most recently written value
  Writes to the same location by any two processors are seen in the same order by all processors
Consistency
  When a written value will be returned by a read
  If a processor writes location A followed by location B, any processor that sees the new value of B must also see the new value of A

## Slide 164: Enforcing Coherence
Coherent caches provide:
  Migration: movement of data
  Replication: multiple copies of data
Cache coherence protocols
  Directory based
    Sharing status of each block kept in one location
  Snooping
    Each core tracks sharing status of each block

## Slide 165: Distributed Cache: Snoopy Cache-Coherence Protocols
165
Bus is a broadcast medium & caches know what they have
  bus protocol: arbitration, command/addr, data
  => Every device observes every transaction
State
Address
Data

## Slide 166: Snooping Cache Coherency
166
Cache Controller “snoops” all transactions on the shared bus
  A transaction is a relevant transaction if it involves a cache block currently contained in this cache
    take action to ensure coherence (invalidate, update, or supply value)

## Slide 167
Hardware Cache Coherence
write-invalidate
write-update (also called distributed write)
P
P
X -> X’
invalidate -->
X -> Inv
P
X -> Inv
. . . . .
memory
P
P
X -> X’
update -->
X -> X’
P
X -> X’
. . . . .
memory

## Slide 168: An Example Snoopy Protocol
Invalidation protocol, write-back cache
  “invalidate” request on memory bus
Each cache block is in one state (track these):
  Shared : multiple caches potentially have copies of the block; the block can be read
  OR Modified : this cache has the only copy of the block; the block is writeable and dirty
  OR Invalid : the block contains no valid data

## Slide 169: Snoopy Coherence Protocols
Write invalidate
  On write, invalidate all other copies
  Use bus itself to serialize
    Write cannot complete until bus access is obtained
Write update
  On write, update all copies

## Slide 170: Snoopy Coherence Protocols

## Slide 171: Snoopy-Cache State Machine
State machine for CPU requests for each cache block and for bus requests for each cache block
Place read miss on bus
Invalid
Shared
(read only)
Exclusive
(modified)
CPU: Read
CPU: Write miss
CPU: Read hit
Place Write Miss on bus
CPU: read miss
Write back block, Place read miss on bus
CPU Write miss
Place Write Miss on Bus
CPU: Read miss
Place read miss
on bus
CPU: Write Miss
Write back data,
Place write miss on bus
CPU: Write hit
CPU: Read hit
Write Back
Block
Bus: Write miss
Bus:Read miss
Write Back Block
Bus: Invalidate
CPU: Write hit Place invalidate on Bus
Bus: Write miss

## Slide 172: Performance
Coherence influences cache miss rate
  Coherence misses
    True sharing misses
      Write to shared block (transmission of invalidation)
      Read an invalidated block
    False sharing misses
      Read an unmodified word in an invalidated block

## Slide 173: Revisit: Coherency Solutions
Snooping Solution (Snoopy Bus):
  Send all requests for data to all caches
  Requires broadcast, works well with bus (natural broadcast medium)
  Dominates for small scale machines (most of the market)
Directory-Based Schemes
  Keep track of what is being shared in 1 centralized place (logically)
  Send point-to-point requests to processors via network
  Scales better than Snooping

## Slide 174: Scalable Shared Memory Architectures
174
Used in IBM SP Multiprocessor
0
1
1
P
0
P
1
P
2
P
3
P
4
P
5
P
6
P
7
M
0
M
1
M
2
M
3
M
4
M
5
M
6
M
7
000
001
010
011
100
101
110
111