## Slide 1: Comp4611 Tutorial 1
Computer Processor History
Die Cost Calculation
Performance Measuring & Evaluation
Sept. 9, 2013

## Slide 2: Overview
Computer Processor History
  A Brief Summary of Intel Microprocessors
Die Cost Calculation
Performance Measuring & Evaluation
Appendix: Amdahl’s Law & Example

## Slide 3: Advances Come from Design - A Brief History of Intel Microprocessors
4 bits processor
8 bits processors
4004 (1971)
Intel's first microprocessor
8008 (1972)
twice as powerful as the 4004
8080 (1974)
brains of the first personal computer
~US$ 400
8086 – 8088 (1978)
brains of IBM's new hit product -- the IBM PC
The 8088's success propelled Intel into the ranks of the Fortune 500, and Fortune magazine named the company one of the "Business Triumphs of the Seventies."
80286 (1982)
first Intel processor that could run all the software written for its predecessor
Within 6 years of its release, an estimated 15 million 286-based personal computers were installed around the world.
16 bits processor

## Slide 4: Advances Come from Design - in the 80’s
80386 (1985)
275,000 transistors--more than 100times as many as the original 4004
32-bit chip
"multi tasking"
80486 (1989)
32 bit chip
built-in math coprocessor
packaged together with cache memory chip
command-level computer  point-and-click computing
color computer
32 bits processors
4
Notes: Find more on:
http://www.intel.com/intel/intelis/museum/online/hist_micro/hof/index.htm
http://article.pchome.net/2003/06/25/10429.htm

## Slide 5: Advances Come from Design - in the 90’s
Pentium Pro (1995)
5.5 million transistors
packaged together with a second speed-enhancing cache memory chip,
pipelining
enabling fast computer-aided design, mechanical engineering and scientific computation
Pentium II (1997)
7.5 million-transistor
MMX technology, designed specifically to process video, audio and graphics data efficiently
high-speed cache memory chip
Celeron (1999)
excellent performance in gaming
Pentium (1993)
incorporate "real world" data such as speech, sound, handwriting and photographic images

## Slide 6: Advances Come from Design - in the Millenniums'
Pentium III (1999)
9.5 million transistors, 0.25-micron technology
70 new SSE (Streaming SIMD Extension) instructions
dramatically enhance the performance of advanced imaging, 3-D, streaming audio, video and speech recognition applications, Internet experiences
Pentium 4 (2000)
42 million transistors and circuit lines of 0.18 microns
1.5 gigahertz (4004 ran at 108 kilohertz )
SSE2 instructions, more pipeline stages, higher successful prediction rate
can create professional-quality movies; deliver TV-like video via the Internet; communicate with real-time video and voice; render 3D graphics in real time; quickly encode music for MP3 players; and simultaneously run several multimedia applications while connected to the Internet.

## Slide 7: Advances Come from Design - in last decade
Pentium D (2005)
Dual-core processing technology
   high-end entertainment: multimedia entertainment, digital photo editing, multiple users and multitasking
Pentium Dual-Core (2007)
High-value performance for multitasking (CPU executes more instructions in less time)
Smart Cache: smarter, more efficient cache and bus design
 enhanced performance, responsiveness and power savings
Core 2 Duo (2006)
A dual-core CPU
A new microarchitecture to replace Netburst
Memory Hierarchy System
Low power consumption
Core™2 Quad (2008)
Four execution cores
More intensive entertainment and more media multitasking
64 bits processors

## Slide 8: Advances Come from Design - Nowadays
Core™ i series (2008)
aims at
  Reducing idle power
  Boosting performance by increasing processor frequency
  Hyper-threading
Core™ i3
A dual-core CPU
Core™ i5
A quad-core CPU
Core™ i7
A quad-core CPU (up to 8 cores)

## Slide 9: Advances Come from Technology - A Comparison
Processor | Intel® Pentium® D Processor | Intel® Pentium® Dual-Core Processor | Intel® Core™2 Duo Processor | Intel® Core™2 Quad Processor | Intel® Core™i-series Processor
Process Technology | 65 nm - 90 nm | 65 nm | 65 nm | 65 nm | 45nm
L2 Cache | 1MB - 2MB for each core | 1MB | 2M - 4M | 8M | 3M – 8M
Clock Speed | 2.80 - 3.60 GHz | 1.6 - 2 GHz | 1.86 – 3.0 GHz | 2.4 - 2.66 GHz | 1.6 GHz – 2.9 GHz
Chipset | Intel® 945P, 945G, 955X, 975X chipsets | N/A | Intel® Q965, Q963, G965, P965, 975X | Intel® P965, 975X | Intel® Z87, H87, H81 chipsets
Increase in processor performance due to the growth in CPU Transistor Count
Notes: Gl: why these indicate progress enabled by technology?

## Slide 10: Overview
Computer Processor History
  A Brief Summary of Intel Microprocessors
Die Cost Calculation
Performance Measuring & Evaluation
Appendix: Amdahl’s Law & Example

## Slide 11: Cost of an Integrated Circuit
Where α is a parameter inversely proportional to the number of mask
Levels, which is a measure of the manufacturing complexity.
For today’s CMOS process, good estimate is α = 3.0 – 4.0
Yield: the percentage of manufactured devices that survives the testing procedure
wafer
die

## Slide 12: Example: Die Cost
Given: wafer 30cm, die 1cm,
defect density 0.6 per cm2 ,
α=4.0 30-cm-diameter wafer with 3-4 metal layers : $3500 wafer yield is 100%
Calculate:
die cost
To calculate the die cost,
Given wafer cost
Dies/Wafer?
Die Yield?

## Slide 13: Example: Die Cost
Given: wafer 30cm, die 1cm,
defect density 0.6 per cm2 ,
α=4.0 30-cm-diameter wafer with 3-4 metal layers : $3500 wafer yield is 100%
Calculate:
die cost
Step 1: dies per wafer

## Slide 14: Example: Die Cost
Given: wafer 30cm, die 1cm,
defect density 0.6 per cm2 ,
α=4.0 30-cm-diameter wafer with 3-4 metal layers : $3500 wafer yield is 100%
Calculate:
die cost
Step 2: die yield

## Slide 15: Example: Die Cost
Given: wafer 30cm, die 1cm,
defect density 0.6 per cm2 ,
α=4.0 30-cm-diameter wafer with 3-4 metal layers : $3500 wafer yield is 100%
Calculate:
die cost
Step 3: die cost

## Slide 16: Overview
Computer Processor History
  A Brief Summary of Intel Microprocessors
Die Cost Calculation
Performance Measuring & Evaluation
Appendix: Amdahl’s Law & Example

## Slide 17: How to Measure Performance ?
Performance Rating
  CPU Time
  Benchmark programs
    Integer programs and floating point programs
      Compression
      Compiler
      Artificial Intelligence
      Physics / Quantum Computing
      Video Compression
      Path-finding Algorithms
  Comparing & Summarizing Performance

## Slide 18: Measuring Performance - CPU Execution Time
Performance = 1 / Execution Time
CPU time = Seconds = Instructions x Cycles x Seconds
Program Program Instruction Cycle
Clock cycle
= 1 / Clock rate
CPI
Instruction
count

## Slide 19: Measuring CPU Time – Example 1
CPU time = Instruction count x CPI x (1/clock rate)
A SPEC CPU2006 integer benchmark (464.h264ref, a video compression program written in C) is run on a Pentium D processor:
Total instruction count: 3731 billion
Average CPI for the program: 2.5 cycles/instruction.
CPU clock rate: 2.1 GHz
Source: Analysis of Redundancy and Application Balance in the SPEC CPU2006 Benchmark Suite
  CPU time = 3731 x 109 x 2.5 / (2.1 x 109)
  = 4442 seconds

## Slide 20: Comparing Performance – Example 2
Suppose SPEC CPU2006 integer benchmark (464.h264ref) is run on a faster processor, with a new compiler:
New total instruction count: 2000 billion
New average CPI for the program: 4 cycles/instruction.
New CPU clock rate: 3.6 GHz
  Speedup = Old CPU time = 4442 = 1.999
  New CPU time 2222
Speedup = Old Execution Time = Iold x CPIold x Clock cycleold
New Execution Time Inew x CPInew x Clock Cyclenew
  New CPU time = 2000 x 109 x 4 / (3.6 x 109)
  = 2222 seconds

## Slide 21: Comparing Performance – Example 3
Speedup = Old Execution Time = Iold x CPIold x Clock cycleold
New Execution Time Inew x CPInew x Clock Cyclenew
Instruction Class | Frequency | Old CPI | New CPI
ALU | 40% | 3 | 2
Load | 20% | 1 | 2
Store | 20% | 1 | 2
Branch | 20% | 2 | 3
Question: Should the new design be implemented?
Answer: Shouldn’t be implemented
Old CPI
= 0.40 x 3 + 0.2 x 1 + 0.2 x 1 + 0.2 x 2
= 2
New CPI
= 0.4 x 2 + 0.2 x 2 + 0.2 x 2 + 0.2 x 3
= 2.2
Speedup
= Iold x 2 x Clock cycleold
Inew x 2.2 x Clock cyclenew
= 0.91

## Slide 22: Metrics for Performance
CPU time: most accurate and fair measure
CPU Time = Instruction Count x CPI x Clock Cycle Time
a priori frequency of the instruction set

## Slide 23
Suppose we have made the following measurements:
  Frequency of FP operations (other than FPSQR) = 23%
  Average CPI of FP operations (other than FPSQR) = 4.0
  Frequency of FPSQR = 2%, CPI of FPSQR = 20
  Average CPI of other instructions = 1.33
Assume that the two design alternatives
  decrease the CPI of FPSQR to 3
  decrease the average CPI of FP operations (other than FPSQR)
  to 2.
Compare these two design alternatives using the CPU performance equation.
Measuring Performance – Example 4

## Slide 24: Solution
Step 1: Original CPI without enhancement:
CPI original = 423% + 20x2% +1.3375% = 2.3175
Step 2: compute the CPI for the enhanced FPSQR by subtracting the cycles saved from the original CPI:
CPI with new FPSQR = CPI original - 2%(CPI old FPSQR – CPI new FPSQR only)
= 2.3175 - 0.02x(20-3) = 1.9775
Step 3: compute the CPI for the enhancement of all FP instructions:
CPI with new FP = CPI original - 23%(CPI old FP – CPI new FP)
= 2.3175 - 0.23x(4-2) = 1.8575
Step 4: the speedup for the FP enhancement over FPSQR enhancement is:
Speedup = CPU time with new FPSQR / CPU time with new FP
= (I  CPI with new FPSQR  C) / (I  CPI with new FP  C)
= CPI with new FPSQR / CPI with new FP
= 1.9775 / 1.8575 = 1.065
Notes: An example of making common case faster.

## Slide 25: Comparing & Summarizing Performance - By total execution time
Total execution time
 | Machine A | Machine B
Program 1 | 1 | 10
Program 2 | 1000 | 100
Total | 1001 | 110
How much faster is Machine B than Machine A?
9.1 times?
Machine A is faster in running Program 1.
Machine B is faster in running Program 2.
UNCLEAR

## Slide 26: Comparing & Summarizing Performance - by arithmetic mean of execution time
 | Machine A | Machine B
Program 1 | 1 | 10
Program 2 | 1000 | 100
Total | 1001 | 110
AM | 500.5 | 55
 | Machine A | Machine B
Program 1 | 200 | 400
Program 2 | 250 | 400
Program 3 | 450 | 100
AM | 300 | 300
Arithmetic Mean:
n
Execution Timei
i=1
1
n
Can be
misleading
Valid only if
programs run equally

## Slide 27: Comparing & Summarizing Performance - by weighted arithmetic mean of execution time
 | Machine A | Machine B | W (1)
Program 1 | 200 | 400 | 0.4
Program 2 | 250 | 500 | 0.4
Program 3 | 550 | 100 | 0.2
AM | 300 | 300 | 
WAM (1) | 200 x 0.4 + 250 x 0.4 + 550 x 0.2 = 290 | 400 x 0.4 + 500 x 0.4 + 100 x 0.2 = 380 | 
Weighted Arithmetic Mean:
n
Weighti x Execution Timei
i=1
Machine A is better
For the 1st of Weights:

## Slide 28: Comparing & Summarizing Performance - by weighted arithmetic mean of execution time
 | Machine A | Machine B | W (2)
Program 1 | 200 | 400 | 0.2
Program 2 | 250 | 500 | 0.2
Program 3 | 550 | 100 | 0.6
AM | 300 | 300 | 
WAM (2) | 200 x 0.2 + 250 x 0.2 + 550 x 0.6 = 420 | 400 x 0.2 + 500 x 0.2 + 100 x 0.6 = 240 | 
Weighted Arithmetic Mean:
n
Weighti x Execution Timei
i=1
Machine B is better
It depends very much on how to weigh each testing item
For the 2nd set of Weights:

## Slide 29: Comparing & Summarizing Performance - by geometric mean of execution time
 | Machine A | Machine B
Program 1 | 1 | 10
Program 2 | 1000 | 100
Total | 1001 | 110
 | Normalized to A | 
 | Machine A | Machine B
Program 1 | 1 | 10
Program 2 | 1 | 0.1
GM | 1 | 1
Geometric Mean: n
Execution time ratioi
I=1
n
Normalized Execution Time to a
reference machine
Same GM
≠
same execution time or same performance

## Slide 30: Overview
Computer Processor History
  A Brief Summary of Intel Microprocessors
Die Cost Calculation
Performance Measuring & Evaluation
Appendix: Amdahl’s Law & Example

## Slide 31: Amdahl’s Law
Amdahl’s Law – law of diminishing returns
In general case, assume several enhancements has been taken for the system, the speedup for whole system is:
where Fi is the fraction of enhancement i and Si is the speedup of the corresponding enhancement
The new execution time is

## Slide 32: Amdahl’s Law - An Example
Float instruction:
  Fraction: 50%
  Speedup: 2.0x
Integer instruction:
  Fraction: 30%
  Speedup: 3.0x
Others keep the same.
= 1 / ((1-0.5-0.3)+(0.5/2+0.3/3))=1.818

## Slide 33: Amdahl’s Law - Intuition: “Make the common case faster”
I have two processors, which can help accelerate one of the below parts by parallel processing. Two parts occupy the total time percentage of 95% and 5%.
Fractionenhanced = 95%, Speedupenhanced = 2.0x
Speedupoverall = 1/((1-0.95)+0.95/2) = 1.905
Fractionenhanced = 5%, Speedupenhanced = 2.0x
Speedupoverall = 1/((1-0.05)+0.05/2) = 1.026
1.905 vs. 1.026
Make the common case faster!!
Fractionenhanced = 5%, Speedupenhanced -> infinity
Speedupoverall = 1/(1-0.05) = 1.052
1.052 is still much smaller than 1.905.

## Slide 34: A Common Confusion: CPI vs. Amdahl’s Law
Assume a program consists of three classes of instructions A,B and C, as shown below.
An enhancement is made by doubling the speed of instruction class A
Assume instruction count for the program and CPU clock cycle is not influenced
What is the overall speedup achieved for the program
Instruction Class | Frequency | Old CPI | New CPI
A | 20% | 2 | 1
B | 20% | 3 | 3
C | 60% | 4 | 4
Method 1: CPI
Method 2: Amdahl’s Law
The fraction in Amdahl’s law is time fraction
Method 2: Amdahl’s Law
Notes: Gl: by double  by doubling

## Slide 35: References:
John L. Hennessy and David A. Patterson. Computer Architecture: A Quantitative Approach. Morgan Kaufman Publishers, 5th Edition, 2011
Intel
  http://www.intel.com
  http://www.intel.com/content/www/us/en/history/museum-story-of-intel-4004.html
  http://www.intel.com/pressroom/kits/quickrefyr.htm
http://en.wikipedia.org/wiki/Microprocessor
Timeline of Microprocessor http://m.theinquirer.net/inquirer/feature/2124781/microprocessor-development