## Slide 1
Input/Output I/O Devices, RAID and Network Storage Lin Gu CSE, HKUST
COMP4611: Design and Analysis of Computer Architectures

## Slide 2: Motivation: Who Cares About I/O?
CPU Performance: 60% improvement per year
I/O system performance: < 10% improvement per year
  sometimes limited by mechanical delays (disk I/O)
10% IO & 10x CPU => 5x Performance (lose 50%)
  10% IO & 100x CPU => 10x Performance (lose 90%)
I/O bottleneck:
  Diminishing value of faster CPUs

## Slide 3: Input and Output Devices
I/O devices are diverse with respect to
  Behavior – input, output or storage
  User – human or machine
  Data rate – the rate at which data are transferred between the I/O device and the main memory or processor
Device | Behavior | User | Data rate (Mb/s)
Keyboard | input | human | 0.0001
Mouse | input | human | 0.0038
Laser printer | output | human | 3.2000
Graphics display | output | human | 800.0000-8000.0000
Network/LAN | input or output | machine | 10.0000-10000.0000
Magnetic disk | storage | machine | 240.0000-2560.0000
9 orders of magnitude range

## Slide 4: I/O Performance Measures
I/O bandwidth (throughput) – amount of information that can be input (output) and communicated across an interconnect (e.g., a bus) to the processor/memory (I/O device) per unit time
  How much data can we move through the system in a certain time?
  How many I/O operations can we do per unit time?
I/O response time (latency) – the total elapsed time to accomplish an input or output operation
  An especially important performance metric in real-time systems
Many applications require both high throughput and short response times

## Slide 5: A Simpe System with I/O
Processor
Cache
Memory - I/O Bus
Main
Memory
I/O
Controller
Disk
Disk
I/O
Controller
I/O
Controller
Graphics
Network
interrupts

## Slide 6: A More Recent System
Processor/Memory
Bus
I/O Bus (PCI)
I/O Buses (ISA)

## Slide 7: Introduction to I/O
Most of the I/O devices are very slow compared to the cycle time of a CPU.
The architecture of I/O systems is an active area of R&D.
  I/O systems can define the performance of a system.
Computer architects strive to design systems that do not tie up the CPU waiting for slow I/O systems (too many applications running simultaneously on processor).

## Slide 8: Hard Disk
Actuator
Arm
Head
Platters (12)
{
Spindle

## Slide 9: Hard Disk Performance
Platter
Arm
Actuator
Head
Sector
Inner
Track
Outer
Track
Disk Latency = Seek Time + Rotation Time + Transfer Time + Controller Overhead
Seek Time depends on the moving distance and moving speed of arms
Rotation Time depends on how fast the disk rotates and how far sector is from head
Transfer Time depends on data rate (bandwidth) of disk and size of request
Controller
Spindle

## Slide 10: Disk Access Time
+ Rotational delay
+ Transfer time
Seek time
Disk access time =
+ Other delays
Disk platter
Disk arm
Disk head
block x
in memory
I want
block X

## Slide 11: Example: Barracuda 180
  181.6 GB, 3.5 inch disk
  12 platters, 24 surfaces
  24,247 cylinders
  7,200 RPM; (4.2 ms avg. latency)
  7.4/8.2 ms avg. seek (r/w)
  65 to 35 MB/s (internal)
  0.1 ms controller time
source: www.seagate.com
Latency =
Queuing Time +
Controller time +
Seek Time + Rotation Time +
Size / Bandwidth
per access
per byte
{
+

## Slide 12: Disk Performance Example
Calculate time to read 64 KB (128 sectors) for Barracuda 180 X using advertised performance; sector is on outer track
Disk latency = average seek time + average rotational delay + transfer time + controller overhead
= 7.4 ms + 0.5 * 1/(7200 RPM) + 64 KB / (65 MB/s) + 0.1 ms
= 7.4 ms + 0.5 /(7200 RPM/(60000ms/M)) + 64 KB / (65 KB/ms) + 0.1 ms
= 7.4 + 4.2 + 1.0 + 0.1 ms = 12.7 ms

## Slide 13: Communication of I/O Devices and Processor
How does the processor command the I/O devices?
  Special I/O instructions
    Must specify both the device (port number) and the command
  For example:
  inp reg, port ; registerport
  out port, reg ; portregister
Physical
address space
each device gets
one or more
addresses
I/O address space

## Slide 14: Communication of I/O Devices and Processor
How does the processor command the I/O devices?
  Memory-mapped I/O
    Portions of the memory address space are assigned to I/O devices
    Read and writes to those memory addresses are interpreted as commands to the I/O devices
    Load/stores to the I/O address space can only be done by the OS
each device gets
one or more
addresses
Physical address space

## Slide 15: Communication of I/O Devices and Processor
How does the I/O device communicate with the processor?
  Polling – the processor periodically checks the status of an I/O device to determine its need for service
    Processor is totally in control – it also does all the work
    Can waste a lot of processor time due to speed differences
  Interrupt-driven I/O – the I/O device issues an interrupt to the processor to indicate that it needs attention

## Slide 16: Interrupt-Driven Input
add
sub
and
or
beq
lbu
sb
...
jr
memory
user
program
1. input interrupt
input
interrupt
service
routine
Processor
Receiver
Memory
:
Keyboard
Notes: For class handout

## Slide 17: Interrupt-Driven Input
memory
user
program
1. input interrupt
2.1 save state
Processor
Receiver
Memory
add
sub
and
or
beq
lbu
sb
...
jr
2.2 jump to interrupt
service routine
2.4 return
to user code
Keyboard
2.3 service interrupt
input
interrupt
service
routine

## Slide 18: Interrupt-Driven Output
Processor
Trnsmttr
Memory
Display
add
sub
and
or
beq
lbu
sb
...
jr
memory
user
program
1.output interrupt
2.1 save state
output
interrupt
service
routine
2.2 jump to interrupt
service routine
2.4 return
to user code
2.3 service interrupt

## Slide 19: Direct-Memory Access (DMA)
Interrupt-driven IO relieves the CPU from waiting for every IO event
But the CPU can still be bogged down if it is used in transferring IO data.
  Typically blocks of bytes.
For high-bandwidth devices (like disks) interrupt-driven I/O would consume a lot of processor cycles

## Slide 20: DMA
DMA – the I/O controller has the ability to transfer data directly to/from the memory without involving the processor

## Slide 21: DMA
Consider printing a 60-line by 80-character page
With no DMA:
  CPU will be interrupted 4800 times, once for each character printed.
With DMA:
  OS sets up an I/O buffer and CPU writes the characters into the buffer.
  DMA is commanded (includes the beginning address of the buffer and its size) to print the buffer.
  DMA will take items from the buffer one-at-a-time and performs everything requested.
  Once the operation is complete, the DMA sends a single interrupt signal to the CPU.

## Slide 22: I/O Communication Protocols
Typically one I/O channel controls multiple I/O devices.
We need a two-way communication between the channel and the I/O devices.
  The channel needs to send the command/data to the I/O devices.
  The I/O devices need to send the data/status information to the channel whenever they are ready.

## Slide 23: Channel to I/O Device Communication
Channel sends the address of the device on the bus.
All devices compare their addresses against this address.
  Optionally, the device which has matched its address places its own address on the bus again.
    First, it is an acknowledgement signal to the channel;
    Second, it is a check of validity of the address.
The channel then places the I/O command/data on the bus received by the correct I/O device.
The command/data is queued at the I/O device and is processed whenever the device is ready.

## Slide 24: I/O Devices to Channel Communication
The I/O devices-to-channel communication is more complicated, since now several devices may require simultaneous access to the channel.
  Need arbitration among multiple devices (bus master?)
  May prefer a priority scheme
Three methods for providing I/O devices-to-channel communication

## Slide 25: Daisy Chaining
Two schemes
Centralized control (priority scheme)
Channel
I/O
1
I/O
2
I/O
n
Bus
Data/Address/Control lines
Grant
Request
Busy

## Slide 26: Daisy Chaining
The I/O devices activate the request line for bus access.
If the bus is not busy (indicated by no signal on busy line), the channel sends a Grant signal to the first I/O device (closest to the channel).
  If the device is not the one that requested the access, it propagates the Grant signal to the next device.
  If the device is the one that requested an access, it then sends a busy signal on the busy line and begins access to the bus.
Only a device that holds the Grant signal can access the bus.
When the device is finished, it resets the busy line.
The channel honors the requests only if the bus is not busy.
Obviously, devices closest to the channel have a higher priority and block access requests by lower priority devices.

## Slide 27: Daisy Chaining
Decentralized control (Round-robin Scheme)
Channel
I/O
1
I/O
2
I/O
n
Bus
Data/Address/Control lines
Grant
Request

## Slide 28: Daisy Chaining
The I/O devices send their request.
The channel activates the Grant line.
The first I/O device which requested access accepts the Grant signal and has control over the bus.
  Only the devices that have received the grant signal can have access to the bus.
When a device is finished with an access, it checks to see if the request line is activated or not.
If it is activated, the current device sends the Grant signal to the next I/O device (Round-Robin) and the process continues.
  Otherwise, the Grant signal is deactivated.

## Slide 29: Polling
The channel interrogates (polls) the devices to find out which one requested access:
Channel
I/O
1
I/O
2
I/O
n
Count
lines
Data/Address/Control lines
Request
Busy

## Slide 30: Polling
Any device requesting access places a signal on request line.
If the busy signal is off, the channel begins polling the devices to see which one is requesting access.
  It does this by sequentially sending a count from 1 to n on log2n lines to the devices.
Whenever a requesting device matches the count against its own number (address), it activates the busy line.
The channel stops the count (polling) and the device has access over the bus.
When access is over, the busy line is deactivated and the channel can either continue the count from the last device (Round-Robin) or start from the beginning (priority).

## Slide 31: Independent Requests

## Slide 32: Independent Requests
Each device has its own Request-Grant lines:
  Again, a device sends in its request, the channel responds by granting access
  Only the device that holds the grant signal can access the bus
  When a device finishes access, it lowers it request signal.
  The channel can use either a Priority scheme or Round-Robin scheme to grant the access.

## Slide 33: I/O Buses
Connect I/O devices (channels) to memory.
  Many types of devices are connected to a bus.
  Have a wide range of bandwidth requirements for the devices connected to a bus.
  Typically follow a bus standard, e.g., PCI, SCSI.
Clocking schemes:
  Synchronous: The bus includes a clock signal in the control lines and a fixed protocol for address and data relative to the clock
  Asynchronous: The bus is self-timed and uses a handshaking protocol between the sender and receiver

## Slide 34: I/O Buses
Synchronous buses are fast and inexpensive, but
  All devices on the bus must run at the same clock rate.
  Due to clock-skew problems, buses cannot be long.
  CPU-Memory buses are typically implemented as synchronous buses.
    The front side bus (FSB) clock rate typically determines the clock speed of the memory you must install.

## Slide 35: I/O Buses
Asynchronous buses are self-timed and use a handshaking protocol between the sender and receiver.
This allows the bus to accommodate a wide variety of devices and to lengthen the bus.
I/O buses are typically asynchronous.
  A master (e.g., an I/O channel writing into memory) asserts address, data, and control and begins the handshaking process.

## Slide 36: I/O Buses
Asynchronous write: master asserts address, data, write buses.

## Slide 37: I/O Buses
Asynchronous write: master asserts request, expecting acknowledgement later.

## Slide 38: I/O Buses
Asynchronous write: slave (memory) asserts acknowledgment, expecting request to be deasserted later.

## Slide 39: I/O Buses
Asynchronous write: master deasserts request and expects the acknowledgement to be deasserted later.

## Slide 40: I/O Buses
Asynchronous write: slave deasserts acknowledgement and operation completes.

## Slide 41: I/O Bus Examples
Multiple master I/O buses:

## Slide 42: I/O Bus Examples
Multiple master CPU-memory buses:

## Slide 43: RAID (Redundant Array of Inexpensive Disks)

## Slide 44: Disk Latency & Bandwidth Improvements
Disk latency is one average seek time plus the rotational latency
Disk bandwidth is the peak transfer rate of formatted data
In the time that the disk bandwidth doubles the latency improves by a factor of only 1.2 to 1.4

## Slide 45: Media Bandwidth/Latency Demands
Bandwidth requirements
  High quality video
    Digital data = (30 frames/s) × (640 x 480 pixels) × (24-b color/pixel) = 221 Mb/s (27.625 MB/s)
  High quality audio
    Digital data = (44,100 audio samples/s) × (16-b audio samples) × (2 audio channels for stereo) = 1.4 Mb/s (0.175 MB/s)
Latency issues
  How sensitive is your eye (ear) to variations in video (audio) rates?
  How can you ensure a constant rate of delivery?
  How important is synchronizing the audio and video streams?
    15 to 20 ms early to 30 to 40 ms late is tolerable

## Slide 46: Storage Pressures
Storage capacity growth estimates: 60-100% per year
  Growth of e-business, e-commerce, and e-mail  now common for organizations to manage hundreds of TB of data
  Mission critical data must be continuously available
  Regulations require long-term archiving
  More storage-intensive applications on market
Storage and Security are leading pain points for the IT community
Managing storage growth effectively is a challenge

## Slide 47: Data Growth Trends
-
1,000,000
2,000,000
3,000,000
4,000,000
5,000,000
6,000,000
7,000,000
1999
2000
2001
2002
2003
2004
2005
2006
(in Terabytes)
From 1999 to 2001
Storage Shipped grew
at 78% CAGR
From 2002 to 2006
Storage shipped grew
at 83% CAGR

## Slide 48: Storage Cost
Storage cost as proportion of total IT spending as compared to server cost
Availability/Reliability and Performance are EXTREMLY important

## Slide 49: Importance of Storage Reliability

## Slide 50: RAID
To increase the availability and the performance (bandwidth) of a storage system, instead of a single disk, a set of disks (disk arrays) can be used.
Similar to memory interleaving, data can be spread among multiple disks (striping), allowing simultaneous access to the data and thus improving the throughput.
However, the reliability of the system drops (n devices have 1/n the reliability of a single device).

## Slide 51: Dependability Measures
Reliability: mean time to failure (MTTF)
Service interruption: mean time to repair (MTTR)
Mean time between failures
  MTBF = MTTF + MTTR
Availability = MTTF / (MTTF + MTTR)
Improving Availability
  Increase MTTF: fault avoidance, fault tolerance, fault forecasting
  Reduce MTTR: improved tools and processes for diagnosis and repair

## Slide 52: Array Reliability
Reliability of N disks = Reliability of 1 Disk ÷N
  50,000 Hours ÷ 70 disks = 700 hours
Disk system Mean Time To Failure (MTTF): Drops from 6 years to 1 month!
Arrays without redundancy too unreliable to be useful!

## Slide 53: RAID
A disk array’s availability can be improved by adding redundant disks:
  If a single disk in the array fails, the lost information can be reconstructed from redundant information.
These systems have become known as RAID - Redundant Array of Inexpensive Disks.
  Depending on the number of redundant disks and the redundancy scheme used, RAIDs are classified into levels.
  6 levels of RAID (0-5) are accepted by the industry.
  Level 2 and 4 are not commercially available, they are included for clarity

## Slide 54: RAID-0
stripe 12
stripe 8
stripe 4
stripe 0
stripe 13
stripe 9
stripe 5
stripe 1
stripe 14
stripe 10
stripe 6
stripe 2
stripe 15
stripe 11
stripe 7
stripe 3
Striped, non-redundant
  Parallel access to multiple disks
  Excellent data transfer rate
  Excellent I/O request processing rate (for large stripes) if the controller supports independent Reads/Writes
  Not fault tolerant (AID)
Typically used for applications requiring high performance for non-critical data (e.g., video streaming and editing)

## Slide 55: RAID-1 - Mirroring
Called mirroring or shadowing, uses an extra disk for each disk in the array (most costly form of redundancy)
Whenever data is written to one disk, that data is also written to a redundant disk: good for reads, fair for writes
If a disk fails, the system just goes to the mirror and gets the desired data.
Fast, but very expensive.
Typically used in system drives and critical files
  Banking, insurance data
  Web (e-commerce) servers
stripe 3
stripe 2
stripe 1
stripe 0
stripe 3
stripe 2
stripe 1
stripe 0

## Slide 56: RAID-2: Memory-Style ECC
f0(b)
b2
b1
b0
b3
f1(b)
P(b)
Data Disks
Multiple ECC Disks and a Parity Disk
Multiple disks record the (error correcting code) ECC information to determine which disk is in fault
A parity disk is then used to reconstruct corrupted or lost data
Needs log2(number of disks) redundancy disks
Least used since ECC is irrelevant because most new Hard drives support built-in error correction

## Slide 57: RAID-3 - Bit-interleaved Parity
Use 1 extra disk for each array of n disks.
Reads or writes go to all disks in the array, with the extra disk to hold the parity information in case there is a failure.
The parity is carried out at bit level:
  A parity bit is kept for each bit position across the disk array and stored in the redundant disk.
  Parity: sum modulo 2.
    parity of 1010 is 0
    parity of 1110 is 1
Or use XOR of bits
10010011
11001101
10010011
. . .
Logical record
1 0 0 1 0 0 1 1 0
1 1 0 0 1 1 0 1 1
1 0 0 1 0 0 1 1 0
Striped physical
records
P
Physical record

## Slide 58: RAID-3 - Bit-interleaved Parity
If one of the disks fails, the data for the failed disk must be recovered from the parity information:
  This is achieved by subtracting the parity of good data from the original parity information:
  Recovering from failures takes longer than in mirroring, but failures are rare, so is okay
  Examples:

## Slide 59: RAID-4 - Block-interleaved Parity
In RAID 3, every read or write needs to go to all disks since bits are interleaved among the disks.
Performance of RAID 3:
  Only one request can be serviced at a time
  Poor I/O request rate
  Excellent data transfer rate
  Typically used in large I/O request size applications, such as imaging or CAD
RAID 4: If we distribute the information block-interleaved, where a disk sector is a block, then for normal reads different reads can access different segments in parallel. Only if a disk fails we will need to access all the disks to recover the data.

## Slide 60: RAID-4: Block Interleaved Parity
block 0
block 4
block 8
block 12
block 1
block 5
block 9
block 13
block 2
block 6
block 10
block 14
block 3
block 7
block 11
block 15
P(0-3)
P(4-7)
P(8-11)
P(12-15)
Allow for parallel access by multiple I/O requests
Doing multiple small reads is now faster than before.
A write, however, is a different story since we need to update the parity information for the block.
Large writes (full stripe), update the parity:
P’ = d0’  d1’  d2’  d3’;
Small writes (eg. write on d0), update the parity:
P = d0  d1  d2  d3
P’ = d0’  d1  d2  d3 = d0’  d0  P;
However, writes are still very slow since parity disk is the bottleneck.

## Slide 61: RAID-4: Small Writes

## Slide 62: RAID-5 - Block-interleaved Distributed Parity
To address the write deficiency of RAID 4, RAID 5 distributes the parity blocks among all the disks.
0
4
8
12
20
. . .
1
5
9
16
21
. . .
2
6
13
17
22
. . .
3
10
14
18
23
. . .
7
11
15
19
. . .
P4
P3
P2
P1
P0
P5
RAID 5

## Slide 63: RAID-5 - Block-interleaved Distributed Parity
This allows some writes to proceed in parallel
  For example, writes to blocks 8 and 5 can occur simultaneously.

## Slide 64: RAID-5 - Block-interleaved Distributed Parity
However, writes to blocks 8 and 11 cannot proceed in parallel.

## Slide 65: Performance of RAID-5 - Block-interleaved Distributed Parity
Performance of RAID-5
  I/O request rate: excellent for reads, good for writes
  Data transfer rate: good for reads, good for writes
  Typically used for high request rate, read-intensive data lookup
  File and Application servers, Database servers, WWW, E-mail, and News servers, Intranet servers
The most versatile and widely used RAID.

## Slide 66: RAID-6 – Row-Diagonal Parity
To handle 2 disk errors
  In practice, another disk error can occur before the first problem disk is repaired
Use p-1 data disks, 1 row-parity disk, 1 diagonal-parity disk
If any two of the p+1 disks fail, data can still be recovered
Data Disk 0 | Data Disk 1 | Dada Disk 2 | Dada Disk 3 | Row Parity Disk | Diagonal Parity Disk
0 | 1 | 2 | 3 | 4 | 0
1 | 2 | 3 | 4 | 0 | 1
2 | 3 | 4 | 0 | 1 | 2
3 | 4 | 0 | 1 | 2 | 3

## Slide 67: Dependability
Notes: 67

## Slide 68: Definitions
Examples on why precise definitions so important for reliability
Is a programming mistake a fault, error, or failure?
  Are we talking about the time it was designed or the time the program is run?
  If the running program doesn’t exercise the mistake, is it still a fault/error/failure?
If an alpha particle hits a DRAM memory cell, is it a fault/error/failure if it doesn’t change the value?
  Is it a fault/error/failure if the memory doesn’t access the changed bit?
  Did a fault/error/failure still occur if the memory had error correction and delivered the corrected value to the CPU?

## Slide 69: IFIP Standard terminology
Computer system dependability: quality of delivered service such that reliance can be justifiably placed on the service
Service is observed actual behavior as perceived by other system(s) interacting with this system’s users
Each module has ideal specified behavior, where service specification is agreed description of expected behavior
A system failure occurs when the actual behavior deviates from the specified behavior
failure occurred because an error, a defect in module
The cause of an error is a fault
When a fault occurs it creates a latent error, which becomes effective when it is activated
When error actually affects the delivered service, a failure occurs (time from error to failure is error latency)

## Slide 70: Fault v. (Latent) Error v. Failure
An error is manifestation in the system of a fault, a failure is manifestation on the service of an error
If an alpha particle hits a DRAM memory cell, is it a fault/error/failure if it doesn’t change the value?
  Is it a fault/error/failure if the memory doesn’t access the changed bit?
  Did a fault/error/failure still occur if the memory had error correction and delivered the corrected value to the CPU?
An alpha particle hitting a DRAM can be a fault
If it changes the memory, it creates an error
Error remains latent until affected memory word is read
If the effected word error affects the delivered service, a failure occurs

## Slide 71: Fault Categories
Hardware faults: Devices that fail, such alpha particle hitting a memory cell
Design faults: Faults in software (usually) and hardware design (occasionally)
Operation faults: Mistakes by operations and maintenance personnel
Environmental faults: Fire, flood, earthquake, power failure, and sabotage
Also by duration:
Transient faults exist for limited time and not recurring
Intermittent faults cause a system to oscillate between faulty and fault-free operation
Permanent faults do not correct themselves over time

## Slide 72: Fault Tolerance vs Disaster Tolerance
Fault-Tolerance (or more properly, Error-Tolerance): mask local faults (prevent errors from becoming failures)
  RAID disks
  Uninterruptible Power Supplies
  Cluster Failover
Disaster Tolerance: masks site errors (prevent site errors from causing service failures)
  Protects against fire, flood, sabotage,..
  Redundant system and service at remote site.
  Use design diversity
From Jim Gray’s “Talk at UC Berkeley on Fault Tolerance " 11/9/00

## Slide 73: Case Studies - Tandem Trends Reported MTTF by Component
1985 1987 1990
SOFTWARE 2 53 33 Years
HARDWARE 29 91 310 Years
MAINTENANCE 45 162 409 Years
OPERATIONS 99 171 136 Years
ENVIRONMENT 142 214 346 Years
SYSTEM 8 20 21 Years
Problem: Systematic Under-reporting
From Jim Gray’s “Talk at UC Berkeley on Fault Tolerance " 11/9/00

## Slide 74: HW Failures in Real Systems: Tertiary Disks
A cluster of 20 PCs in seven 7-foot high, 19-inch wide racks with 368 8.4 GB, 7200 RPM, 3.5-inch IBM disks. The PCs are P6-200MHz with 96 MB of DRAM each. They run FreeBSD 3.0 and the hosts are connected via switched 100 Mbit/second Ethernet. Data collected during 18 months of operation.

## Slide 75: How Realistic is "5 Nines"?
HP claims HP-9000 server HW and HP-UX OS can deliver 99.999% availability guarantee “in certain pre-defined, pre-tested customer environments”
  Application faults?
  Operator faults?
  Environmental faults?
Collocation sites (lots of computers in 1 building on Internet) have
  1 network outage per year (~1 day)
  1 power failure per year (~1 day)
Microsoft Network unavailable recently for a day due to problem in Domain Name Server: if only outage per year, 99.7% or 2 Nines

## Slide 76
Data Processing for Today’s Web-Scale Services
  Petabytes of data and demanding computation
  Network performance is essential!
Application tasks | Data size | Computation | Network
Web crawl | 800TB | Highly parallel | High bandwidth
Data analytics | 200TB | Intensive | High bandwidth, low latency
Orkut (social network) | 9TB | Parallelizable | Low latency
Youtube | Estimated multi-petabytes | Intensive, parallelizable | Very high bandwidth, low latency
e-business (e.g., Amazon) | Estimated multi-petabytes | Intensive | High bandwidth, very low latency
Chang, F et al. Bigtable: a distributed storage system for structured data. In Proceedings of the 7th Symposium on Operating Systems Design and Implementation (Seattle, Washington, November 06 - 08, 2006). 205-218. http://baijia.info/showthread.php?tid=4

## Slide 77
A distributed file system at work (GFS)
  Single master and numerous slaves communicate with each other
  File data unit, “chunk”, is up to 64MB. Chunks are replicated.
Requires extremely high network bandwidth, very low network latency
Large-Scale Fault Tolerant File System

## Slide 78: Network Storage Systems
Notes: 78

## Slide 79: Which Storage Architecture?
DAS - Directly-Attached Storage
NAS - Network Attached Storage
SAN - Storage Area Network

## Slide 80: Storage Architectures (Direct Attached Storage (DAS))
Unix
Netware
NT/W2K
NetWare Server
Storage
NT Server
Storage
Virtual Drive 3
Unix Server
Storage

## Slide 81: DAS
CPUs
Bus
Memory
SCSI Adaptor
SCSI Adaptor
SCSI Disk Drive
NIC
SCSI protocol
MS Windows
Traditional Server
Block
I/O

## Slide 82: Storage Architectures (Direct Attached Storage (DAS))
Disk C
ERP Server
Disk B
Exchange Server
Disk A
File Server

## Slide 83: The Problem with DAS
Direct Attached Storage (DAS)
Data is bound to the server hosting the disk
Expanding the storage may mean purchasing and managing another server
In heterogeneous environments, management is complicated
Windows NT/2K
Linux/Unix
Netware

## Slide 84
Advantages
Low cost
Simple to use
Easy to install
Disadvantages
No shared resources
Difficult to backup
Limited distance
Limited high-availability options
Complex maintenance
Solution for small organizations only
Storage Architectures (Direct Attached Storage (DAS))

## Slide 85: Storage Architectures (Network Attached Storage (NAS))
Hosts
IP Network
NAS Controller
Disk subsystem
Shared
Information

## Slide 86: NAS (Network Attached Storage)
What is it?
NAS devices contain embedded processors that run specialized OS or micro kernel that understands networking protocols and is optimized for particular tasks, such as file service. NAS devices usually deploy some level of RAID storage.

## Slide 87: NAS
CPUs
Bus
Memory
NIC
MS Windows
“Diskless” App Server
(or rather a “Less Disk” server)
IP network
File protocol (CIFS, NFS)
CPUs
Bus
Memory
NIC
Optimized OS
NAS appliance
SCSI Adaptor
SCSI Adaptor
SCSI Disk Drive
SCSI Adaptor
SCSI Adaptor
SCSI Disk Drive
SCSI protocol
Block
I/O

## Slide 88: The NAS Network
IP network
App Server
App Server
App Server
NAS Appliance
NAS - truly an appliance

## Slide 89: More on NAS
NAS Devices can easily and quickly attach to a LAN
NAS is platform and OS independent and appears to machines as another server
NAS Devices provide storage that can be addressed via standard file system (e.g., NFS, CIFS) protocols

## Slide 90
Advantages
Easy to install
Easy to maintain
Shared information
Unix, Windows file sharing
Remote access
Disadvantages
Not suitable for databases
Storage islands
Not-very-scalable solution
NAS controller is a bottle neck
Vendor-dependable
Suitable for file based application
Storage Architectures (Network Attached Storage (NAS))

## Slide 91: Some NAS Problems
Network Attached Storage (NAS)
Each appliance represents a larger island of storage
Data is bound to the NAS device hosting the disk and cannot be accessed if the system hosting the drive fails
Storage is labor-intensive and thus expensive
Network is bottleneck
Windows NT/2K
Linux/Unix
Netware
NAS

## Slide 92: Some Benefits of NAS
Files are easily shared among users at high demand and performance
Files are easily accessible by the same user from different locations
Demand for local storage at the desktop is reduced
Storage can be added more economically and partitioned among users— reasonably scalable
Data can be backed up from the common repository more efficiently than from desktops
Multiple file servers can be consolidated into a single managed storage pool

## Slide 93: Storage Architectures (Storage Area Networks (SAN))
Storage
Network
Hosts
IP
Network
Clients
Shared
Storage

## Slide 94: SAN (Storage Area Network)
what is it?
In short, SAN is essentially just another type of network, consisting of storage components (instead of computers), one or more interfaces, and interface extension technologies. The storage units communicate in much the same form and function as computers communicate on a LAN.

## Slide 95: Advantages of SANs
Superior Performance
Reduces Network bottlenecks
Highly Scalable
Allows backup of storage devices with minimal impact on production operations
Flexibility in configuration

## Slide 96: Additional Benefits of SANs
Storage Area Network (SAN)
Server Consolidation
Storage Consolidation
Storage Flexibility and Management
LAN Free backup and archive
Modern data protection (change from traditional tape backup to snap-shot, archive, geographically separate mirrored storage)
Windows NT/2K
Linux/Unix
Netware
SAN Switch

## Slide 97: Additional Benefits of SANs
Disks appear to be directly attached to each host
Provides potential of direct attached performance over Fibre Channel distances (Uses block level I/O)
Provides flexibility of multiple host access
  Storage can be partitioned, with each partition dedicated to a particular host computer
  Storage can be shared among a heterogeneous set of host computers
Economies of scale can reduce management costs by allowing administration of a centralized pool of storage and allocating storage to projects on an as-needed basis
SAN can be implemented within a single computer room environment, across a campus network, or across a wide area network