## Slide 1
Memory System Cache Lin Gu CSE, HKUST
COMP4611: Design and Analysis of Computer Architectures

## Slide 2: Memory Hierarchy: Motivation The Principle Of Locality
Programs usually access a relatively small portion of their address space (instructions/data) at any instant of time (loops, data arrays).
Two Types of locality:
  Temporal Locality: If an item is referenced, it will tend to be referenced again soon.
  Spatial locality: If an item is referenced, items whose addresses are close by will tend to be referenced soon .
The presence of locality in program behavior (e.g., loops, data arrays), makes it possible to satisfy a large percentage of program access needs (both instructions and operands) using memory levels with much less capacity than the program address space.

## Slide 3: Locality Example
Locality Example:
  Data
    Reference array elements in succession (stride-1 reference pattern):
    Reference sum each iteration:
  Instructions
    Reference instructions in sequence:
    Cycle through loop repeatedly:
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;
Spatial locality
Spatial locality
Temporal locality
Temporal locality

## Slide 4: Memory Hierarchy: Terminology
A Block: The smallest unit of information transferred between two levels.
Hit: Item is found in some block in the upper level (example: Block X)
  Hit Rate: The fraction of memory accesses found in the upper level.
  Hit Time: Time to access the upper level which consists of
    memory access time + time to determine hit/miss
Miss: Item needs to be retrieved from a block in the lower level (Block Y)
  Miss Rate = 1 - (Hit Rate)
  Miss Penalty: Time to replace a block in the upper level +
    Time to deliver the block to the processor
Hit Time << Miss Penalty
Lower Level
Memory
Upper Level
Memory
To Processor
From Processor
Blk X
Blk Y

## Slide 5: Caching in a Memory Hierarchy
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Larger, slower, cheaper storage
device at level k+1 is partitioned
into blocks.
Data is copied between
levels in block-sized transfer units
8
9
14
3
Smaller, faster, more expensive
device at level k caches a
subset of the blocks from level k+1
Level k:
Level k+1:
4
4
4
10
10
10

## Slide 6: General Caching Concepts
Request
14
Request
12
Program needs object d, which is stored in some block b.
Cache hit
  Program finds b in the cache at level k. E.g., block 14.
Cache miss
  b is not at level k, so level k cache must fetch it from level k+1. E.g., block 12.
  If level k cache is full, then some current block must be replaced (evicted). Which one is the “victim”?
    Placement policy: where can the new block go? E.g., b mod 4
    Replacement policy: which block should be evicted? E.g., LRU
9
3
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Level
k:
Level
k+1:
14
14
12
14
4*
4*
12
12
0
1
2
3
Request
12
4*
4*
12

## Slide 7: Cache Design & Operation Issues
Q1: Where can a block be placed in cache? (Block placement strategy & Cache organization)
  Fully Associative, Set Associative, Direct Mapped.
Q2: How is a block found if it is in cache? (Block identification)
  Tag/Block.
Q3: Which block should be replaced on a miss? (Block replacement)
  Random, LRU.
Q4: What happens on a write? (Cache write policy)
  Write through, write back.

## Slide 8: Types of Caches: Organization
Type of cache | Mapping of data from memory to cache | Complexity of searching the cache
Direct mapped (DM) | A memory value can be placed at a single corresponding location in the cache | Easy search mechanism
Set-associative (SA) | A memory value can be placed in any of a set of locations in the cache | Slightly more involved search mechanism
Fully-associative (FA) | A memory value can be placed in any location in the cache | Extensive hardware resources required to search (CAM)
DM and FA can be thought as special cases of SA
  DM  1-way SA
  FA  All-way SA

## Slide 9: Cache Organization & Placement Strategies
Placement strategies or mapping of a main memory data block onto cache block frame addresses divide cache into three organizations:
Direct mapped cache: A block can be placed in one location only, given by:
(Block address) MOD (Number of blocks in cache)
  Advantage: It is easy to locate blocks in the cache (only one possibility)
  Disadvantage: Certain blocks cannot be simultaneously present in the cache (they can only have the same location)

## Slide 10: Cache Organization: Direct Mapped Cache
0
0
0
0
1
0
0
1
0
1
0
1
0
0
1
0
1
1
0
1
1
0
0
0
1
1
0
1
0
1
1
1
0
0
1
1
1
1
0
1
0
0
0
C
a
c
h
e
M
e
m
o
r
y
0
0
1
0
1
0
0
1
1
1
0
0
1
0
1
1
1
0
1
1
1
A block can be placed in one location only, given by:
(Block address) MOD (Number of blocks in cache)
In this case: (Block address) MOD (8)
32 memory
blocks
cacheable
8 cache block
frames
(11101) MOD (1000) = 101

## Slide 11: Direct Mapping
0xF0
11111
11111
0xAA
0x0F
00000
00000
0x55
0
1
0
00001
0
1
0
1
0x0F
00000
00000
0x55
11111
0xAA
0xF0
11111
Tag
Index
Data
Direct mapping:
  A memory value can only be placed at a single corresponding location in the cache

## Slide 12: Cache Organization & Placement Strategies
Fully associative cache: A block can be placed anywhere in cache.
  Advantage: No restriction on the placement of blocks. Any combination of blocks can be simultaneously present in the cache.
  Disadvantage: Costly (hardware and time) to search for a block in the cache
Set associative cache: A block can be placed in a restricted set of places, or cache block frames. A set is a group of block frames in the cache. A block is first mapped onto the set and then it can be placed anywhere within the set. The set in this case is chosen by:
(Block address) MOD (Number of sets in cache)
  If there are n blocks in a set the cache placement is called n-way set-associative, or n-associative.
  A good compromise between direct mapped and fully associative caches (most processors use this method).

## Slide 13: Cache Organization Example

## Slide 14: Set Associative Mapping (2-Way)
0xF0
1111
1111
0xAA
0x0F
0000
0000
0x55
0
1
0x0F
0x55
0xAA
0xF0
Tag
Index
Data
00
01
10
0001
10
11
0000
0000
1111
1111
Way 1
Way 0
Set-associative mapping:
  A memory value can be placed in any block frame of a set corresponding to the block address

## Slide 15: Fully Associative Mapping
0xF0
1111
1111
0xAA
0x0F
0000
0000
0x55
0x0F
0x55
0xAA
0xF0
Tag
Data
000110
000001
000000
111110
111111
0xF0
1111
1111
0xAA
0x0F
0000
0000
0x55
0x0F
0x55
0xAA
0xF0
000110
000001
000000
111110
111111
Fully-associative mapping:
  A block can be stored anywhere in the cache

## Slide 16: Cache Organization Tradeoff
For a given cache size, there is a tradeoff between hit rate and complexity
If L = number of lines (blocks) in the cache, L = Cache Size / Block Size
How many places Name of Number of Sets for a block to go cache type
1 Direct Mapped L
n n-way associative L/n
L Fully Associative 1
Number of comparators needed to compare tags

## Slide 17: An Example
Assume a direct mapped cache with 4-word blocks and a total size of 16 words.
Consider the following string of address references given as word addresses:
  1, 4, 8, 5, 20, 17, 19, 56, 9, 11, 4, 43, 5, 6, 9, 17
Show the hits and misses and final cache contents.

## Slide 19
Main memory
block no in
cache
0
1, 4, 8, 5, 20, 17, 19, 56, 9, 11, 4, 43, 5, 6, 9, 17

## Slide 20
Main memory
block no in
cache
0
1
1, 4, 8, 5, 20, 17, 19, 56, 9, 11, 4, 43, 5, 6, 9, 17

## Slide 21
Main memory
block no in
cache
0
1
2
1, 4, 8, 5, 20, 17, 19, 56, 9, 11, 4, 43, 5, 6, 9, 17

## Slide 22
Main memory
block no in
cache
0
1
2
Cache
0
14
13
12
11
10
9
8
7
6
5
4
3
2
1
21
20
19
18
3
2
1
0
11
10
9
8
7
6
5
4
3
2
1
0
17
16
15
Memory
Block #
Block #
0
1
2
3
0
1
2
3
4
Address 5: Hit, access block 1 of cache
1, 4, 8, 5, 20, 17, 19, 56, 9, 11, 4, 43, 5, 6, 9, 17

## Slide 23
Main memory
block no in
cache
0
5
2
1, 4, 8, 5, 20, 17, 19, 56, 9, 11, 4, 43, 5, 6, 9, 17

## Slide 24
Main memory
block no in
cache
4
5
2
1, 4, 8, 5, 20, 17, 19, 56, 9, 11, 4, 43, 5, 6, 9, 17

## Slide 25
Main memory
block no in
cache
4
5
2
1, 4, 8, 5, 20, 17, 19, 56, 9, 11, 4, 43, 5, 6, 9, 17

## Slide 26
Main memory
block no in
cache
4
5
14
1, 4, 8, 5, 20, 17, 19, 56, 9, 11, 4, 43, 5, 6, 9, 17

## Slide 27
Main memory
block no in
cache
4
5
2
1, 4, 8, 5, 20, 17, 19, 56, 9, 11, 4, 43, 5, 6, 9, 17

## Slide 28
Main memory
block no in
cache
4
5
2
1, 4, 8, 5, 20, 17, 19, 56, 9, 11, 4, 43, 5, 6, 9, 17

## Slide 29
Main memory
block no in
cache
4
1
2
1, 4, 8, 5, 20, 17, 19, 56, 9, 11, 4, 43, 5, 6, 9, 17

## Slide 30
Main memory
block no in
cache
4
1
10
1, 4, 8, 5, 20, 17, 19, 56, 9, 11, 4, 43, 5, 6, 9, 17

## Slide 31
Main memory
block no in
cache
4
1
10
1, 4, 8, 5, 20, 17, 19, 56, 9, 11, 4, 43, 5, 6, 9, 17

## Slide 32
Main memory
block no in
cache
4
1
10
1, 4, 8, 5, 20, 17, 19, 56, 9, 11, 4, 43, 5, 6, 9, 17

## Slide 33
Main memory
block no in
cache
4
1
2
1, 4, 8, 5, 20, 17, 19, 56, 9, 11, 4, 43, 5, 6, 9, 17

## Slide 34
Main memory
block no in
cache
4
1
2
1, 4, 8, 5, 20, 17, 19, 56, 9, 11, 4, 43, 5, 6, 9, 17

## Slide 35
Summary
Number of Hits = 6
Number of Misses = 10
Hit Ratio: 6/16 =
37.5%  Unacceptable
Typical Hit ratio:
> 90%

## Slide 36: Locating A Data Block in Cache
Each block in the cache has an address tag.
The tags of every cache block that might contain the required data are checked in parallel.
A valid bit is added to the tag to indicate whether this cache entry is valid or not.
The address from the CPU to the cache is divided into:
  A block address, further divided into:
    An index field to choose a block set in the cache.
    (no index field when fully associative).
    A tag field to search and match addresses in the selected set.
  A block offset to select the data from the block.
Block Address
Block
Offset
Tag
Index

## Slide 37: Address Field Sizes
Block Address
Block
Offset
Tag
Index
  Block offset size = log2(block size)
Index size = log2(Total number of blocks/associativity)
Tag size = address size - index size - offset size
Physical Address Generated by CPU
Mapping function:
Cache set or block frame number = Index =
= (Block Address) MOD (Number of Sets)
Number of Sets

## Slide 38: Locating A Data Block in Cache
Increasing associativity shrinks index, expands tag
  Block index not needed for fully associative cache
Block
Offset, m bits
Block Address
Tag – r bits
Index – k bits
2k addressable blocks in the cache
2m bytes in a block
Tag to identify a unique block

## Slide 39: Direct-Mapped Cache Example
Suppose we have a 16KB of data in a direct-mapped cache with 4 word blocks
Determine the size of the tag, index and offset fields if we’re using a 32-bit architecture
Offset
  need to specify correct byte within a block
  block contains 4 words = 16 bytes = 24 bytes
  need 4 bits to specify correct byte

## Slide 40: Direct-Mapped Cache Example
Index: (~index into an “array of blocks”)
  need to specify correct row in cache
  cache contains 16 KB = 214 bytes
  block contains 24 bytes (4 words)
  # rows/cache =# blocks/cache (since there’s one block/row)
  = bytes/cache bytes/row
  = 214 bytes/cache 24 bytes/row
  = 210 rows/cache
  need 10 bits to specify this many rows

## Slide 41: Direct-Mapped Cache Example
Tag: use remaining bits as tag
  tag length = mem addr length - offset - index = 32 - 4 - 10 bits = 18 bits
  so tag is leftmost 18 bits of memory address

## Slide 42: 4KB Direct Mapped Cache Example
A
d
d
r
e
s
s
(
s
h
o
w
i
n
g
b
i
t
p
o
s
i
t
i
o
n
s
)
2
0
1
0
B
y
t
e
o
f
f
s
e
t
V
a
l
i
d
T
a
g
D
a
t
a
I
n
d
e
x
0
1
2
1
0
2
1
1
0
2
2
1
0
2
3
T
a
g
I
n
d
e
x
H
i
t
D
a
t
a
2
0
3
2
3
1
3
0
1
3
1
2
1
1
2
1
0
1K = 1024 Blocks
Each block = one word
Can cache up to
232 bytes = 4 GB
of memory
Mapping function:
Cache Block frame number =
(Block address) MOD (1024)
Index field
Tag field
Block offset
= 2 bits
Block Address = 30 bits
Tag = 20 bits
Index = 10 bits

## Slide 43: 64KB Direct Mapped Cache Example
A
d
d
r
e
s
s
(
s
h
o
w
i
n
g
b
i
t
p
o
s
i
t
i
o
n
s
)
1
6
1
2
B
y
t
e
o
f
f
s
e
t
V
T
a
g
D
a
t
a
H
i
t
D
a
t
a
1
6
3
2
4
K
e
n
t
r
i
e
s
1
6
b
i
t
s
1
2
8
b
i
t
s
M
u
x
3
2
3
2
3
2
2
3
2
B
l
o
c
k
o
f
f
s
e
t
I
n
d
e
x
T
a
g
3
1
1
6
1
5
4
3
2
1
0
4K= 4096 blocks
Each block = four words = 16 bytes
Can cache up to
232 bytes = 4 GB
of memory
Mapping Function: Cache Block frame number = (Block address) MOD (4096)
Larger blocks take better advantage of spatial locality
Index field
Tag field
Word select
Block Address = 28 bits
Tag = 16 bits
Index = 12 bits
Block offset
= 4 bits

## Slide 44: Cache Organization: Set Associative Cache
T
a
g
D
a
t
a
T
a
g
D
a
t
a
T
a
g
D
a
t
a
T
a
g
D
a
t
a
T
a
g
D
a
t
a
T
a
g
D
a
t
a
T
a
g
D
a
t
a
T
a
g
D
a
t
a
E
i
g
h
t
-
w
a
y
s
e
t
a
s
s
o
c
i
a
t
i
v
e
(
f
u
l
l
y
a
s
s
o
c
i
a
t
i
v
e
)
T
a
g
D
a
t
a
T
a
g
D
a
t
a
T
a
g
D
a
t
a
T
a
g
D
a
t
a
F
o
u
r
-
w
a
y
s
e
t
a
s
s
o
c
i
a
t
i
v
e
S
e
t
0
1
T
a
g
D
a
t
a
O
n
e
-
w
a
y
s
e
t
a
s
s
o
c
i
a
t
i
v
e
(
d
i
r
e
c
t
m
a
p
p
e
d
)
B
l
o
c
k
0
7
1
2
3
4
5
6
T
a
g
D
a
t
a
T
w
o
-
w
a
y
s
e
t
a
s
s
o
c
i
a
t
i
v
e
S
e
t
0
1
2
3
T
a
g
D
a
t
a

## Slide 45: Direct-Mapped Cache Design
45
CACHE SRAM
ADDR
DATA[31:0]
0x00001C0
0xff083c2d
0
1
0x0000000
0x00000021
1
0x0000000
0x00000103
0
0
1
0
0x23F0210
0x00000009
1
Tag
V
Data
=
0
3
0x0000000
DATA[58:32]
DATA[59]
DATA
HIT
ADDRESS
=1
Tag (27-bit)
Cache
Index (3-bit)
Byte Offset (2-bit)
32-bit architecture, 32-bit blocks, 8 blocks
Block Address
Block
Offset
Tag
Index

## Slide 46: 4K Four-Way Set Associative Cache: MIPS Implementation Example
46
A
d
d
r
e
s
s
2
2
8
V
T
a
g
I
n
d
e
x
0
1
2
2
5
3
2
5
4
2
5
5
D
a
t
a
V
T
a
g
D
a
t
a
V
T
a
g
D
a
t
a
V
T
a
g
D
a
t
a
3
2
2
2
4
-
t
o
-
1
m
u
l
t
i
p
l
e
x
o
r
H
i
t
D
a
t
a
1
2
3
8
9
1
0
1
1
1
2
3
0
3
1
0
Index
Field
Tag
Field
1024 block frames
1 block = one word (32 bits)
4-way set associative
256 sets
Can cache up to
232 bytes = 4 GB
of memory
Block Address = 30 bits
Tag = 22 bits
Index = 8 bits
Block offset
= 2 bits
Mapping Function: Cache Set Number = (Block address) MOD (256)

## Slide 47: Fully Associative Cache Design
47
tag 11110111
data 1111000011110000101011
=
Key idea: set size of one block
  1 comparator required for each block
  No address decoding
  Practical only for small caches due to hardware demands
tag 00011100
data 0000111100001111111101
=
=
=
=
=
tag 11111110
tag 00000011
tag 11100110
tag 11110111
data 1111000011110000101011
data 0000000000001111111100
data 1110111100001110000001
data 1111111111111111111111
tag in 11110111
data out 1111000011110000101011

## Slide 48: Fully Associative
48
Fully Associative Cache
  0 bit for cache index
  Compare the Cache Tags of all cache entries in parallel
  Example: Block Size = 32 B blocks, we need N 27-bit comparators
:
Cache Data
Byte 0
0
4
31
:
Cache Tag (27 bits long)
Valid Bit
:
Byte 1
Byte 31
:
Byte 32
Byte 33
Byte 63
:
Cache Tag
Byte Select
Ex: 0x01
X
X
X
X
X
Notes: 48

## Slide 49: Unified vs.Separate Level 1 Cache
49
Unified Level 1 Cache
A single level 1 cache is used for both instructions and data.
Separate instruction/data Level 1 caches (Harvard Memory Architecture):
The level 1 (L1) cache is split into two caches, one for instructions (instruction cache, L1 I-cache) and the other for data (data cache, L1 D-cache).
Control
Datapath
Processor
Registers
Unified
Level
One
Cache
L1
Control
Datapath
Processor
Registers
L1
I-cache
L1
D-cache
Unified Level 1 Cache
Separate Level 1 Caches
(Harvard Memory Architecture)

## Slide 50: Cache Replacement Policy
When a cache miss occurs the cache controller may have to select a block of cache data to be removed from a cache block frame and replaced with the requested data, such a block is selected by one of two methods (for direct mapped cache, there is only one choice):
  Random:
    Any block is randomly selected for replacement providing uniform allocation.
    Simple to build in hardware.
    The most widely used cache replacement strategy.
  Least-recently used (LRU):
    Accesses to blocks are recorded and the block replaced is the one that was not used for the longest period of time.
    LRU is expensive to implement, as the number of blocks to be tracked increases, and is usually approximated.

## Slide 51: LRU Policy
51
A
B
C
D
MRU
LRU
LRU+1
MRU-1
Access C
C
A
B
D
Access D
D
C
A
B
Access E
E
D
C
A
Access C
C
E
D
A
Access G
G
C
E
D
MISS, replacement
needed
MISS, replacement
needed
Notes: 51

## Slide 52: Miss Rates for Caches with Different Size, Associativity & Replacement Algorithm Sample Data
Associativity: 2-way 4-way 8-way
Size LRU Random LRU Random LRU Random
16 KB 5.18% 5.69% 4.67% 5.29% 4.39% 4.96%
64 KB 1.88% 2.01% 1.54% 1.66% 1.39% 1.53%
256 KB 1.15% 1.17% 1.13% 1.13% 1.12% 1.12%

## Slide 53: Cache and Memory Performance Average Memory Access Time (AMAT), Memory Stall cycles
The Average Memory Access Time (AMAT): The average number of cycles required to complete a memory access request by the CPU.
Memory stall cycles per memory access: The number of stall cycles added to CPU execution cycles for one memory access.
For an ideal memory: AMAT = 1 cycle, this results in zero memory stall cycles.
Memory stall cycles per memory access = AMAT -1
Memory stall cycles per instruction =
Memory stall cycles per memory access
x Number of memory accesses per instruction
= (AMAT -1 ) x ( 1 + fraction of loads/stores)
Instruction Fetch

## Slide 54: Cache Performance Unified Memory Architecture
For a CPU with a single level (L1) of cache for both instructions and data and no stalls for cache hits:
Total CPU time = (CPU execution clock cycles +
Memory stall clock cycles) x clock cycle time
Memory stall clock cycles =
(Reads x Read miss rate x Read miss penalty) +
(Writes x Write miss rate x Write miss penalty)
If write and read miss penalties are the same:
Memory stall clock cycles = Memory accesses x Miss rate x Miss penalty
With ideal memory

## Slide 55: Cache Performance Unified Memory Architecture
CPUtime = Instruction count x CPI x Clock cycle time
CPIexecution = CPI with ideal memory
CPI = CPIexecution + MEM Stall cycles per instruction
CPUtime = Instruction Count x (CPIexecution +
MEM Stall cycles per instruction) x Clock cycle time
MEM Stall cycles per instruction =
MEM accesses per instruction x Miss rate x Miss penalty
CPUtime = IC x (CPIexecution + MEM accesses per instruction x
Miss rate x Miss penalty) x Clock cycle time
Misses per instruction = Memory accesses per instruction x Miss rate
CPUtime = IC x (CPIexecution + Misses per instruction x Miss penalty) x
Clock cycle time

## Slide 56: Memory Access Tree For Unified Level 1 Cache
CPU Memory Access
L1 Miss:
% = (1- Hit rate) = (1-H1)
Access time = M + 1
Stall cycles per access = M x (1-H1)
L1 Hit:
% = Hit Rate = H1
Access Time = 1
Stalls= H1 x 0 = 0
( No Stall)
L1
AMAT = H1 x 1 + (1 -H1 ) x (M+ 1) = 1 + M x ( 1 -H1)
Stall Cycles Per Access = AMAT - 1 = M x (1 -H1)
M = Miss Penalty
H1 = Level 1 Hit Rate
1- H1 = Level 1 Miss Rate

## Slide 57: Cache Impact On Performance: An Example
Assuming the following execution and cache parameters:
  Cache miss penalty = 50 cycles
  Normal instruction execution CPI ignoring memory stalls = 2.0 cycles
  Miss rate = 2%
  Average memory references/instruction = 1.33
CPU time = IC x [CPI execution + Memory accesses/instruction x Miss rate x
Miss penalty ] x Clock cycle time
CPUtime with cache = IC x (2.0 + (1.33 x 2% x 50)) x clock cycle time
= IC x 3.33 x Clock cycle time
Lower CPI execution increases the impact of cache miss clock cycles

## Slide 58: Cache Performance Example
Suppose a CPU executes at Clock Rate = 200 MHz (5 ns per cycle) with a single level of cache.
CPIexecution = 1.1
Instruction mix: 50% arith/logic, 30% load/store, 20% control
Assume a cache miss rate of 1.5% and a miss penalty of 50 cycles.
CPI = CPIexecution + mem stalls per instruction
Mem Stalls per instruction = Mem accesses per instruction x Miss rate x Miss penalty
Mem accesses per instruction = 1 + .3 = 1.3
Mem Stalls per instruction = 1.3 x .015 x 50 = 0.975
CPI = 1.1 + .975 = 2.075
The ideal memory CPU with no misses is 2.075/1.1 = 1.88 times faster
Instruction fetch
Load/store

## Slide 59: Cache Performance Example
Suppose for the previous example we double the clock rate to 400 MHZ, how much faster is this machine, assuming similar miss rate, instruction mix?
Since memory speed is not changed, the miss penalty takes more CPU cycles:
Miss penalty = 50 x 2 = 100 cycles.
CPI = 1.1 + 1.3 x .015 x 100 = 1.1 + 1.95 = 3.05
Speedup = (CPIold x Cold)/ (CPInew x Cnew)
= 2.075 x 2 / 3.05 = 1.36
The new machine is only 1.36 times faster rather than 2 times faster due to the increased effect of cache misses.
CPUs with higher clock rate, have more cycles per cache miss and more memory impact on CPI.

## Slide 60: Cache Performance Harvard Memory Architecture
For a CPU with separate or split level one (L1) caches for
instructions and data (Harvard memory architecture) and no
stalls for cache hits:
CPUtime = Instruction count x CPI x Clock cycle time
CPI = CPIexecution + Mem Stall cycles per instruction
CPUtime = Instruction Count x (CPIexecution +
Mem Stall cycles per instruction) x Clock cycle time
Mem Stall cycles per instruction = Instruction Fetch Miss rate x Miss Penalty + Data Memory Accesses Per Instruction x Data Miss Rate x Miss Penalty

## Slide 61: Memory Access Tree For Separate Level 1 Caches
CPU Memory Access
L1
Instruction
Data
Data L1 Miss:
Access Time : M + 1
Stalls per access:
% data x (1 - Data H1 ) x M
Data L1 Hit:
Access Time: 1
Stalls = 0
Instruction L1 Hit:
Access Time = 1
Stalls = 0
Instruction L1 Miss:
Access Time = M + 1
Stalls Per access:
%instructions x (1 - Instruction H1 ) x M
Stall Cycles Per Access = % Instructions x ( 1 - Instruction H1 ) x M + % data x (1 - Data H1 ) x M
AMAT = 1 + Stall Cycles per access

## Slide 62: Typical Cache Performance Data Using SPEC92

## Slide 63: Cache Performance Example
To compare the performance of either using a 16-KB instruction cache and a 16-KB data cache as opposed to using a unified 32-KB cache, we assume a hit to take one clock cycle and a miss to take 50 clock cycles, and a load or store to take one extra clock cycle on a unified cache, and that 75% of memory accesses are instruction references. Using the miss rates for SPEC92 we get:
Overall miss rate for a split cache = (75% x 0.64%) + (25% x 6.47%) = 2.1%
From SPEC92 data a unified cache would have a miss rate of 1.99%
Average memory access time = 1 + stall cycles per access
= 1 + % instructions x (Instruction miss rate x Miss penalty)
+ % data x ( Data miss rate x Miss penalty)
For split cache:
Average memory access timesplit
= 1 + 75% x ( 0.64% x 50) + 25% x (6.47%x50) = 2.05 cycles
For unified cache:
Average memory access timeunified
= 1 + 75% x ( 1.99%) x 50) + 25% x ( 1 + 1.99% x 50) = 2.24 cycles

## Slide 64: Cache Write Strategies

## Slide 65: Cache Read/Write Operations
65
Statistical data suggest that reads (including instruction fetches) dominate processor cache accesses (writes account for 25% of data cache traffic).
In cache reads, a block is read at the same time while the tag is being compared with the block address (searching). If the read is a hit the data is passed to the CPU, if a miss it ignores it.
In cache writes, modifying the block cannot begin until the tag is checked to see if the address is a hit.
Thus for cache writes, tag checking cannot take place in parallel, and only the specific data requested by the CPU can be modified.
Cache is classified according to the write and memory update strategy in place: write through, or write back.

## Slide 66: Write-through Policy
66
0x1234
0x1234
0x1234
Processor
Cache
Memory
0x1234
0x5678
0x5678
Notes: 66

## Slide 67: Cache Write Strategies
67
Write Though: Data is written to both the cache block and the main memory.
  The lower level always has the most updated data; an important feature for I/O and multiprocessing.
  Easier to implement than write back.
  A write buffer is often used to reduce CPU write stall while data is written to memory.
Processor
Cache
Write Buffer
DRAM

## Slide 68: Write Buffer for Write Through
68
A Write Buffer is needed between the Cache and Memory
  Processor: writes data into the cache and the write buffer
  Memory controller: write contents of the buffer to memory
Write buffer is just a FIFO queue:
  Typical number of entries: 4
  Works fine if: Store frequency (w.r.t. time) << 1 / DRAM write cycle
Processor
Cache
Write Buffer
DRAM
Notes: 68

## Slide 69: Write-back Policy
69
0x1234
0x1234
0x1234
Processor
Cache
Memory
0x1234
0x5678
0x5678
0x5678
0x9ABC
Notes: 69

## Slide 70: Cache Write Strategies
70
Write back: Data is written or updated only to the cache block.
  Writes occur at the speed of cache
  The modified or dirty cache block is written to main memory later (e.g., when it’s being replaced from cache)
  A status bit called a dirty bit, is used to indicate whether the block was modified while in cache; if not the block is not written to main memory.
  Uses less memory bandwidth than write through.

## Slide 71: Write misses
71
If we try to write to an address that is not already contained in the cache; this is called a write miss.
Let’s say we want to store 21763 into Mem[1101 0110] but we find that address is not currently in the cache.
When we update Mem[1101 0110], should we also load it into the cache?
Index
Tag
Data
V
Address
...
110
...
1
00010
123456
Data
6378
...
1101 0110
...

## Slide 72: No write-allocate
72
With a no-write allocate policy, the write operation goes directly to main memory without affecting the cache.
This is good when data is written but not immediately used again, in which case there’s no point to load it into the cache yet.
Index
Tag
Data
V
...
110
...
1
00010
123456
Address
Data
21763
...
1101 0110
...
Mem[1101 0110] = 21763

## Slide 73: Write Allocate
73
A write allocate strategy would instead load the newly written data into the cache.
If that data is needed again soon, it will be available in the cache.
Index
Tag
Data
V
Address
...
110
...
1
11010
21763
Data
21763
...
1101 0110
...
Mem[214] = 21763

## Slide 74: Memory Access Tree, Unified L1 Write Through, No Write Allocate, No Write Buffer
74
CPU Memory Access
L1
Read
Write
L1 Write Miss:
Access Time : M + 1
Stalls per access:
% write x (1 - H1 ) x M
L1 Write Hit:
Access Time: M +1
Stalls Per access:
% write x (H1 ) x M
L1 Read Hit:
Access Time = 1
Stalls = 0
L1 Read Miss:
Access Time = M + 1
Stalls Per access
% reads x (1 - H1 ) x M
Stall Cycles Per Memory Access = % reads x (1 - H1 ) x M + % write x M
AMAT = 1 + % reads x (1 - H1 ) x M + % write x M

## Slide 75: Memory Access Tree Unified L1 Write Back, With Write Allocate
75
CPU Memory Access
L1
Read
Write
L1 Write Miss
L1 Write Hit:
% write x H1
Access Time = 1
Stalls = 0
L1 Hit:
% read x H1
Access Time = 1
Stalls = 0
L1 Read Miss
Stall Cycles Per Memory Access = (1-H1) x ( M x % clean + 2M x % dirty )
AMAT = 1 + Stall Cycles Per Memory Access
Clean
Access Time = M +1
Stall cycles = M x (1-H1 ) x
% reads x % clean
Dirty
Access Time = 2M +1
Stall cycles = 2M x (1-H1) x
%read x % dirty
Clean
Access Time = M +1
Stall cycles = M x (1 -H1) x
% write x % clean
Dirty
Access Time = 2M +1
Stall cycles = 2M x (1-H1) x
%write x % dirty

## Slide 76: Write Through Cache Performance Example
76
A CPU with CPIexecution = 1.1 uses a unified L1 Write Through, No Write Allocate and no write buffer.
Instruction mix: 50% arith/logic, 15% load, 15% store, 20% control
Assume a cache miss rate of 1.5% and a miss penalty of 50 cycles.
CPI = CPIexecution + MEM stalls per instruction
MEM Stalls per instruction = MEM accesses per instruction x Stalls per access
MEM accesses per instruction = 1 + .3 = 1.3
Stalls per access = % reads x miss rate x Miss penalty + % write x Miss penalty
% reads = 1.15/1.3 = 88.5% % writes = .15/1.3 = 11.5%
Stalls per access = 50 x (88.5% x 1.5% + 11.5%) = 6.4 cycles
Mem Stalls per instruction = 1.3 x 6.4 = 8.33 cycles
AMAT = 1 + 6.4 = 7.4 cycles
CPI = 1.1 + 8.33 = 9.43
The ideal memory CPU with no misses is 9.43/1.1 = 8.57 times faster

## Slide 77: Write Back Cache Performance Example
77
A CPU with CPIexecution = 1.1 uses a unified L1 with write back , write allocate, and the probability a cache block is dirty = 10%
Instruction mix: 50% arith/logic, 15% load, 15% store, 20% control
Assume a cache miss rate of 1.5% and a miss penalty of 50 cycles.
CPI = CPIexecution + mem stalls per instruction
MEM Stalls per instruction =
MEM accesses per instruction x Stalls per access
MEM accesses per instruction = 1 + .3 = 1.3
Stalls per access = (1-H1) x ( M x % clean + 2M x % dirty )
Stalls per access = 1.5% x (50 x 90% + 100 x 10%) = .825 cycles
Mem Stalls per instruction = 1.3 x .825 = 1.07 cycles
AMAT = 1 + .825 = 1.825 cycles
CPI = 1.1 + 1.07 = 2.17
The ideal CPU with no misses is 2.17/1.1 = 1.97 times faster

## Slide 78: Impact of Cache Organization: An Example
78
Given:
A CPI with ideal memory = 2.0 Clock cycle = 2 ns
1.3 memory references/instruction Cache size = 64 KB with
Cache miss penalty = 70 ns, no stall on a cache hit
Compare two caches
One cache is direct mapped with miss rate = 1.4%
The other cache is two-way set-associative, where:
  CPU clock cycle time increases 1.1 times to account for the cache selection multiplexor
  Miss rate = 1.0%

## Slide 79: Impact of Cache Organization: An Example
79
Average memory access time = Hit time + Miss rate x Miss penalty
Average memory access time 1-way = 2.0 + (.014 x 70) = 2.98 ns
Average memory access time 2-way = 2.0 x 1.1 + (.010 x 70) = 2.90 ns
CPU time = IC x [CPI execution + Memory accesses/instruction x Miss rate x
Miss penalty ] x Clock cycle time
CPUtime 1-way = IC x (2.0 x 2 + (1.3 x .014 x 70) = 5.27 x IC
CPUtime 2-way = IC x (2.0 x 2 x 1.10 + (1.3 x 0.01 x 70)) = 5.31 x IC
In this example, 1-way cache offers slightly better performance with less complex hardware.

## Slide 80: 2 Levels of Cache: L1, L2
80
CPU
L1 Cache
L2 Cache
Main Memory
Hit Rate= H1, Hit time = 1 cycle
(No Stall)
Hit Rate= H2, Hit time = T2 cycles
Memory access penalty, M

## Slide 81: Miss Rates For Multi-Level Caches
81
Local Miss Rate: This rate is the number of misses in a cache level divided by the number of memory accesses to this level. Local Hit Rate = 1 - Local Miss Rate
Global Miss Rate: The number of misses in a cache level divided by the total number of memory accesses generated by the CPU.
Since level 1 receives all CPU memory accesses, for level 1:
  Local Miss Rate = Global Miss Rate = 1 - H1
For level 2 since it only receives those accesses missed in level 1:
  Local Miss Rate = Miss rateL2= 1- H2
  Global Miss Rate = Miss rateL1 x Miss rateL2
  = (1- H1) x (1 - H2)

## Slide 82: 2-Level Cache Performance Memory Access Tree
82
CPU Memory Access
L1 Miss:
% = (1-H1)
L1 Hit:
Stalls= H1 x 0 = 0
(No Stall)
L2 Miss:
Stalls= (1-H1)(1-H2) x M
L2 Hit:
(1-H1) x H2 x T2
Stall cycles per memory access = (1-H1) x H2 x T2 + (1-H1)(1-H2) x M
AMAT = 1 + (1-H1) x H2 x T2 + (1-H1)(1-H2) x M
L1
L2
T2: L2 cache hit time in cycle

## Slide 83: 2-Level Cache Performance
83
CPUtime = IC x (CPIexecution + Mem Stall cycles per instruction) x C
Mem Stall cycles per instruction = Mem accesses per instruction x Stall cycles per access
For a system with 2 levels of cache, assuming no penalty when found in L1 cache:
Stall cycles per memory access =
[miss rate L1] x [ Hit rate L2 x Hit time L2
+ Miss rate L2 x Memory access penalty) ] =
(1-H1) x H2 x T2 + (1-H1)(1-H2) x M
L1 Miss, L2 Hit
L1 Miss, L2 Miss:
Must Access Main Memory

## Slide 84: Two-Level Cache Example
84
CPU with CPIexecution = 1.1 running at clock rate = 500 MHZ
1.3 memory accesses per instruction.
L1 cache operates at 500 MHZ with a miss rate of 5%
L2 cache operates at 250 MHZ with local miss rate 40%, (T2 = 2 cycles)
Memory access penalty, M = 100 cycles. Find CPI.
CPI = CPIexecution + MEM Stall cycles per instruction
With No Cache, CPI = 1.1 + 1.3 x 100 = 131.1
With single L1, CPI = 1.1 + 1.3 x .05 x 100 = 7.6
With L1 and L2 caches:
MEM Stall cycles per instruction =
MEM accesses per instruction x Stall cycles per access
Stall cycles per memory access = (1-H1) x H2 x T2 + (1-H1)(1-H2) x M
= .05 x .6 x 2 + .05 x .4 x 100
= .06 + 2 = 2.06
MEM Stall cycles per instruction =
MEM accesses per instruction x Stall cycles per access
= 2.06 x 1.3 = 2.678
CPI = 1.1 + 2.678 = 3.778 Speedup = 7.6/3.778 = 2

## Slide 85: 3 Levels of Cache
85
CPU
L1 Cache
L2 Cache
L3 Cache
Main Memory
Hit Rate= H1, Hit time = 1 cycle
Hit Rate= H2, Hit time = T2 cycles
Hit Rate= H3, Hit time = T3
Memory access penalty, M

## Slide 86: 3-Level Cache Performance Memory Access Tree CPU Stall Cycles Per Memory Access
86
CPU Memory Access
L1 Miss:
% = (1-H1)
L1 Hit:
Stalls= H1 x 0 = 0
( No Stall)
L2 Miss:
% = (1-H1)(1-H2)
L2 Hit:
(1-H1) x H2 x T2
Stall cycles per memory access = (1-H1) x H2 x T2 + (1-H1) x (1-H2) x H3 x T3 + (1-H1)(1-H2) (1-H3)x M
AMAT = 1 + Stall cycles per memory access
L3 Miss:
(1-H1)(1-H2)(1-H3) x M
L3 Hit:
(1-H1) x (1-H2) x H3 x T3
L1
L3
L2

## Slide 87: 3-Level Cache Performance
87
CPUtime = IC x (CPIexecution + Mem Stall cycles per instruction) x C
Mem Stall cycles per instruction = Mem accesses per instruction x Stall cycles per access
For a system with 3 levels of cache, assuming no penalty when found in L1 cache:
Stall cycles per memory access =
[miss rate L1] x [ Hit rate L2 x Hit time L2
+ Miss rate L2 x (Hit rate L3 x Hit time L3
+ Miss rate L3 x Memory access penalty) ] =
(1-H1) x H2 x T2 + (1-H1) x (1-H2) x H3 x T3
+ (1-H1)(1-H2) (1-H3)x M
L1 Miss, L2 Hit
L2 Miss, L3 Hit
L1 Miss, L2 Miss:
Must Access Main Memory

## Slide 88: Three-Level Cache Example
88
CPU with CPIexecution = 1.1 running at clock rate = 500 MHZ
1.3 memory accesses per instruction.
L1 cache operates at 500 MHZ with a miss rate of 5%
L2 cache operates at 250 MHZ with a local miss rate 40%, (T2 = 2 cycles)
L3 cache operates at 100 MHZ with a local miss rate 50%, (T3 = 5 cycles)
Memory access penalty, M= 100 cycles. Find CPI.

## Slide 89: Three-Level Cache Example
89
Memory access penalty, M= 100 cycles. Find CPI.
With No Cache, CPI = 1.1 + 1.3 x 100 = 131.1
With single L1, CPI = 1.1 + 1.3 x .05 x 100 = 7.6
With L1, L2 CPI = 1.1 + 1.3 x (.05 x .6 x 2 + .05 x .4 x 100) = 3.778
CPI = CPIexecution + Mem Stall cycles per instruction
Mem Stall cycles per instruction = Mem accesses per instruction x Stall cycles per access
Stall cycles per memory access = (1-H1) x H2 x T2 + (1-H1) x (1-H2) x H3 x T3 + (1-H1)(1-H2) (1-H3)x M
= .05 x .6 x 2 + .05 x .4 x .5 x 5 + .05 x .4 x .5 x 100
= .06 + .05 + 1 = 1.11
CPI = 1.1 + 1.3 x 1.11 = 2.54
Speedup compared to L1 only = 7.6/2.54 = 3
Speedup compared to L1, L2 = 3.778/2.54 = 1.49

## Slide 90: Cache on Multicore
90
Notes: 90

## Slide 91: Multi-Core and caches coherence
91
memory
L2 cache
L1 cache
L1 cache
C O R E 1
C O R E 0
L2 cache
memory
L2 cache
L1 cache
L1 cache
C O R E 1
C O R E 0
L2 cache
Both L1 and L2 are private
Examples: AMD Opteron, AMD Athlon, Intel Pentium D
L3 cache
L3 cache
A design with L3 caches Example: Intel Itanium 2
Notes: 91

## Slide 92: The cache coherence problem
92
Since we have private caches: How to keep the data consistent across caches?
Each core should perceive the memory as a monolithic array, shared by all the cores
Notes: 92

## Slide 93
93
Suppose variable x initially contains 15213
Core 1
Core 2
Core 3
Core 4
One or more levels of cache
One or more levels of cache
One or more levels of cache
One or more levels of cache
Main memory
x=15213
multi-core chip
The cache coherence problem
Notes: 93

## Slide 94
94
Core 1 reads x
Core 1
Core 2
Core 3
Core 4
One or more levels of cache
x=15213
One or more levels of cache
One or more levels of cache
One or more levels of cache
Main memory
x=15213
multi-core chip
The cache coherence problem
Notes: 94

## Slide 95
95
Core 2 reads x
Core 1
Core 2
Core 3
Core 4
One or more levels of cache
x=15213
One or more levels of cache
x=15213
One or more levels of cache
One or more levels of cache
Main memory
x=15213
multi-core chip
The cache coherence problem
Notes: 95

## Slide 96
96
Core 1 writes to x, setting it to 21660
Core 1
Core 2
Core 3
Core 4
One or more levels of cache
x=21660
One or more levels of cache
x=15213
One or more levels of cache
One or more levels of cache
Main memory
x=21660
multi-core chip
assuming write-through caches
The cache coherence problem
Notes: 96

## Slide 97
97
Core 2 attempts to read x… gets a stale copy
Core 1
Core 2
Core 3
Core 4
One or more levels of cache
x=21660
One or more levels of cache
x=15213
One or more levels of cache
One or more levels of cache
Main memory
x=21660
multi-core chip
The cache coherence problem
Notes: 97

## Slide 98: Reduce Miss Rate
98
Notes: 98

## Slide 99: Reducing Misses (3 Cs)
99
Classifying Misses: 3 Cs
  Compulsory—The first access to a block is not in the cache, so the block must be brought into the cache. These are also called cold start misses or first reference misses. (Misses even in infinite size cache)
  Capacity—If the cache cannot contain all the blocks needed during the execution of a program, capacity misses will occur due to blocks being discarded and later retrieved. (Misses due to size of cache)
  Conflict—If the block-placement strategy is not fully associative, conflict misses (in addition to compulsory and capacity misses) will occur because a block can be discarded and later retrieved if too many blocks map to its set. These are also called collision misses or interference misses. (Misses due to associativity and size of cache)
Notes: 99

## Slide 100: 3Cs Absolute Miss Rates
100
2:1 cache rule
2:1 cache rule: The miss rate of a direct mapped cache of size N is about the same as a 2-way set associative cache of size N/2.
Cache Size (KB)
Miss Rate per Type
0
0.02
0.04
0.06
0.08
0.1
0.12
0.14
1
2
4
8
16
32
64
128
Conflict
1-way
2-way
4-way
8-way
Capacity
Compulsory

## Slide 101: 3Cs Relative Miss Rate
101
Cache Size (KB)
Miss Rate per Type
0%
20%
40%
60%
80%
100%
1
2
4
8
16
32
64
128
1-way
2-way
4-way
8-way
Capacity
Compulsory
Conflict
Notes: 101

## Slide 102: How to Reduce the 3 Cs Cache Misses?
102
Increase Block Size
Increase Associativity
Use a Victim Cache
Use a Pseudo Associative Cache
Hardware Prefetching
Notes: 102

## Slide 103: 1. Increase Block Size
103
One way to reduce the miss rate is to increase the block size
  Take advantage of spatial locality
  Reduce compulsory misses
However, larger blocks have disadvantages
  May increase the miss penalty (need to get more data)
  May increase hit time
  May increase conflict misses (smaller number of block frames)
Increasing the block size can help, but don’t overdo it.

## Slide 104: 1. Reduce Misses via Larger Block Size
104
Cache Size (bytes)
Miss
Rate
0%
5%
10%
15%
20%
25%
16
32
64
128
256
1K
4K
16K
64K
256K
Block Size (bytes)
Notes: 104

## Slide 105: 2. Reduce Misses via Higher Associativity
105
Increasing associativity helps reduce conflict misses (8-way should be good enough)
2:1 Cache Rule:
  The miss rate of a direct mapped cache of size N is about equal to the miss rate of a 2-way set associative cache of size N/2
Disadvantages of higher associativity
  Need to do large number of comparisons
  Need n-to-1 multiplexor for n-way set associative
  Could increase hit time
    Hit time for 2-way vs. 1-way external cache +10%, internal + 2%
Notes: 105

## Slide 106: Example: Avg. Memory Access Time vs. Associativity
106
Example: assume CCT = 1.10 for 2-way, 1.12 for 4-way, 1.14 for 8-way vs. CCT=1 of direct mapped.
Cache Size Associativity
(KB) 1-way 2-way 4-way 8-way
1 7.65 6.60 6.22 5.44
2 5.90 4.90 4.62 4.09
4 4.60 3.95 3.57 3.19
8 3.30 3.00 2.87 2.59
16 2.45 2.20 2.12 2.04
32 2.00 1.80 1.77 1.79
64 1.70 1.60 1.57 1.59
128 1.50 1.45 1.42 1.44
(Red means memory access time not improved by higher associativity)
Does not take into account effect of slower clock on rest of program
Notes: 106

## Slide 107: 3. Reducing Misses via Victim Cache
107
Add a small fully associative victim cache to hold data discarded from the regular cache
When data not found in cache, check victim cache
4-entry victim cache removed 20% to 95% of conflicts for a 4 KB direct mapped data cache
Get access time of direct mapped with reduced miss rate
Notes: 107

## Slide 108: 3. Victim Cache
108
Address
Data Data
in out
CPU
Write buffer
Lower level memory
=?
=?
Tag
Data
Victim Cache
Fully associative, small cache reduces conflict misses without impairing clock rate

## Slide 109: 4. Reducing Misses via Pseudo-Associativity
109
How to combine fast hit time of direct mapped cache and the lower conflict misses of 2-way SA cache?
Divide cache: on a miss, check other half of cache to see if there, if so have a pseudo-hit (slow hit).
Usually check other half of cache by flipping the MSB of the index.
Drawbacks
  CPU pipeline is hard if hit takes 1 or 2 cycles
  Slightly more complex design
Hit Time
Pseudo Hit Time
Miss Penalty
Notes: 109

## Slide 110: Pseudo Associative Cache
110
Address
Data Data
in out
CPU
Write buffer
Lower level memory
Tag
Data
1
1
2
2
3
=?
=?

## Slide 111: 5. Hardware Prefetching
111
Instruction Prefetching
  Alpha 21064 fetches 2 blocks on a miss
  Extra block placed in stream buffer
  On miss check stream buffer
Works with data blocks too:
  1 data stream buffer gets 25% misses from 4KB DM cache; 4 streams get 43%
  For scientific programs: 8 streams got 50% to 70% of misses from 2 64KB, 4-way set associative caches
Prefetching relies on having extra memory bandwidth that can be used without penalty

## Slide 112: Summary
112
3 Cs: Compulsory, Capacity, Conflict Misses
Reducing Miss Rate
  1. Larger Block Size
  2. Higher Associativity
  3. Victim Cache
  4. Pseudo-Associativity
  5. HW Prefetching Instr, Data

## Slide 113: Pros and cons – Re-visit cache design choices
113
Larger cache block size
Pros
  Reduces miss rate
Cons
  Increases miss penalty
Important factors deciding cache performance: hit time, miss rate, miss penalty

## Slide 114: Pros and cons – Re-visit cache design choices
114
Bigger cache
Pros
  Reduces miss rate
Cons
  May increases hit time
  My increase cost and power consumption

## Slide 115: Pros and cons – Re-visit cache design choices
115
Higher associativity
Pros
  Reduces miss rate
Cons
  Increases hit time

## Slide 116: Pros and cons – Re-visit cache design choices
116
Multiple levels of caches
Pros
  Reduces miss penalty
Cons
  Increases cost and power consumption

## Slide 117: Multilevel Cache Design Considerations
Design considerations for L1 and L2 caches are very different
  Primary cache should focus on minimizing hit time in support of a shorter clock cycle
    Smaller cache with smaller block sizes
  Secondary cache (s) should focus on reducing miss rate to reduce the penalty of long main memory access times
    Larger cache with larger block sizes and/or higher associativity

## Slide 118: Key Cache Design Parameters
 | L1 typical | L2 typical
Total size (blocks) | 250 to 2000 | 4000 to 250,000
Total size (KB) | 16 to 64 | 500 to 8000
Block size (B) | 32 to 64 | 32 to 128
Miss penalty (clocks) | 10 to 25 | 100 to 1000
Miss rates (global for L2) | 2% to 5% | 0.1% to 2%

## Slide 119: Reducing Miss rate with programming
j=0
i=0
j=0
i=0
Examples:
  cold cache, 4-byte words, 4-word cache blocks
int sumarrayrows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}
int sumarraycols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}
Miss rate =
～1/N
～ 100%
Miss rate =

## Slide 120: Reducing Miss Penalty
120
Notes: 120

## Slide 121: The cost of a cache miss
121
For a memory access, assume:
  1 clock cycle to send address to memory
  25 clock cycles for each DRAM access (clock cycle 2ns, 50 ns access time)
  1 clock cycle to send each resulting data word
This actually depends on the bus speed
Miss access time (4-word block)
  4 x (Address + access + sending data word)
  4 x (1 + 25 + 1) = 108 = 108 cycles for each miss
Notes: 121

## Slide 122: Memory Interleaving
122
Interleaving
Default
Begin accessing one word, and while waiting, start accessing other three words (pipelining)
CPU
Cache
Memory
4 bytes
Bus
Bus
CPU
Cache
Memory2
4 bytes
Memory1
Memory3
Memory0
Bus
Bus
Bus
Bus
Bus
Requires 4 separate memories, each 1/4 size
Must finish accessing one word before starting the next access
(1+25+1)x4 = 108 cycles
1
25
1
30 cycles
1
25
1
1
25
1
1
25
1
Spread out addresses among the memories
Interleaving works perfectly with caches
Sophisticated DRAMs provide support for this
Notes: 122

## Slide 123: Memory Interleaving: An Example
123
Given the following system parameters with single cache level L1:
Block size=1 word Memory bus width=1 word Miss rate =3% Miss penalty=27 cycles
(1 cycle to send address 25 cycles access time/word, 1 cycle to send a word)
Memory access/instruction = 1.2 Ideal CPI (ignoring cache misses) = 2
Miss rate (block size=2 words) = 2% Miss rate (block size=4 words) =1%
The CPI of the base machine with 1-word blocks = 2+(1.2 x 0.03 x 27) = 2.97
Increasing the block size to two words gives the following CPI:
  32-bit bus and memory, no interleaving = 2 + (1.2 x .02 x 2 x 27) = 3.29
  32-bit bus and memory, interleaved = 2 + (1.2 x .02 x (28)) = 2.67
Increasing the block size to four words; resulting CPI:
  32-bit bus and memory, no interleaving = 2 + (1.2 x 0.01 x 4 x 27) = 3.29
  32-bit bus and memory, interleaved = 2 + (1.2 x 0.01 x (30)) = 2.36

## Slide 124: Summary
124
Interleaving
Multiple levels of caches
Other advanced techniques…

## Slide 125: Cache Optimization
Six basic cache optimizations:
  Larger block size
    Reduces compulsory misses
    Increases capacity and conflict misses, increases miss penalty
  Larger total cache capacity to reduce miss rate
    Increases hit time, increases power consumption
  Higher associativity
    Reduces conflict misses
    Increases hit time, increases power consumption
  Higher number of cache levels
    Reduces overall memory access time
  Giving priority to read misses over writes
    Reduces miss penalty
  Avoiding address translation in cache indexing
    Reduces hit time

## Slide 126: Ten Advanced Optimizations
Small and simple first level caches
  Critical timing path:
    addressing tag memory, then
    comparing tags, then
    selecting correct set
  Direct-mapped caches can overlap tag compare and transmission of data
  Lower associativity reduces power because fewer cache lines are accessed

## Slide 127: L1 Size and Associativity
Access time vs. size and associativity

## Slide 128: L1 Size and Associativity
Energy per read vs. size and associativity

## Slide 129: Way Prediction
To improve hit time, predict the way to pre-set mux
  Mis-prediction gives longer hit time
  Prediction accuracy
    > 90% for two-way
    > 80% for four-way
    I-cache has better accuracy than D-cache
  First used on MIPS R10000 in mid-90s
  Used on ARM Cortex-A8
Extend to predict block as well
  “Way selection”
  Increases mis-prediction penalty

## Slide 130: Pipelining Cache
Pipeline cache access to improve bandwidth
  Examples:
    Pentium: 1 cycle
    Pentium Pro – Pentium III: 2 cycles
    Pentium 4 – Core i7: 4 cycles
Increases branch mis-prediction penalty
Makes it easier to increase associativity

## Slide 131: Nonblocking Caches
Allow hits before previous misses complete
  “Hit under miss”
  “Hit under multiple miss”
L2 must support this
In general, processors can hide L1 miss penalty but not L2 miss penalty

## Slide 132: Multibanked Caches
Organize cache as independent banks to support simultaneous access
  ARM Cortex-A8 supports 1-4 banks for L2
  Intel i7 supports 4 banks for L1 and 8 banks for L2
Interleave banks according to block address

## Slide 133: Critical Word First, Early Restart
Critical word first
  Request missed word from memory first
  Send it to the processor as soon as it arrives
Early restart
  Request words in normal order
  Send missed work to the processor as soon as it arrives
Effectiveness of these strategies depends on block size and likelihood of another access to the portion of the block that has not yet been fetched

## Slide 134: Merging Write Buffer
When storing to a block that is already pending in the write buffer, update write buffer
Reduces stalls due to full write buffer
Do not apply to I/O addresses
No write buffering
Write buffering

## Slide 135: Compiler Optimizations
Loop Interchange
  Swap nested loops to access memory in sequential order
Blocking
  Instead of accessing entire rows or columns, subdivide matrices into blocks
  Requires more memory accesses but improves locality of accesses

## Slide 136: Hardware Prefetching
Fetch two blocks on miss (include next sequential block)
Pentium 4 Pre-fetching

## Slide 137: Compiler Prefetching
Insert prefetch instructions before data is needed
Non-faulting: prefetch doesn’t cause exceptions
Register prefetch
  Loads data into register
Cache prefetch
  Loads data into cache
Combine with loop unrolling and software pipelining

## Slide 138: Summary