## Slide 1: Instruction Set Architectures
RISC, CISC, and MIPS

## Slide 2: CISC (Complex Instruction Set Computers)

## Slide 3: IA - 32
1978: The Intel 8086 is announced (16 bit architecture)
1980: The 8087 floating point coprocessor is added
1982: The 80286 increases address space to 24 bits, +instructions
1985: The 80386 extends to 32 bits, new addressing modes
1989-1995: The 80486, Pentium, Pentium Pro add a few instructions (mostly designed for higher performance)
1997: 57 new “MMX” instructions are added, Pentium II
1999: Pentium III added another 70 instructions (SSE)
2001: Another 144 instructions (SSE2)
2003: AMD extends the architecture to expand address space to 64 bits, widens all registers to 64 bits and other changes (AMD64)
2004: Intel capitulates and embraces AMD64 (calls it EM64T) and adds more media extensions
“This history illustrates the impact of the `golden handcuffs’ of compatibility”:
“adding new features as someone might add clothing to a packed bag” “an architecture that is difficult to explain and impossible to love”

## Slide 4: IA-32 Overview
Complexity:
  Instructions from 1 to 17 bytes long
  one operand must act as both a source and destination
  one operand can come from memory
  complex addressing modes e.g., “base or scaled index with 8 or 32 bit displacement”

## Slide 5: The Rationale for CISC
One of the most visible forms of evolution associated with computers is that of programming languages
As the cost of hardware has dropped, the relative cost of software has risen.
Complexity of modern software has increased the prevalence of faults (bugs).
Thus, the major cost in the lifecycle of a system is software, not hardware.

## Slide 6: The Rationale for CISC
The response from researchers and industry has been to develop ever more powerful and complex high-level languages.
These high-level languages (HLL) allow the programmer to express algorithms more concisely, take care of much of the detail, and naturally support structured programming and object-oriented design.
This solution gave rise to another problem, known as the semantic gap. This is the difference between the operations provided in HLLs and those provided in computer architecture ISA.

## Slide 7: The Rationale for CISC
Symptoms of this gap include:
  Execution inefficiency
  Excessive program size
  Compiler complexity
Designers responded with architectures intended to close this gap. Key feature include:
  Large instruction sets
  Dozens of addressing modes
  Various HLL statements implemented in hardware.

## Slide 8: The Rationale for CISC
Such complex instruction sets are intended to:
  Ease the task of the compiler writer
  Improve execution efficiency, because complex sequences of operations can be implemented in microcode
  Provide support for even more complex and sophisticated HLLs.

## Slide 9: RISC (Reduced Instruction Set Computers)

## Slide 10: The Rationale for RISC
A number of studies have been done to determine the characteristics and patterns of execution of machine instructions generated from HLL programs.
The results of these studies inspired some researchers to look for a different approach.
Namely, to make the architecture that supports the HLL simpler, rather than more complex.

## Slide 11: RISC
RISC systems have been defined and designed in a variety of ways, the key elements shared by most designs are:
  A limited and simple instruction set.
  A large number of general-purpose registers, and the use of compiler technology to optimize register usage.
  An emphasis on optimizing the instruction pipeline.

## Slide 12: Characteristics of RISC Architectures
Although there are a variety of approaches to RISC architectures, certain characteristics are typical to RISC architectures, particularly early systems:
One instruction per cycle – RISC machine instructions comprise only one cycle of fetch, execute, store. With simple, one-cycle instructions, there is no need for microcode (as in CISC); machine instructions can be hardwired. Such instructions should execute faster than comparable machine instructions on CISC machines, as it is not necessary to access a micro-program control store.
Register-to-register operation – If most register operations are register-to-register, the instruction set and therefore the control unit are simplified. For example, a RISC instruction set may only include one or two ADD instructions; VAX has 25 different ADD instructions. This also encourages the optimization of register use.

## Slide 13: Characteristics of RISC Architectures
Simple addressing modes – Almost all RISC instructions use simple register addressing. Complex addressing modes can be synthesized in software from simple ones. Again, this design feature simplifies the instruction set and the control unit.
Simple instruction formats - Generally, only one or a few formats are used. Instruction length is fixed and aligned on word boundaries. Field locations, especially the opcode, are fixed. This has a number of benefits:
  With fixed fields, opcode decoding and register operand accessing can occur simultaneously.
  Simplified formats simplify the control unit.
  Instruction fetching is optimized because word-length units are fetched.
  Alignment on word boundary also means that a single instruction does not cross page boundaries.

## Slide 14: Prospective Benefits of RISC
The benefits of RISC fall into the following two main categories
More effective compiler optimization: With more primitive instructions, there are more opportunities for moving operations out of loops, reorganizing code, maximizing register utilization, etc.
Simple instructions (and little or no microcode) permit a relatively simple control unit, which is likely to be faster than a more complex one.
Instruction pipelining. RISC researchers feel that the instruction pipelining technique can be applied much more effectively with a reduced instruction set.
VLSI Implementation
Chip real estate: a CISC processor typically devotes about half of its area to the control unit. A RISC processor typically uses only about 10% of the area for the control unit, using precious real estate for registers instead.
Design and implementation time. The simple control unit and circuitry of RISC result in faster design cycles.
Performance

## Slide 15: CISC vs. RISC Characteristics
After the initial enthusiasm for RISC, there has been a growing realization that RISC designs may benefits from the inclusion of some CISC features, and vice-versa.
The result is that more recent RISC design, PowerPC and SPARC, are no longer "pure" RISC and the more recent CISC designs, notably the Pentium and Core Duo incorporate core RISC characteristics internally.
  Recent Intel processors implement an internal instruction set that shares similarity with RISC and support x86 (CISC) instruction set externally.
  Hardware translates x86 instructions into the internal instruction set
CRISC—Complex-Reduced Instruction Set Computer?

## Slide 16: Example CISC ISA: Intel X86,386/486/Pentium
12 addressing modes:
Register.
Immediate.
Direct.
Base.
Base + Displacement.
Index + Displacement.
Scaled Index + Displacement.
Based Index.
Based Scaled Index.
Based Index + Displacement.
Based Scaled Index + Displacement.
Relative.
Operand sizes:
Can be 8, 16, 32, 48, 64, or 80 bits long.
Also supports string operations.
Instruction Encoding:
Variable-size instructions
The first bytes generally contain the opcode, mode specifiers, and register fields.
The remainder bytes are for address displacement and immediate data.

## Slide 17: Example RISC ISA: PowerPC
8 addressing modes:
Register direct.
Immediate.
Register indirect.
Register indirect with immediate index (loads and stores).
Register indirect with register index (loads and stores).
Absolute (jumps).
Link register indirect (calls).
Count register indirect (branches).
Operand sizes:
Four operand sizes: 1, 2, 4 or 8 bytes.
Instruction Encoding:
Instruction set has 15 different formats with many minor variations.
All are 32 bits in length.

## Slide 18: Example RISC ISA: HP Precision Architecture, HP-PA
7 addressing modes:
Register
Immediate
Base with displacement
Base with scaled index and displacement
Predecrement
Postincrement
PC-relative
Operand sizes:
Five operand sizes ranging in powers of two from 1 to 16 bytes.
Instruction Encoding:
Instruction set has 12 different formats.
All are 32 bits in length.

## Slide 19: Example RISC ISA: SPARC
Operand sizes:
Four operand sizes: 1, 2, 4 or 8 bytes.
Instruction Encoding:
Instruction set has 3 basic instruction formats with 3 minor variations.
All are 32 bits in length.
5 addressing modes:
Register indirect with immediate displacement.
Register indirect indexed by another register.
Register direct.
Immediate.
PC relative.

## Slide 20: Example RISC ISA: Compaq Alpha AXP
4 addressing modes:
Register direct.
Immediate.
Register indirect with displacement.
PC-relative.
Operand sizes:
Four operand sizes: 1, 2, 4 or 8 bytes.
Instruction Encoding:
Instruction set has 7 different formats.
All are 32 bits in length.

## Slide 21: Architectural Evolution Macro-Level
Common Instruction Set Architecture
No need to port
No need for multiple validations
Built in OS integration
Robust security
Investment protection
Desktop
Server
Laptop
Today
Storage
Handheld
Happening Now
Networking
Ubiquitous
The Future?

## Slide 22
MIPS: Case Study of
Instruction Set Architecture

## Slide 23: MIPS
MIPS: Microprocessor without Interlocked Pipeline Stages
The MIPS instruction set architecture
  is similar to other RISC architectures (SPARC)
  has almost 200 million MIPS processors manufactured in 2006
  is used by NEC, Nintendo, Cisco, Silicon Graphics, Sony, networking equipment, …

## Slide 24: MIPS Design Principles
Simplicity Favors Regularity
  Keep all instructions a single size
  Always require three register operands in arithmetic instructions
2. Smaller is Faster
  Has only 32 registers rather than many more
3. Good Design Makes Good Compromises
  Comprise between providing larger addresses and constants in the instruction and keeping instructions the same length
4. Make the Common Case Fast
  PC-relative addressing for conditional branches
  Immediate addressing for constant operands

## Slide 25: MIPS Instruction Set (RISC)
Instructions execute simple functions.
Maintain regularity of format – each instruction is one word, contains opcode and arguments.
Minimize memory accesses – whenever possible use registers as arguments.
Three types of instructions:
    Register (R)-type – only registers as arguments.
    Immediate (I)-type – arguments are registers and numbers (constants or memory addresses).
    Jump (J)-type – argument is an address.

## Slide 26: MIPS Instructions
All instructions exactly 32 bits wide
Different formats for different purposes
Similarities in formats ease implementation
op
rs
rt
offset
6 bits
5 bits
5 bits
16 bits
op
rs
rt
rd
funct
shamt
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
R-Format
I-Format
op
address
6 bits
26 bits
J-Format
31
0
31
0
31
0

## Slide 27: MIPS Instruction Types
Arithmetic & Logical - manipulate data in registers add $s1, $s2, $s3 $s1 = $s2 + $s3 or $s3, $s4, $s5 $s3 = $s4 OR $s5
Data Transfer - move register data to/from memory lw $s1, 100($s2) $s1 = Memory[$s2 + 100] sw $s1, 100($s2) Memory[$s2 + 100] = $s1
Branch - alter program flow beq $s1, $s2, 25 if ($s1==$s2) PC = PC + 4 + 4*25

## Slide 28: MIPS Registers and Memory
Memory
4GB Max
0x00000000
0x00000004
0x00000008
0x0000000C
0x00000010
0x00000014
0x00000018
0x0000001C
0xfffffff4
0xfffffffc
0xfffffffc
PC = 0x0000001C
Registers
32 General Purpose Registers
R0
R1
R2
R30
R31
32 bits
  232 bytes with addresses 0, 1, 2, …, 232-1

## Slide 29: MIPS Registers and Usage
Each register can be referred to by number or name.

## Slide 30: Machine Language
Instructions, like registers and words of data, are also 32 bits long
  Example: add $t1, $s1, $s2
  registers have numbers, $t1=9, $s1=17, $s2=18
Instruction Format: 000000 10001 10010 01001 00000 100000 op rs rt rd shamt funct
op
rs
rt
offset
6 bits
5 bits
5 bits
16 bits
op
rs
rt
rd
funct
shamt
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
R-Format
I-Format
op
address
6 bits
26 bits
J-Format
31
0
31
0
31
0

## Slide 31: MIPS Data Transfer Instructions
Transfer data between registers and memory
Instruction format (assembly) lw $dest, offset($addr) load word sw $src, offset($addr) store word
Uses:
  Accessing a variable in main memory
  Accessing an array element

## Slide 32: Memory Instructions
Load and store instructions
Example: C code: A[12] = h + A[8]; MIPS code: lw $t0, 32($s3) #addr of A in reg s3 add $t0, $s2, $t0 #h in reg s2 sw $t0, 48($s3)
Can refer to registers by name (e.g., $s2, $t2) instead of number
Store word has destination last
Remember arithmetic operands are registers, not memory! Can’t write: add 48($s3), $s2, 32($s3)

## Slide 33: Example - Loading a Simple Variable
lw R5,8(R2)
Memory
0x00
Variable Z = 692310
Variable X
Variable Y
0x04
0x08
0x0c
0x10
0x14
0x18
0x1c
8
+
Registers
R0=0 (constant)
R1
R2=0x10
R30
R31
R3
R4
R5
R5
R2=0x10
R5 = 629310
Variable Z = 692310

## Slide 34: Data Transfer Instructions - Binary Representation
Used for load, store instructions
  op: Basic operation of the instruction (opcode)
  rs: first register source operand
  rt: second register source operand
  offset: 16-bit signed address offset (-32,768 to +32,767)
Also called “I-Format” or “I-Type” instructions
op
rs
rt
offset
6 bits
5 bits
5 bits
16 bits

## Slide 35: MIPS Arithmetic Instructions
All instructions have 3 operands
Operand order is fixed (destination first) Example: C code: a = b + c MIPS ‘code’: add a, b, c (a, b, c are the corresponding registers) “The natural number of operands for an operation like addition is three… requiring every instruction to have exactly three operands conforms to the philosophy of keeping the hardware simple”

## Slide 36: Arithmetic & Logical Instructions - Binary Representation
Used for arithmetic, logical, shift instructions
  op: Basic operation of the instruction (opcode)
  rs: first register source operand
  rt: second register source operand
  rd: register destination operand
  shamt: shift amount (more about this later)
  funct: function - specific type of operation
Also called “R-Format” or “R-Type” Instructions
op
rs
rt
rd
funct
shamt
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
0
31

## Slide 37: I-Format vs. R-Format Instructions
Compare with R-Format
offset
6 bits
5 bits
5 bits
16 bits
I-Format
op
rs
rt
rd
funct
shamt
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
R-Format
op
rs
rt
Note similarity!

## Slide 38: MIPS Conditional Branch Instructions
Conditional branches allow decision making beq R1, R2, LABEL if R1==R2 goto LABEL bne R3, R4, LABEL if R3!=R4 goto LABEL Example C Code if (i==j) goto L1; f = g + h; L1: f = f - i; Assembly beq $s3, $s4, L1 add $s0, $s1, $s2 L1: sub $s0, $s0, $s3

## Slide 39: Binary Representation - Branch
Branch instructions use I-Format
offset is added to PC when branch is taken beq r0, r1, offset has the effect: if (r0==r1) pc = pc + 4 + offset else pc = pc + 4;
op
rs
rt
offset
6 bits
5 bits
5 bits
16 bits

## Slide 40: Binary Representation - Jump
Jump Instruction uses J-Format (op=2)
What happens during execution? PC = PC[31:28] : (IR[25:0] << 2)
op
address
6 bits
26 bits
Conversion to
word offset
Concatenate upper 4 bits
of PC to form complete
32-bit address

## Slide 41: Summary - MIPS Instruction Set
simple instructions all 32 bits wide
very structured, no unnecessary baggage
only three instruction formats
op
rs
rt
offset
6 bits
5 bits
5 bits
16 bits
op
rs
rt
rd
funct
shamt
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
R-Format
I-Format
op
address
6 bits
26 bits
J-Format

## Slide 42: Summary: MIPS Instructions

## Slide 43
2004 © Morgan Kaufman Publishers
Addressing Modes