## Slide 1
Memory System Memory Hierarchy Lin Gu CSE, HKUST
COMP4611: Design and Analysis of Computer Architectures

## Slide 2: Memory System
Main memory generally uses Dynamic RAM (DRAM),
which uses a single transistor to store a bit, but requires a periodic data refresh (~every 8 msec).
Cache uses SRAM: Static Random Access Memory
  No refresh (6 transistors/bit vs. 1 transistor/bit for DRAM)
Size: DRAM/SRAM ­ 4-8, Cost & Cycle time: SRAM/DRAM ­ 8-16
Performance metrics
  Latency is concern of cache
  Access time: The time it takes between a memory access request and the time the requested information is available to cache/CPU.
  Cycle time: The minimum time between unrelated requests to memory (greater than access time in DRAM to allow address lines to be stable)‏
  Memory bandwidth: The maximum sustained data transfer rate between main memory and cache/CPU.

## Slide 3: Memory Technology
SRAM
  Requires low power to retain bit
  Requires 6 transistors/bit
DRAM
  Must be re-written after being read
  Must also be periodically refeshed
    Every ~ 8 ms
    Each row can be refreshed simultaneously
  One transistor/bit
  Address lines are multiplexed:
    Upper half of address: row access strobe (RAS)
    Lower half of address: column access strobe (CAS)

## Slide 4: Conventional DRAM Organization
d x w DRAM:
  dw total bits organized as d supercells of size w bits
cols
rows
0
1
2
3
0
1
2
3
internal row buffer
16 x 8 DRAM chip
addr
data
supercell
(2,1)
2 bits
/
8 bits
/
memory
controller
(to CPU)

## Slide 5: Reading DRAM Supercell (2,1)
Step 1(a): Row access strobe (RAS) selects row 2.
cols
rows
RAS = 2
0
1
2
3
0
1
2
internal row buffer
16 x 8 DRAM chip
3
addr
data
2
/
8
/
memory
controller
Step 1(b): Row 2 copied from DRAM array to row buffer.

## Slide 6: Reading DRAM Supercell (2,1)
Step 2(a): Column access strobe (CAS) selects column 1.
cols
rows
0
1
2
3
0
1
2
3
internal row buffer
16 x 8 DRAM chip
CAS = 1
addr
data
2
/
8
/
memory
controller
Step 2(b): Supercell (2,1) copied from buffer to data lines, and eventually back to the CPU.
supercell
(2,1)
supercell
(2,1)
To CPU

## Slide 7: Memory Modules
: supercell (i,j)
64 MB
memory module
consisting of
eight 8Mx8 DRAMs
addr (row = i, col = j)
Memory
controller
DRAM 7
DRAM 0
0
31
7
8
15
16
23
24
32
63
39
40
47
48
55
56
64-bit doubleword at main memory address A
bits
0-7
bits
8-15
bits
16-23
bits
24-31
bits
32-39
bits
40-47
bits
48-55
bits
56-63
64-bit doubleword
0
31
7
8
15
16
23
24
32
63
39
40
47
48
55
56
64-bit double word at main memory address A

## Slide 8: Memory Optimizations

## Slide 9: Memory Optimizations

## Slide 10: Memory Optimizations
DDR:
  DDR2
    Lower power (2.5 V -> 1.8 V)
    Higher clock rates (266 MHz, 333 MHz, 400 MHz)
  DDR3
    1.5 V
    800 MHz
  DDR4
    1-1.2 V
    1600 MHz
GDDR5 is graphics memory based on DDR3

## Slide 11: Memory Optimizations
Graphics memory:
  Achieve 2-5 X bandwidth per DRAM vs. DDR3
    Wider interfaces (32 vs. 16 bit)
    Higher clock rate
      Possible because they are attached via soldering instead of socketted DIMM modules
Reducing power in SDRAMs:
  Lower voltage
  Low power mode (ignores clock, continues to refresh)

## Slide 12: Memory Power Consumption

## Slide 13: Flash Memory
Type of EEPROM
Must be erased (in blocks) before being overwritten
Non volatile
Limited number of write cycles
Cheaper than SDRAM, more expensive than disk
Slower than SRAM, faster than disk

## Slide 14: Memory Dependability
Memory is susceptible to cosmic rays
Soft errors: dynamic errors
  Detected and fixed by error correcting codes (ECC)
Hard errors: permanent errors
  Use sparse rows to replace defective rows
Chipkill: a RAID-like error recovery technique

## Slide 15
Impact on Performance
Suppose a processor executes at
  Clock Rate = 200 MHz (5 ns per cycle)
  CPI = 1.1
  50% arith/logic, 30% ld/st, 20% control
Suppose that 10% of memory operations get 50 cycle miss penalty
CPI = ideal CPI + average stalls per instruction = 1.1(cyc) +( 0.30 (datamops/ins) x 0.10 (miss/datamop) x 50 (cycle/miss) ) = 1.1 cycle + 1.5 cycle = 2.6
58 % of the time the processor is stalled waiting for memory!
a 1% instruction miss rate would add an additional 0.5 cycles to the CPI!

## Slide 16: Memory Technology
Amdahl:
  Memory capacity should grow linearly with processor speed
  Unfortunately, memory capacity and speed has not kept pace with processors
Some optimizations:
  Multiple accesses to same row
  Synchronous DRAM
    Added clock to DRAM interface
    Burst mode with critical word first
  Wider interfaces
  Double data rate (DDR)
  Multiple banks on each DRAM device

## Slide 17: Memory Performance Gap

## Slide 18: Latency in a Single PC
Memory Access Time
CPU Time
Ratio
THE WALL

## Slide 19: Technology Trends
Capacity Speed (latency)
Logic: 2x in 3 years 2x in 3 years
DRAM: 4x in 3 years 2x in 10 years
Disk: 4x in 3 years 2x in 10 years
DRAM Generations
Year Size Cycle Time
1980 64 Kb 250 ns
1983 256 Kb 220 ns
1986 1 Mb 190 ns
1989 4 Mb 165 ns
1992 16 Mb 120 ns
1996 64 Mb 110 ns
1998 128 Mb 100 ns
2000 256 Mb 90 ns
2002 512 Mb 80 ns
2006 1024 Mb 60ns
16000:1 4:1
(Capacity) (Latency)

## Slide 20: Processor-DRAM Performance Gap Impact: Example
To illustrate the performance impact, assume a single-issue pipelined CPU with CPI = 1 using non-ideal memory.
The minimum cost of a full memory access in terms of number of wasted CPU cycles:
CPU CPU Memory Minimum CPU cycles or
Year speed cycle Access instructions wasted
MHZ ns ns
1986: 8 125 190 190/125 - 1 = 0.5
1989: 33 30 165 165/30 -1 = 4.5
1992: 60 16.6 120 120/16.6 -1 = 6.2
1996: 200 5 110 110/5 -1 = 21
1998: 300 3.33 100 100/3.33 -1 = 29
2000: 1000 1 90 90/1 - 1 = 89
2003: 2000 .5 80 80/.5 - 1 = 159
2006: 3700 0.27 60 60/.27 – 1 = 221

## Slide 21: How to make memory system better?
Programmers want unlimited amounts of memory with low latency
Fast memory technology is more expensive per bit than slower memory
Solution: organize memory system into a hierarchy
  Entire addressable memory space available in largest, slowest memory
  Incrementally smaller and faster memories, each containing a subset of the memory below it, proceed in steps up toward the processor
Temporal and spatial locality insures that nearly all references can be found in smaller memories
  Gives the allusion of a large, fast memory being presented to the processor

## Slide 22: Memory Hierarchy Design
Memory hierarchy design becomes more crucial with recent multi-core processors:
  Aggregate peak bandwidth grows with # cores:
    Intel Core i7 can generate two references per core per clock
    Four cores and 3.2 GHz clock
      25.6 billion 64-bit data references/second +
      12.8 billion 128-bit instruction references
      = 409.6 GB/s!
    DRAM bandwidth is only 6% of this (25 GB/s)
    Requires:
      Multi-port, pipelined caches
      Two levels of cache per core
      Shared third-level cache on chip
High-end microprocessors have >10 MB on-chip cache
  Consumes large amount of area and power budget

## Slide 23: Memory Hierarchy
The idea is to build a memory subsystem that consists of:
  Very small, very fast, very expensive memory “close” to the processor.
  Larger, slower, but more affordable memory “further away” from the processor.
  Hence, provide the appearance of virtually unlimited memory while minimizing delays to the processor.
The memory hierarchy is organized into levels of memory with the smaller, more expensive, and faster memory levels closer to the CPU: registers, then primary Cache Level (L1), then additional secondary cache levels (L2, L3…), then main memory, then mass storage (virtual memory).

## Slide 24: Levels of The Memory Hierarchy
Part of The On-chip CPU Datapath
16-256 Registers
One or more levels (Static RAM):
Level 1: On-chip 16-64K
Level 2: On or Off-chip 128-512K
Level 3: Off-chip 1M-64M
Registers
Cache
Main Memory
Magnetic Disc
Optical Disk or Magnetic Tape
Farther away from
The CPU
Lower Cost/Bit
Higher Capacity
Increased Access
Time/Latency
Lower Throughput
DRAM, RDRAM
16M-16G
Interface:
SCSI, RAID,
IDE, 1394
4G-100G

## Slide 25: A Typical Memory Hierarchy (With Two Levels of Cache)
Virtual
Memory,
Secondary
Storage
(Disk)
Main
Memory
(DRAM)
Second
Level
Cache
(SRAM)
L2
1s
10,000,000s
(10s ms)
Speed (ns):
10s
100s
100s
Gs
Size (bytes):
Ks
Ms
Tertiary
Storage
(Tape)
10,000,000,000s
(10s sec)
Ts
Control
Datapath
Processor
Registers
On-Chip
Level
One
Cache
L1
Larger Capacity
Faster

## Slide 26: Levels of The Memory Hierarchy

## Slide 27: Recently Typical Configurations

## Slide 28: Memory Hierarchy: Apple iMac G5
07 | Reg | L1 Inst | L1 Data | L2 | DRAM | Disk
Size | 1K | 64K | 32K | 512K | 256M | 80G
Latency Cycles, Time | 1, 0.6 ns | 3, 1.9 ns | 3, 1.9 ns | 11, 6.9 ns | 88, 55 ns | 107, 12 ms
Let programs address a memory space that scales to the disk size, at a speed that is usually as fast as register access
Managed
by compiler
Managed
by hardware
Managed by OS,
hardware,
application
Goal: Illusion of large, fast, cheap memory

## Slide 29: Memory on the CPU Chip
Cache
  Small, Fast Memory
  Holds information (expected) to be used soon
  Mostly Successful
Apply Recursively
  Level-one cache(s)
  Level-two cache
Most of microprocessor die area is cache!
Architects Use Transistors to Tolerate Slow Memory

## Slide 30: Pentium 4 Cache hierarchy (Gallatin)
Processor
L1 I (12Ki)
L1 D (8KiB)
L2 cache (512 KiB)
L3 cache (2 MiB)
Cycles: 2
Cycles: 19
Cycles: 43
Memory
Cycles: 206

## Slide 31: iMac’s PowerPC 970: All caches on-chip
(1K)
Registers
512K
L2
L1 (64K Instruction)
L1 (32K Data)

## Slide 32: Case study: Intel Core2 Duo
L2 Cache
Core0
Core1
L1 | 32 KB, 8-Way, 64 Byte/Line, LRU, WB 3 Cycle Latency
L2 | 4.0 MB, 16-Way, 64 Byte/Line, LRU, WB 14 Cycle Latency
Source: http://www.sandpile.org

## Slide 33: Memory Hierarchy Basics
When a word is not found in the higher level, a miss occurs:
  Fetch word from lower level in hierarchy, requiring a higher latency reference
  Also fetch the other words contained within the block
    Takes advantage of spatial locality
  Place block into cache in any location within its set, determined by address
    block address MOD number of sets

## Slide 34: Memory Hierarchy Operation
If an instruction or operand is required by the CPU, the levels of the memory hierarchy are searched for the item starting with the level closest to the CPU (Level 1 cache):
  If the item is found, it’s delivered to the CPU resulting in a cache hit.
  If the item is missing from an upper level, resulting in a miss, the level just below is searched.
  For systems with several levels of cache, the search continues with cache level 2, 3 etc.
  If all levels of cache report a miss then main memory is accessed.
    CPU « cache « memory: Managed by hardware.
  If the item is not found in main memory resulting in a page fault, then disk (virtual memory), is accessed for the item.
    Memory « disk: Managed by hardware and the operating system.

## Slide 35: Memory Hierarchy Basics
n sets => n-way set associative
  Direct-mapped cache => one block per set
  Fully associative => one set
Writing to cache: two strategies
  Write-through
    Immediately update lower levels of hierarchy
  Write-back
    Only update lower levels of hierarchy when an updated block is replaced
  Both strategies use write buffer to make writes asynchronous

## Slide 36: Memory Hierarchy Basics
Miss rate
  Fraction of cache access that result in a miss
Causes of misses
  Compulsory
    First reference to a block
  Capacity
    Blocks discarded and later retrieved
  Conflict
    Program makes repeated references to multiple addresses from different blocks that map to the same location in the cache

## Slide 37: Memory Hierarchy Basics
Note that speculative and multithreaded processors may execute other instructions during a miss
  Reduces performance impact of misses