## Slide 1
Memory System Virtual Memory Lin Gu CSE, HKUST
COMP4611: Design and Analysis of Computer Architectures

## Slide 2: Why Virtual Memory?
An example: MIPS64 is a 64-bit architecture allowing an address space defined by 64 bits
  Maximum address space:
    264 = 16 x 1018 =16,000 petabytes
    peta = 1015
This is several orders of magnitude larger than any realistic and economical (or necessary for that matter) physical memory system

## Slide 3: Virtual Memory
Originally invented to support program sizes larger than then-available physical memory
  later on it finds applications in multi-programming and virtual machines
Virtual memory is as large as the address space allowed by the ISA…but
  only a portion of the address space resides in physical memory at any given time
  the rest is kept on disks and brought into physical memory as needed
  virtual memory can be viewed as providing an interface between the physical main memory and disk storage
    this is similar to the role that cache plays for main memory (recall that cache size << main memory size)

## Slide 4: Motivations for Virtual Memory
(1) Use Physical DRAM as a Cache for the Disk
  Address space of a process (program) can exceed physical memory size
  Sum of address spaces of multiple processes can exceed physical memory
(2) Simplify Memory Management
  Multiple processes reside in main memory.
    Each process with its own address space
  Only “active” code and data are actually in memory
    Allocate more memory to process as needed.

## Slide 5: Motivation #1: DRAM a “Cache” for Disk
Full address space is quite large:
  32-bit addresses: 0—4,294,967,295 (~ 4 billion bytes)
  64-bit addresses: 0—18,446,744,073,709,551,615 (~ 16,000 petabytes)
Disk storage is ~500X cheaper than DRAM storage
  80 GB of DRAM: ~ $25,000
  80 GB of disk: ~ $50
To access large amounts of data in a cost-effective manner, the bulk of the data must be stored on disk
1GB: ~$300
160 GB: ~$100
4 MB: ~$500
Disk
DRAM
SRAM

## Slide 6: DRAM vs. SRAM as a “Cache”
DRAM vs. disk is more extreme than SRAM vs. DRAM
  Access latencies:
    DRAM ~10X slower than SRAM
    Disk ~100,000X slower than DRAM
  Bottom line:
    Design decisions made for DRAM caches driven by enormous cost of misses
DRAM
SRAM
Disk

## Slide 7: Multi-programming
Multiple programs run concurrently, each with the illusion that it owns all the machine resources
Each program requires memory space

## Slide 8: Multiprogramming and Memory Protection
In the early machines, I/O operations were slow
  having the CPU wait pending completion of I/O operation was a waste of precious machine cycles
Higher throughput is achieved if CPU and I/O of 2 or more programs were overlapped
How to overlap execution of multiple programs?
  use multiprogramming
How to protect programs from one another in a multiprogramming environment?
  use a bound register
CPU
CPU
CPU
I/O
I/O
I/O

## Slide 9: Away With Absolute Addressing
In early (1950) machines only one program ran at any given time, with unrestricted access to the entire machine (RAM + I/O devices)
Addresses in a program were location-dependent
  they depended upon where the program was to be loaded in memory
  so when programmers wrote code, they had to have a pretty good idea where in memory they should load the program
  but it was more convenient for programmers to write location-independent programs
How to achieve location-independence?
  a base register was used to support re-locatable code

## Slide 10: Base & Bound Registers
Base & bound registers loaded from the process table when the program is context-switched
Permits multiple memory-resident concurrent programs
Protects programs from one another

## Slide 11: Program Size
Program is copied from disk storage to main memory by the operating system
  program counter is then set to the beginning of the program
What if program is too big?
  original DOS would not let you run
MIPS64 address space is:
264 = 16 x 1018 =16,000 petabytes (peta = 1015)
This is several orders of magnitude larger than
any realistic memory device .

## Slide 12: Virtual Memory
Address translation
Program “sees” entire VM address space
Program is run in physical memory which is typically smaller than the address space
Pages of address space are swapped in/out of disk storage as needed
Strictly speaking VM is required to overcome limitation on the size of physical memory
  but VM is extended in a natural way to support multiprogramming & memory protection
  There are machines where the physical memory space is larger than the virtual memory space (e.g., PDP-11)
Disk
Physical memory
Virtual memory
Address
translation

## Slide 13: Advantages of Virtual Memory
Translation
  program has a consistent view of a contiguous memory, even though physical memory is scrambled
  Allows multi-programming
  relocation: allows the same program to run in any location in physical memory
Protection
  different processes are protected from each other
  different pages can have different behavior (read-only; user/supervisor)
    kernel code/data protected from user programs
Sharing
  can map same physical memory to multiple processes (shared memory)

## Slide 14: How VM Works
On program startup
  OS loads as much of the program as possible into RAM; this includes enough code to start execution
  if program size exceeds allocated RAM space the remainder is maintained on disk
During execution
  if program needs a code segment not resident in RAM, it fetches the segment from disk into RAM
  if there is not enough room in RAM, some resident pages must be evicted to make room
  if evicted pages are “dirty”, they must be updated on disk

## Slide 15: Address Translation

## Slide 16: VA-to-PA Address Translation
Processor
0x00
0x04
0x04
0x00
0x08
0x12
0x12
Disk
Lw R1, 0(R4)
add R1, R2, R4
Sub R5, R2, R1
BNEZ R5, 0x64
0x00
0x04
0x08
0x12
Disk
Virtual
address
VA
PA
Main memory
Programs use virtual addresses (VA) for data & instructions
VA translated to physical addresses (PA) using the Page Table
Instruction/data fetched/updated in memory
Page table

## Slide 17: Page Table
Virtual page number
Page offset
0
11
12
31
Physical page number
Page offset
0
11
12
23
Page table
Memory organized in pages (similar to blocks in cache)
Page size is 4-8 Kbytes
Virtual address
Physical address

## Slide 18: VA to PA Translation
Page offset
Virtual address space
Physical address space
Page frame
Virtual page number
Page offset
0
11
12
63
Page table maps the base address of virtual and physical page frames
Page offset need not be used in VA=>PA translation because virtual and physical block sizes are the same
Page
Table
Page offset

## Slide 19: Multiprogramming View of VM
VA 1
VA 1
VA 1
Program 1
Program 2
Program 3
Page Table 1
1
2
3
Page Table 2
1
2
3
4
Page Table 3
1
2
3
4
Physical Memory
Each application has a separate page table
Page table contains an entry for each user page
Page table base pointer maintained by OS for each process
Page table
base pointer 3
Page table
base pointer 2
Page table
base pointer 1

## Slide 20: Page Table Structure
0x00000
0x00001
0x00002
0x00003
0x00004
0x00005
0x00006
0x00007
V
Physical page number
0xFFFFF
.
.
.
.
.
.
.
.
.
0
11
12
31
Page offset
Virtual page number
0
11
12
23
Page offset <=> page size
12 bits: 4096 bytes
Virtual page number <=> page table size
20 bits: ~1 million
Physical address

## Slide 21: Determining Page Table Size
Assume
  32-bit virtual address
  30-bit physical address
  4 KB pages => 12 bit page offset
  Each page table entry is one word (4 bytes)
How large is the page table?
  Virtual page number = 32 - 12 = 20 bits
  Number of entries = number of pages = 2^20
  Total size = number of entries x bytes/entry
  = 2^20 x 4 = 4 Mbytes
  Each process running needs its own page table

## Slide 22: Page Fault
How is it known whether the page is in memory?
  Maintain a valid bit per page table entry
  valid bit is set to INVALID if the page is not in memory
  valid bit is set to VALID if the page is in memory
Page fault occurs when a page is not in memory
  fault results in OS fetching the page from disk into DRAM
  if DRAM is full, OS must evict a page (victim) to make room
  if victim is dirty OS updates the page on disk before fetch
  OS changes page table to reflect turnover
After a page fault and page-fetching, execution resumes at the instruction which caused the fault

## Slide 23: Page Faults (like “Cache Misses”)
CPU
Memory
Page Table
Disk
Virtual
Addresses
Physical
Addresses
CPU
Memory
Page Table
Disk
Virtual
Addresses
Physical
Addresses
Before fault
After fault

## Slide 24: Page Fault Handling
Processor Signals Controller
  Read block of length P starting at disk address X and store starting at memory address Y
Read Occurs
  Direct Memory Access (DMA)
  Under control of I/O controller
I / O Controller Signals Completion
  Interrupt processor
  OS resumes suspended process
disk
Disk
disk
Disk
Memory-I/O bus
Processor
Cache
Memory
I/O
controller
Reg
(2) DMA Transfer
(1) Initiate Block Read
(3) Read Done

## Slide 25: Page Fault Handling
User program runs
Page fault
OS requests page
Disk read
Another user program runs
Disk interrupt
OS installs page
User program resumes

## Slide 26: Accelerating Virtual Memory Operations

## Slide 27: Virtual Memory Hardware
Protection via virtual memory
  Keeps processes in their own memory space
Role of architecture:
  Provide user mode and supervisor mode
  Protect certain aspects of CPU state
  Provide mechanisms for switching between user mode and supervisor mode
  Provide mechanisms to limit memory accesses
  Provide TLB to accelerate the address translation

## Slide 28: VM => PM Translation
Each program memory reference requires two memory accesses: one for VM => PM mapping and one for actual data/instruction
  must make page table lookup as fast as possible
Page table too big to keep in fast memory (SRAM) in its entirety
  store page table in main memory
  cache a portion of the page table in TLB (Translation Look-Aside Buffer)
Virtual page number
Page offset
0
11
12
31
Physical page number
Page offset
0
11
12
24
Page table
Virtual address
Physical address

## Slide 29: Virtual Addressing with a Cache
Thus it takes an extra memory access to translate a VA to a PA
CPU
Trans-
lation
Cache
Main
Memory
VA
PA
miss
hit
data
This makes memory (cache) accesses very expensive (if every access was really two accesses)
Translation Lookaside Buffer (TLB) keeps track of recently used address mappings to avoid having to do a page table lookup

## Slide 30: Speeding Up Address Translation: Translation Lookaside Buffer (TLB)
TLB: A small and fast on-chip memory structure used for address translations.
If a virtual address is found in TLB (a TLB hit), the page table in main memory is not accessed.
1
1
1
1
0
1
1
0
1
1
0
1
1
1
1
1
0
1
Physical Memory
Disk Storage
TLB (on-chip)
128-256 Entries
Physical Page
Address
Virtual Page
Number
Page Table
(in main memory)
Physical Page
or Disk Address
Tag
Valid
Valid
128-256
TLB Entries

## Slide 31: Translation Look-Aside Table (TLB)
Processor
TLB
Memory
TLB maintains a list of most-recently used pages
Similar to instruction & data cache
  virtual address is used to index into the TLB
  TLB entry contains physical address
  takes ~ 1 clock cycle
What if VM=>PM lookup and data/instruction lookup takes more than 1 clock cycle?
  To avoid TLB lookup, remember the last VM => PM translation
  if same page is referenced, TLB lookup can be avoided

## Slide 32: TLB / Cache Interaction
V
a
l
i
d
T
a
g
D
a
t
a
P
a
g
e
o
f
f
s
e
t
P
a
g
e
o
f
f
s
e
t
V
i
r
t
u
a
l
p
a
g
e
n
u
m
b
e
r
V
i
r
t
u
a
l
a
d
d
r
e
s
s
P
h
y
s
i
c
a
l
p
a
g
e
n
u
m
b
e
r
V
a
l
i
d
1
2
2
0
2
0
1
6
1
4
C
a
c
h
e
i
n
d
e
x
3
2
C
a
c
h
e
D
a
t
a
C
a
c
h
e
h
i
t
2
B
y
t
e
o
f
f
s
e
t
D
i
r
t
y
T
a
g
T
L
B
h
i
t
P
h
y
s
i
c
a
l
p
a
g
e
n
u
m
b
e
r
P
h
y
s
i
c
a
l
a
d
d
r
e
s
s
t
a
g
T
L
B
P
h
y
s
i
c
a
l
a
d
d
r
e
s
s
3
1
3
0
2
9
1
5
1
4
1
3
1
2
1
1
1
0
9
8
3
2
1
0

## Slide 33
Just like any other cache, the TLB can be organized as fully associative, set associative, or direct mapped
TLBs are usually small, typically not more than 128 - 256 entries even on high end machines. This permits fully associative lookup on these machines. Most mid-range machines use small n-way set associative organizations.
CPU
TLB
Lookup
Cache
Main
Memory
VA
PA
miss
hit
data
Trans-
lation
hit
miss
20 t
t
1/2 t
Translation
with a TLB
Techniques for Fast Address Translation

## Slide 34: TLB and Context Switch
In multi-programming we need to use TLB for the active process
  What to do with TLB at context switch?
Too costly to clear TLB on every context switch
Keep track of PTE in TLB per process using ASID

## Slide 35: TLB Organization
TLB is typically a fully-associative cache (why?)
Additional info per page
  Dirty: page modified (if the page is swapped out, should the disk copy be updated?)
  Valid: TLB entry valid
  Used: Recently used or not (for selecting a page for eviction)
  Access: Read/Write
  ASID:Address Space ID
Tag

## Slide 36: Example

## Slide 37: Part a

## Slide 38: Part b

## Slide 39: Part c

## Slide 40: Cache, Virtual Memory and Virtual Machines

## Slide 41: Cache and Virtual Memory
Which address to use to index to cache sets?
  Physical address? May be slow due to translation
  Virtual? Protection, process switching, aliasing
How to make a virtual cache work?
  Page coloring
Get the best of both: virtually indexed, physically tagged cache

## Slide 42: Cache vs. Virtual Memory
Concept behind VM is almost identical to concept behind cache.
But different terminology
  Cache: Block VM: Page
  Cache: Cache Miss VM: Page Fault
Caches implemented completely in hardware. VM implemented in software, with hardware support from the processor.
Cache speeds up main memory access, while main memory speeds up VM access.

## Slide 43: VM & Caching Comparison
CPU
Cache
Main
Memory
Caching
CPU
Main
Memory
Virtual Memory
Disk

## Slide 44: Impact of These Properties on Design
Comparing to cache, how would we set the following design parameters?
  block size?
    Large, since disks perform better at transferring large blocks
  Associativity?
    High, to minimize miss rate
  Write through or write back?
    Write back, since can’t afford to perform small writes to disk
What would the impact of these choices be on:
  miss rate
    Extremely low. << 1%
  hit time
    Must match cache/DRAM performance
  miss latency (penalty)
    Very high. ~20ms

## Slide 45: Associativity of VM
Cache miss penalty: 8-150 clock cycles
VM miss penalty: 1,000,000 - 10,000,000 clock cycles
Because of the high miss penalty, VM design minimizes miss rate by allowing full associativity for page placement

## Slide 46: Write Strategies
Disk I/O slow (millions of clock cycles)
Always write-back; never write-through
Use dirty bit to decide whether to write disk before eviction
Smart disk controllers buffers writes
  copy replaced page in buffer
  read new page into main memory
  write from buffer to disk

## Slide 47: Virtual Machines
Supports isolation and security
Sharing a computer among many unrelated users
Enabled by raw speed of processors, making the overhead more acceptable
Allows different ISAs and operating systems to be presented to user programs
  “System Virtual Machines”
  SVM software is called “virtual machine monitor” or “hypervisor”
  Individual virtual machines run under the monitor are called “guest VMs”

## Slide 48: Impact of VMs on Virtual Memory
Each guest OS maintains its own set of page tables
  VMM adds a level of memory between physical and virtual memory called “real memory”
  VMM maintains shadow page table that maps guest virtual addresses to physical addresses
    Requires VMM to detect guest’s changes to its own page table
    Occurs naturally if accessing the page table pointer is a privileged operation