## Slide 1: Multiprocessor
COMP4611
Tutorial 11
Nov. 26 – 30, 2012

## Slide 2: Outline
Why Multiprocessor?
Performance Potential
New Problems
  Cache Coherence Problem & Solution
Challenges of Parallel Processing

## Slide 3: The Bottleneck of Single Processor
Even various ways of increasing a single processor performance have been introduced, the performance of a single processor still has its bottleneck.
The figures above demonstrate the limitation of ILP.

## Slide 4: We Need High Performance
  Less time for a time-consuming operation
More operations in a period of time
10 MB
100 MB
1 GB
10 GB
100 GB
1 TB
100 MFLOPS
1 GFLOPS
10 GFLOPS
100 GFLOPS
1 TFLOPS
2D airfoil
48-hour
weather
oil reservoir
modelling
3D plasma modelling
72-hour
weather
vehicle dynamics
chemical dynamics
pharmaceutical design
structural biology
Computational Performance Requirements
Storage Requirements

## Slide 5: Multiprocessing
Concurrent execution of tasks (programs) using multiple computing, memory and interconnection resources
  Provide alternative to faster processors
  Use multiple processors to solve a problem

## Slide 6: Outline
Why Multiprocessor?
Performance Potential
New Problems
  Cache Coherence Problem & Solution
Challenges in Using Multiprocessors

## Slide 7: Performance Potential Using Multiprocessor
Amdahl’s Law
  Using multiple processors to solve the same problems as the single processor
  Pessimistic, limited speedup factor
Gustafson’s View
  Using multiple processors to solve larger or more complex problems
  Parallel portion increases as the problem size increases
  Speedup factor can be increased by deploying more processors

## Slide 8: Amdahl’s Law
A parallel program has sequential parts and parallel parts, the proportion for both of them are  and (1-)
  The total execution time for a single processer is
    T1 = T1 + (1-)T1
  The total execution time for p processors would be
    Tp = T1 + (1-)T1 / p
Speedup(p) = 1 / ( + (1-)/p)  1 / 

## Slide 9: Amdahl’s Law
  S is the serial part
  P is the part that can be parallelized in 6 ways
  Serial: SSPPPPPP
  6 processors: SSP
  P
  P
  P
  P
  P
  Speedup = 8/3 = 2.67
Speedup(p) = 1 / ( + (1- )/p)
As p  , Speedup(p)  1/ 

## Slide 10
10%
20%
30%
40%
50%
60%
70%
80%
90%
99%
0
5
10
15
20
25
Speedup
% Serial
1000 CPUs
16 CPUs
4 CPUs
Amdahl’s Law
Limited speedup factor!!!

## Slide 11: Gustafson’s View
  Parallel portion increases as the problem size increases
  Old Serial: SSPPPPPP
  Hypothetical Serial: SSPPPPPP PPPPPP PPPPPP PPPPPP PPPPPP PPPPPP
  6 processors: SSPPPPPP
  PPPPPP
  PPPPPP
  PPPPPP
  PPPPPP
  PPPPPP
  Speedup(6) = (8+5*6)/8 = 4.75
  Speedup(p) = p(1- ) + ; Speedup(p) p    

## Slide 12
0
20
40
60
80
100
10%
20%
30%
40%
50%
60%
70%
80%
90%
99%
% Serial
Speedup
Gustafson
Amdhal
Amdahl vs. Gustafson

## Slide 13
Example 1. To achieve a speedup of 80 with 100 processors, the fraction of the original computation can be sequential
Amdahl’s law
  1 / ( + (1- )/100) = 80
   = 0.25%
Gustafson’s view
  100(1- ) +  = 80
   =20%
In practice, programs usually have much more sequential fraction
To achieve high speedup, only a very small fraction of a program can be sequential

## Slide 14: Outline
Why Multiprocessor?
Performance Potential
New Problems
  Cache Coherence Problem & Solution
Challenges in Using Multiprocessors

## Slide 15: Programming with Shared Memory
Process
Process
System
X
load(X)
store(X)
Processor
Memory
Shared variable
Virtual address spaces for a collection of processes communicating via shared addresses
Machine physical address space
Shared portion of address space
Private portion of address space
Pn private
Common physical addresses
P2 private
P1 private
P0 private
Load
Store

## Slide 16: Cache Coherence Problem
16
Processor P4 does not see the value written by processor P1
X:42
R: X
$
MEM
P1
$
P2
$
P3
$
P4
X:42
X:17
W: X = 17
R: X
X:42

## Slide 17: Write Through Does Not Help
17
Processor P4 sees 42 in cache and does not get the value (17) from memory.
X:42
R: X
$
MEM
P1
$
P2
$
P3
$
P4
X:42
X:17
W: X = 17
R: X
X:42
X:17
R: X

## Slide 18: Some Solutions to Cache Coherence Problem
Shared Cache
  Cache placement identical to single cache
  Only one copy of any cached block which results in limited bandwidth
Snoopy Cache-Coherence Protocols for Distributed Cache

## Slide 19: Snooping Cache Coherency
19
Cache Controller “snoops” all transactions on the shared bus and takes action to ensure coherence (invalidate, update, or supply value)
A transaction is a relevant transaction if it involves a cache block currently contained in this cache
Bus snoop
Cache-memory
transaction

## Slide 20
Hardware Cache Coherence Demonstration
write-invalidate
X -> X’
invalidate -->
X -> Inv
X -> Inv
. . . . .
memory
X -> X’
update -->
X -> X’
X -> X’
. . . . .
memory
write-update (also called distributed write)

## Slide 21: Outline
Why Multiprocessor?
Performance Potential
New Problems
  Cache Coherence Problem & Solution
Challenges in Using Multiprocessors

## Slide 22: Challenges in Using Multiprocessors
Limited parallelism available in programs
  Example 1
Relatively high cost of communications
  Example 2

## Slide 23
Example 2
We have a 32-processor multiprocessor
  Clock rate is 3.3 GHz
  Base CPI is 0.5 (no remote request)
  Shared memory - nonuniform memory access
  200 ns to handle a remote memory reference
  A processor is stalled when it invokes a remote memory access
How much slower if 0.2% of the instructions involve remote requests?

## Slide 24
Effective CPI
  = Base CPI + Remote req. rate x Remote req. cost
  = 0.5 + 0.2% x Remote req. cost
Remote req. cost
  = Remote access cost / cycle time
  = 200 ns / (1/3.3) ns = 660 cycles
CPI = 0.5 + 0.2% x 660 = 1.8
CPI / Base CPI = 1.8 / 0.5 = 3.6
0.2% remote requests make the program 3.6 times slower

## Slide 25
Questions?