## Slide 1: Vector, SIMD Extensions and GPU
COMP 4611
Tutorial 12

## Slide 2: Introduction
SIMD architectures can exploit significant data-level parallelism for:
  Matrix-oriented scientific computing
  Media-oriented image and sound processors
SIMD can be more energy efficient than MIMD
  Only needs to fetch one instruction per data operation
  Makes SIMD attractive for personal mobile devices
SIMD allows programmer to continue to think sequentially
Introduction

## Slide 3: SIMD Parallelism
Vector architectures
SIMD extensions
Graphics Processor Units (GPUs)
For x86 processors:
  In the previous decade, roughly
    Two additional cores per chip per year
    SIMD width doubles every four years
  If the rates are the similar in the next decade
    Potential speedup from SIMD to be twice that from MIMD
Introduction
Notes: 12 years:
MIMD: 16 -> 16+2*12 = 40 (2.5)
SIMD: 8 - > 8 * 2 * 2 * 2 = 64 (8)

## Slide 4: Vector Architectures
Basic idea:
  Read sets of data elements into “vector registers”
  Operate on those registers
    A single instruction -> dozens of operations on independent data elements
  Disperse the results back into memory
Registers are controlled by compiler
  Used to hide memory latency
  Leverage memory bandwidth
Vector Architectures

## Slide 5: VMIPS
Example architecture: VMIPS
  Loosely based on Cray-1
  Vector registers
    Each register holds a 64-element, 64 bits/element vector
    Register file has 16 read ports and 8 write ports
  Vector functional units
    Fully pipelined
    Data and control hazards are detected
  Vector load-store unit
    Fully pipelined
    One word per clock cycle after initial latency
  Scalar registers
    32 general-purpose registers
    32 floating-point registers
Vector Architectures

## Slide 6: VMIPS Instructions
ADDVV.D: add two vectors
MULVS.D: multiply each element of a vector by a scalar
LV/SV: vector load and vector store from address
Example: DAXPY
  Y = a x X + Y, X and Y are vectors, a is a scalar
  L.D F0,a ; load scalar a
  LV V1,Rx ; load vector X
  MULVS.D V2,V1,F0 ; vector-scalar multiply
  LV V3,Ry ; load vector Y
  ADDVV V4,V2,V3 ; add
  SV Ry,V4 ; store the result
Requires 6 instructions vs. almost 600 for MIPS
Vector Architectures

## Slide 7: Vector Execution Time
Execution time depends on three factors:
  Length of operand vectors
  Structural hazards
  Data dependencies
VMIPS functional units consume one element per clock cycle
  Execution time is approximately the vector length
Convoy
  Set of vector instructions that could potentially execute together
Vector Architectures

## Slide 8: Chimes
Sequences with read-after-write dependency hazards can be in the same convoy via chaining
Chaining
  Allows a vector operation to start as soon as the individual elements of its vector source operand become available
Chime
  Unit of time to execute one convoy
  m convoys executes in m chimes
  For vector length of n, requires m x n clock cycles
Vector Architectures

## Slide 9: Example
LV V1,Rx ;load vector X
MULVS.D V2,V1,F0 ;vector-scalar multiply
LV V3,Ry ;load vector Y
ADDVV.D V4,V2,V3 ;add two vectors
SV Ry,V4 ;store the sum
Convoys:
1 LV MULVS.D
2 LV ADDVV.D
3 SV
3 chimes, 2 FP ops per result, cycles per FLOP = 1.5
For 64 element vectors, requires 64 x 3 = 192 clock cycles
Vector Architectures

## Slide 10: Challenges
Start up time
  Latency of vector functional unit
  Assume the same as Cray-1
    Floating-point add => 6 clock cycles
    Floating-point multiply => 7 clock cycles
    Floating-point divide => 20 clock cycles
    Vector load => 12 clock cycles
Improvements:
  > 1 element per clock cycle
  IF statements in vector code
  Non-64 wide vectors
  Memory system optimizations to support vector processors
  Multiple dimensional matrices
  Sparse matrices
  Programming a vector computer
Vector Architectures

## Slide 11: Multiple Lanes
Element n of vector register A is “hardwired” to element n of vector register B
  Allows for multiple hardware lanes
Vector Architectures

## Slide 12: Vector Mask Registers
Consider:
for (i = 0; i < 64; i=i+1)
if (X[i] != 0)
X[i] = X[i] – Y[i];
Use vector mask register to “disable” elements:
LV V1,Rx ;load vector X into V1
LV V2,Ry ;load vector Y
L.D F0,#0 ;load FP zero into F0
SNEVS.D V1,F0 ;sets VM(i) to 1 if V1(i)!=F0
SUBVV.D V1,V1,V2 ;subtract under vector mask
SV Rx,V1 ;store the result in X
Compilers manipulate mask registers explicitly
Vector Architectures

## Slide 13: SIMD Extensions
Media applications operate on data types narrower than the native word size
  Example: disconnect carry chains to “partition” 64-bit adder --> eight 8-bit elements
Limitations, compared to vector instructions:
  Number of data operands encoded into op code
  No sophisticated addressing modes
  No mask registers
SIMD Instruction Set Extensions for Multimedia

## Slide 14: SIMD Implementations
Implementations:
  Intel MMX (1996)
    Eight 8-bit integer ops or four 16-bit integer ops
  Streaming SIMD Extensions (SSE) (1999)
    Eight 16-bit integer ops
    Four 32-bit integer/fp ops or two 64-bit integer/fp ops
  Advanced Vector Extensions (2010)
    Four 64-bit integer/fp ops
SIMD Instruction Set Extensions for Multimedia

## Slide 15: Graphical Processing Units
Given the hardware invested to do graphics well,
how can we supplement it to improve performance of a wider range of applications?
Graphical Processing Units

## Slide 16: GPU Accelerated or Many-core Computation
NVIDIA GPU
  Reliable performance, communication between CPU and GPU using the PCIE channels
  Tesla M2090
    512 CUDA cores (16 Streaming Multiprocessor x 32 cores/SM )
    1331 GFLOPs (single precision)
    6GB memory with 177GB/sec bandwidth
Notes: http://www.nvidia.com/object/tesla-servers.html

## Slide 17: GPU Accelerated or Many-core Computation (cont.)
APU (Accelerated Processing Unit) – AMD
  CPU and GPU functionality on a single chip
  AMD FirePro A320
    4 CPU cores and 384 GPU processors
    736 GFLOPs (single precision) @ 100W
    Up to 2GB dedicated memory
Notes: http://www.amd.com/us/products/workstation/graphics/ati-firepro-3d/APU/Pages/APU.aspx#4

## Slide 18: GPU Accelerated or Many-core Computation (cont.)
MIC (Many Integrated Core) – Intel
  Many CPU cores on a single chip
  Intel Xeon Phi Coprocessor 5110P
    60 cores/1.053 GHz/240 threads
    8 GB memory and 320 GB/s bandwidth
    829 GFLOPs (double precision) @ 195W (Intel Xeon Phi coprocessor SE10P)
Easier programming, lower power consumption, and better integration of the CPU and GPU capabilities
Notes: http://www.intel.com/content/www/us/en/processors/xeon/xeon-phi-detail.html

## Slide 19: Programming the NVIDIA GPU
Heterogeneous execution model
  CPU is the host, GPU is the device
Develop a programming language (CUDA) for GPU
Unify all forms of GPU parallelism as CUDA thread
Programming model is “Single Instruction Multiple Thread”
Graphical Processing Units
We use NVIDIA GPU as the example for discussion

## Slide 20: Fermi GPU
One Stream Processor (SM)
Notes: Fermi’s 16 SM are positioned around a common L2 cache. Each SM is a vertical rectangular strip that contain an orange portion (scheduler and dispatch), a green portion (execution units), and light blue portions (register file and L1 cache).
Figure from: http://www.nvidia.com/content/PDF/fermi_white_papers/NVIDIA_Fermi_Compute_Architecture_Whitepaper.pdf

## Slide 21: NVIDIA GPU Memory Structures
Each SIMD Lane has private section of off-chip DRAM
  “Private memory”
Each multithreaded SIMD processor also has local memory
  Shared by SIMD lanes
Memory shared by SIMD processors is GPU Memory
  Host can read and write GPU memory
Graphical Processing Units

## Slide 22: Fermi Multithreaded SIMD Proc.
Graphical Processing Units
Each Streaming Processor (SM)
  32 SIMD lanes
  16 load/store units
  32,768 registers
Each SIMD thread has up to
  64 vector registers of 32 32-bit elements

## Slide 23: GPU Compared to Vector
Similarities to vector machines:
  Works well with data-level parallel problems
  Mask registers
  Large register files
Differences:
  No scalar processor
  Uses multithreading to hide memory latency
  Has many functional units, as opposed to a few deeply pipelined units like a vector processor
Graphical Processing Units

## Slide 24: http://www.nvidia.com/object/fermi-architecture.html
Introduction to Fermi from NVIDIA

## Slide 25: Questions?