## Slide 1: Project Tutorial
COMP4611 Tutorial 7
Oct 29th-Nov 2nd

## Slide 2: Outline
Objectives
Project Task I
  Task description
Project Task II
  Task description
  Skeleton code
Project Task III
  Task description
Deliverables
Submission & Grading

## Slide 3: Objectives
To have hands-on experiments with the branch prediction using SimpleScalar
To design your own branch predictor for higher prediction accuracy

## Slide 4: Background
Branch predictor types in SimpleScalar (alpha)
  Taken or not-taken
  Perfect predictor
  2-bit predictor
  2-level adaptive predictor
Specifying the branch predictor type
  Option: -bpred <type>
  <type>: nottaken, taken, perfect, bimod, 2lev

## Slide 5: Background
Configuring taken/nottaken predictor
  Option: -bpred taken, -bpred nottaken
  Command line example for “-bpred taken”:
  ./sim-bpred -bpred taken benchmarks/cc1.alpha -O benchmarks/1stmt.1
  Command line example for “-bpred nottaken”:
  ./sim-bpred -bpred nottaken benchmarks/cc1.alpha -O benchmarks/1stmt.i

## Slide 6: Simulating Not-Taken Predictor
  Branch prediction accuracy:
  bpred_dir_rate =

## Slide 7: Background
Configuring 2-bit predictor
  -bpred:bimod <size>
  <size>: the size of direct-mapped branch target buffer (BTB)
  Command line example:
  ./sim-bpred -bpred:bimod 2048 benchmarks/cc1.alpha -O benchmarks/1stmt.i
Predict: Taken
Predict: Not Taken
T
NT
11
10
00
NT
NT
NT
T
T
T
01

## Slide 8: Project Task I
Evaluation of 2-bit dynamic branch predictor
  Varied number of table entries (512, 1024, 2048)
  Benchmark: Go (Alpha)
  Configuration parameters for Go: 2 17
  Input file for Go: 2stone9.in
  Branch prediction accuracy (bpred_dir_rate) and command lines to be included in the project report
  Command line example:
  ./sim-bpred -redir:prog results/go-2bit-512-2-17.progout -redir:sim results/go-2bit-512-2-17.simout -bpred:bimod 512 benchmarks/go.alpha 2 17 benchmarks/2stone9.in

## Slide 9: Project Task II
Write a 3-bit branch predictor on SimpleScalar
  Implementation
  Evaluation
Guideline
  Skeleton code at http://course.cse.ust.hk/comp4611/comp4611_project.tar.gz
  Extract the package and compile it by typing “make config-alpha” and then “make”
  Fill in the missing code in bpred.c and recompile

## Slide 10: Code Glimpse
Source code that implements the branch predictor is in simplesim-3.0/
  sim-bpred.c: simulating a program with configured branch prediction instance
  brpred.c: implementing the logic of several branch predictors
  brpred.h: defining the structure of several branch predictors
  main.c: simulating a program on SimpleScalar

## Slide 11: Code Glimpse
bpred.h
  bpred_class: branch predictor types
  bpred_t: branch predictor structure
  bpred_dir_t: branch direction structure
  bpred_update_t: branch state update structure (containing predictor state counter)
  bpred_btb_ent_t: entry structure in a BTB

## Slide 12: Code Glimpse
Predictor’s state counter
struct bpred_update_t {
char *pdir1; /* direction-1 predictor counter */
char *pdir2; /* direction-2 predictor counter */
char *pmeta; /* meta predictor counter */
struct { /* predicted directions */
unsigned int ras : 1; /* RAS used */
unsigned int bimod : 1; /* bimodal predictor */
unsigned int twolev : 1; /* 2-level predictor */
unsigned int meta : 1; /* meta predictor (0..bimod / 1..2lev) */
} dir;
};

## Slide 13: Code Glimpse
bpred.c
  bpred_create: create a new branch predictor instance
  bpred_dir_create: create a branch direction instance
  bpred_lookup: predict a branch target
  bpred_dir_lookup: predict a branch direction
  bpred_update: update an entry in BTB

## Slide 14: Code Glimpse
Workflow of branch prediction
main
sim_check_options
bpred_create
bpred_dir_create
allocate BTB
sim_main
bpred_lookup
bpred_update
pred->dir_hits
*dir_update_ptr->pdir1

## Slide 15: 3-bit Branch Predictor
  A 3-bit branch predictor has 8 states in total
111
110
101
001
010
011
NT
NT
NT
NT
T
T
NT
T
T
T
000
NT
T
100
NT
T
NT
T
Predict Taken
Predict Not Taken

## Slide 16: Implementation
Configuring 3-bit predictor
  -bpred:tribit <size>
  <size>: the size of direct-mapped BTB
  Command line example:
  ./sim-bpred -v -redir:prog results/go-3bit-2048-2-17.progout -redir:sim results/go-3bit-2048-2-17.simout -bpred:tribit 2048 benchmarks/go.alpha 2 17 benchmarks/5stone21.in
  Command must include verbose option –v

## Slide 17: Skeleton Code
branch_lookup() in bpred.c
/* comp4611 3-bit predict saturating cntr pred (dir mapped) */
if (pbtb == NULL) {
if (pred->class != BPred3bit) {
return ((*(dir_update_ptr->pdir1) >= 2)? /* taken */ 1 : /* not taken */ 0);
}
else {
// code to be filled in here
}
}
else {
……
}
/************************************************************/

## Slide 18: Skeleton Code
branch_update() in bpred.c
/* comp4611 3-bit predict saturating cntr pred (dir mapped) */
if (dir_update_ptr->pdir1) {
if (pred->class != BPred3bit) {
…….
}
else {
if (taken) {
// code to be filled in here
}
else { /* not taken */
// code to be filled in here
}
}
}
/****************************************************/

## Slide 19: Evaluation
  3-bit predictor with the table size as 2048
  Benchmark: Go (Alpha)
  Parameters for Go: 2 17
  Input file for Go: 2stone9.in
  Branch prediction accuracy and command line to be included in the project report
  Output trace files (include option –v)
    are the redirected program and simulation output
    should be saved in the “results” directory
    are as large as a few GBs and make sure you have sufficient disk storage for them in your PC

## Slide 20: Project Task III
Design and implement your own predictor
  Use existing predictors (e.g. 2-level) or create your own predictor to achieve higher accuracy than the 2-bit predictor
  Evaluate your predictor using Go (Alpha)
  Parameters for Go: 2 17
  Input file for Go: 2stone9.in
  Branch prediction accuracy and command line to be included in the project report
  Output trace files (include option –v)
    are the redirected program and simulation output
    should be saved in the “results” directory
    are as large as a few GBs and make sure you have sufficient disk storage for them in your PC

## Slide 21: Deliverables
  Source code
  Code for 3-bit predictor: bpred.c, saved as “3bit/bpred.c”
  Code for your own predictor: including bpred.h, bpred.c, sim-bpred.c, readme (specify your command line format) and other relevant files, saved under “own/”
  To be submitted to CASS
  Output trace files
  Output trace files for 3-bit predictor
  Output trace files for your own predictor
  To be submitted separately (not CASS)
Project report (no longer than 2 pages)
  Evaluation result (2-bit, 3-bit, your own predictor)
  Description of your own predictor
  To be submitted to CASS

## Slide 22: Grading Scheme
  2-bit predictor (20%)
  Correctness
  3-bit predictor (40%)
  Correctness
  Your own predictor (30%)
  If correct, score = max{0, (prediction accuracy – 0.85) * 200}
Project report (10%)
  Completeness
  Correctness
  Clarity

## Slide 23: Submission Guideline
Submit your source code and report to CASS
  Report should contain your group ID, each group member’s name, UST ID, email on the first page
  Package the code and report files in one zip file as “comp4611_project_groupID.zip”
  Deadline: Nov 30, 2012
Submit the hardcopy of your report to the homework box
  Report should contain your group ID, each group member’s name, UST ID, email on the first page
  Deadline: Nov 30, 2012
Submission of your output trace files will be informed later

## Slide 24: References
SimpleScalar LLC: www.simplescalar.com
Introduction to SimpleScalar: www.ecs.umass.edu/ece/koren/architecture/Simplescalar/SimpleScalar_introduction.htm
SimpleScalar Tool Set: http://www.ece.uah.edu/~lacasa/tutorials/ss/ss.htm

## Slide 25: Appendix
Branch direction structure
struct bpred_dir_t {
enum bpred_class class; /* type of predictor */
union {
struct {
unsigned int size; /* number of entries in direct-mapped table */
unsigned char *table; /* prediction state table */
} bimod;
……
} config;
};

## Slide 26: Appendix
sim-bpred.c
  sim_main: execute each conditional branch instruction
  sim_reg_options: register command options
  sim_check_options: determine branch predictor type and create a branch predictor instance
  pred_type: define the type of branch predictor
  *_nelt & *_config[]: configure the parameters for each branch predictor

## Slide 27: Appendix
sim_main() in sim-bpred.c
if (MD_OP_FLAGS(op) & F_CTRL) {
if (pred) {
pred_PC = bpred_lookup(pred, …, &update_rec, …);
if (!pred_PC) {
pred_PC = regs.regs_PC + sizeof(md_inst_t);
}
bpred_update(pred, …, &update_rec, …);
}
}
……
regs.regs_PC = regs.regs_NPC;
regs.regs_NPC += sizeof(md_inst_t);

## Slide 28: Appendix
main() in main.c
sim_odb = opt_new(orphan_fn);
opt_reg_flag(sim_odb, …);
……
sim_reg_options(sim_odb);
opt_process_options(sim_odb, argc, argv);
……
sim_check_options(sim_odb, argc, argv);
……
sim_reg_stats(sim_sdb);
……
sim_main();
……