## Slide 1: COMP4611: Design and Analysis of Computer Architectures Instruction Set Architectures

## Slide 2: Instruction Set Architecture (ISA)
instruction set
software
hardware
In order to use the hardware of a computer, we must speak its language.
The words of a computer language are called instructions, and its vocabulary is called an instruction set.
Instruction set of a computer: the portion of the computer visible to the assembly level programmer or to the compiler writer.

## Slide 3: Instruction Set Architecture
Application
Instruction Set Architecture
Implementation
…SPARC MIPS ARM x86 HP-PA IA-64…
Intel Pentium X, Core 2
AMD K6, Athlon, Opteron
Transmeta Crusoe TM5x00

## Slide 4: Interface Design
A good interface
  lasts through many implementations (portability, compatibility)
  is used in many different ways (generality)
  provides convenient functionality to higher levels
  permits an efficient implementation at lower levels
Interface
imp 1
imp 2
imp 3
use
use
use
time

## Slide 5: Instruction Set Architecture
Strong influence on cost/performance
  Remember the Execution Time equation?
  ISA has a huge impact on programs and their performance!
New ISAs are rare, but new (extended) versions are not
  16-bit, 32-bit and 64-bit X86 versions
Longevity is a strong function of marketing prowess
CPU time = Seconds = Instructions x Cycles x Seconds
Program Program Instruction Cycle

## Slide 6: Instruction Set Architecture
What is an instruction set architecture?
  Specification of a set of instructions
  Each instruction is directly executed by the CPU hardware.
How is it represented?
  By a binary format, typically bits, bytes, words.
  Word size is typically 16, 32, 64 bits today.
  Length format options:
    Fixed – each instruction encoded in same size field
    Variable – half-word, whole word, multiple word instructions are possible

## Slide 7: Instruction Formats
Alpha (fixed length)
32 bits
6 bits
opcode
opcode
opcode
opcode
RA
RA
RA
RB
RB
RC
TRAP
Branch
Mem
Operate
x86 (variable length)
prefixes
opcode
addr mode
displ
imm
0 to 4 bytes of prefix
1 or 2 bytes of opcode
0 to 2 bytes (ModR/M and SIB)
0 to 8 bytes
VAX-11: 1—53 bytes

## Slide 8: Evolution of Instruction Sets
Single Accumulator (EDSAC 1950)
Accumulator + Index Registers
(Manchester Mark I, IBM 700 series 1953)
Separation of Programming Model
from Implementation
High-level Language Based
Concept of a Family
(B5000 1963)
(IBM 360 1964)
General Purpose Register Machines
Complex Instruction Sets
Load/Store Architecture
RISC
(Vax, Intel 432 1977-80)
(CDC 6600, Cray 1 1963-76)
(MIPS,Sparc,HP-PA,IBM RS6000,PowerPC 1987,AVR)
Mixed CISC & RISC?
(IA-64. . .1999)
CISC
(Intel x86 1980-199x)

## Slide 9: Basic ISA Classes
Accumulator:
  1 Address: add A (acc  acc + Mem[A]).
Stack:
  0 address: add (tos  tos + second of stack).
General Purpose Register (GPR):
  A fast register file (collection of registers)
  Operands of arithmetic operations are explicitly specified
    Operands can be memory locations or registers
  2 addresses: add A, B EA(A) EA(A)+EA(B)
  3 addresses: add A, B, C EA(A) EA(B)+EA(C)

## Slide 10: Basic ISA Classes
Classes of GPR computers
  Register-register, register-memory, memory-memory
Load/Store (register-register):
  ALU operations : No memory reference.
  3 addresses: add R1, R2, R3 R1  R2 + R3
  load R1, R2 R1 Mem[R2]
  store R1, R2 Mem[R1]  R2
Comparison: Bytes per Instruction? Number of Instructions? Cycles per instruction?

## Slide 11: Operand Locations in Four ISA Classes

## Slide 12: Comparison of ISA Classes
Code Sequence for C = A+B
  A, B, and C are variables stored in memory
Memory efficiency? Instruction access? Data access?
What’s the minimum number of instructions we need for a computer?

## Slide 13: What may an ISA want to provide?
Computers should use general purpose registers
Computer should use a load-store architecture
The number of instructions is not a limitation any more

## Slide 14: Addressing Modes
An important aspect of ISA design
  Has major impact on both the HW complexity and the instruction count
  HW complexity affects the CPI and the cycle time
Basically a set of mappings
  From address specified to address used
  Address used = effective address
  Effective address may go to memory or to register file
  Effective address generation is an important focus

## Slide 15: Typical Memory Addressing Modes
Register
Immediate
Displacement
Indirect
Indexed
Absolute
Memory indirect
Autoincrement
Autodecrement
Scaled
Regs [R4] ¬Regs[R4] + Regs[R3]
Regs[R4] ¬Regs[R4] + 3
Regs[R4] ¬Regs[R4]+Mem[10+Regs[R1]]
Regs[R4] ¬Regs[R4]+ Mem[Regs[R1]]
Regs [R3] ¬Regs[R3]+Mem[Regs[R1]+Regs[R2]]
Regs[R1] ¬Regs[R1] + Mem[1001]
Regs[R1] ¬Regs[R1] + Mem[Mem[Regs[R3]]]
Regs[R1] ¬Regs[R1] + Mem[Regs[R2]]
Regs[R2] ¬Regs[R2] + d
Regs [R2] ¬Regs[R2] -d
Regs{R1] ¬Regs[Regs[R1] +Mem[Regs[R2]]
Regs[R1] ¬Regs[R1] +
Mem[100+Regs[R2]+Regs[R3]*d]
Add R4, R3
Add R4, #3
Add R4, 10 (R1)
Add R4, (R1)
Add R3, (R1 + R2)
Add R1, (1001)
Add R1, @ (R3)
Add R1, (R2) +
Add R1, - (R2)
Add R1, 100 (R2) [R3]
Addressing Sample
Mode Instruction Meaning

## Slide 16: Utilization of Memory Addressing Modes

## Slide 17: Addressing Modes Usage Example
Displacement 42% avg, 32% to 55%
Immediate: 33% avg, 17% to 43%
Register deferred (indirect): 13% avg, 3% to 24%
Scaled: 7% avg, 0% to 16%
Memory indirect: 3% avg, 1% to 6%
Misc: 2% avg, 0% to 3%
75% displacement & immediate
88% displacement, immediate & register indirect.
Observation: In addition to Register direct, Displacement, Immediate, Register Indirect addressing modes are important.
For 3 programs running on VAX ignoring direct register mode:
75%
88%

## Slide 18: Displacement Address Size Example
Avg. of 5 SPECint programs vs. avg. 5 SPECfp programs
1% of addresses > 16-bits
12 - 16 bits of displacement needed
Displacement Address Bits Needed

## Slide 19: Immediate Addressing Mode
About one quarter of data transfers and ALU operations
have an immediate operand for SPEC CPU2000 programs.

## Slide 20: Immediate Addressing Mode
50% to 60% fit within 8 bits
75% to 80% fit within 16 bits
gcc
spice
Tex

## Slide 21: Addressing Mode Summary
Important data addressing modes
  Displacement
  Immediate
  Register Indirect
Displacement size should be 12 to 16 bits.
Immediate size should be 8 to 16 bits.

## Slide 22: Instruction Operations
Arithmetic and Logical:
  add, subtract, and , or, etc.
Data transfer:
  Load, Store, etc.
Control
  Jump, branch, call, return, trap, etc.
Synchronization:
  Test & Set.
String:
  string move, compare, search.

## Slide 23: Instruction Usage Example: Top 10 Intel X86 Instructions
Rank
Integer Average Percent total executed
1
2
3
4
5
6
7
8
9
10
instruction
load
conditional branch
compare
store
add
and
sub
move register-register
call
return
Total
Observation: Simple instructions dominate instruction usage frequency.
22%
20%
16%
12%
8%
6%
5%
4%
1%
1%
96%

## Slide 24: Instructions for Control Flow
Breakdown of control flow instructions into three classes: calls or returns,
jumps and conditional branches for SPEC CPU2000 programs.

## Slide 25: Conditional Branch Distance
Short displacement fields often sufficient for branch
PC-relative, since most branches from current PC address
  At least 8 bits.

## Slide 26: Conditional Branch Addressing
Compare Equal/Not Equal/Less than (or Equal) are important

## Slide 27: Data Type and Size of Operands
Byte, half word (16 bits), word (32 bits), double word (64 bits).
Arithmetic:
  Decimal: 4bit per digit.
  Integers: 2’s complement
    8 bits (C char), 16 bits (C int16_t, sometimes int, short), 32 bits (C int32_t, sometimes long), 64 bits (C int64_t, sometimes long long)
  Floating-point: IEEE standard
    Single precision: 32 bits (C float)
    Double precision: 64 bits (C double)
    Quadruple precision: 128 bits
    Extended precision: e.g., 80 bits

## Slide 28: Type and Size of Operands
Distribution of data accesses by size for SPEC CPU2000
benchmark programs

## Slide 29: Instruction Set Encoding
Considerations affecting instruction set encoding:
  To support registers and addressing modes provided
  The impact of the size of the register and addressing mode fields on the average instruction size and on the average program.
  To encode instructions into lengths that will be easy to handle in the implementation.
    Usually, the instruction length should be a multiple of bytes.

## Slide 30: Instruction Format
Fixed
  Operation, address specifier 1, address specifier 2, address specifier 3.
  MIPS, SPARC, Power PC.
Variable
  Operation & # of operands, address specifier1, …, specifier n.
  VAX
Hybrid
  Intel x86
  operation, address specifier, address field.
  operation, address specifier 1, address specifier 2, address field.
  operation, address field, address specifier 1, address specifier 2.
Summary:
  If code size is most important, use variable format.
  If performance is most important, use fixed format.

## Slide 31: Three Examples of Instruction Set Encoding
    Variable: VAX (1-53 bytes)
Operations &
no of operands
Address
specifier 1
Address
field 1
Address
specifier n
Address
field n
Operation
Address
field 1
Address
field 2
Address
field3
Fixed: DLX, MIPS, PowerPC, SPARC
Operation
Address
Specifier
Address
field
Operation
Address
Specifier 1
Address
Specifier 2
Address field
Operation
Address
Specifier
Address
field 1
Address
field 2
    Hybrid : IBM 360/370, Intel 80x86

## Slide 32
Endian-ness: byte ordering in multibyte data
Little Endian vs. Big Endian
Memory Address | +0 | +1 | +2 | +3 | 
Big Endian | Byte 0 | Byte 1 | Byte 2 | Byte 3 | MSB in the lowest (first) memory address
Little Endian | Byte 3 | Byte 2 | Byte 1 | Byte 0 | LSB in the lowest (first) memory address
 | Byte 0 | Byte 1 | Byte 2 | Byte 3 | 
Most Significant Byte (MSB) |  |  |  |  | Least Significant Byte (LSB)
Instruction Format
To know how important this issue is, read to “Gulliver's Travels”

## Slide 33: What should an ISA want to provide?
Use general purpose registers with a load-store architecture.
Support these addressing modes: displacement, immediate, register indirect.
Support these simple instructions: load, store, add, subtract, move register, shift, compare equal, compare not equal, branch, jump, call, return.
Support these data size: 8-,16-,32-bit integer, IEEE FP standard.
Provide at least 16 general purpose registers plus separate FP registers and aim for a minimal instruction set.

## Slide 34: 64-Bit Processors
Notes: Please if anyone has additional comments please speak up

## Slide 35: 32-bit Computing
In computer architecture, a word is defined as a unit of data that can be addressed and moved between the computer processor and the storage area.
In 32-bit computing a word is 32 bits.
Usually, the defined bit-length of a word is equivalent to the width of the computer's data bus (and registers) so that a word can be moved in a single operation from the storage to the processor registers

## Slide 36: 32-bit Computing
In a 32-bit microprocessor;
  There are 32-bit general-purpose registers in the processor.
  There are 232 = 4GB memory to be addressed.

## Slide 37: 64-bit Computing
The best and simple definition is enhancing the processing word in the architecture to 64 bits.
The addressable memory increases from 4 GB to up to 264 = 18 billion GB
  Many implementations support less than this
Size of registers extended to 64 bits
Integer and address data up to 64 bits in length can now be operated on
264 = 1.8 x 1019 integers can be represented with 64 bits vs. 4.3 x 109 with 32 bits
Dynamic range has increased by a factor of 4.3 billion!

## Slide 38: 64-bit Computing
Stepping up from 32 to 64 bits does not mean doubling performance
Certain applications will benefit, others may not
What Applications Can Benefit Most From 64-bit?
Large databases
Business and scientific simulation and modeling programs
Highly graphics-intensive software (CAD, 3-D games)
Cryptography
Etc.