## Slide 1: COMP4611: Design and Analysis of Computer Architectures Basic Pipelining Lin Gu CSE, HKUST

## Slide 2: Introduction to Pipelining – Boeing Everett
Courtesy photos by Boeing

## Slide 3: Introduction to Pipelining
Pipelining: An implementation technique that overlaps the execution of multiple instructions. It is a key technique in achieving high-performance
Laundry Example
Ann, Brian, Cathy, Dave each has one load of clothes to wash, dry, and fold
Washing takes 30 minutes
Drying takes 40 minutes
“Folding” takes 20 minutes
A
B
C
D
dryer
washer
folding

## Slide 4: Sequential Laundry
Sequential laundry takes 6 hours for 4 loads
A
B
C
D
30
40
20
30
40
20
30
40
20
30
40
20
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time

## Slide 5: Pipelined Laundry: start work ASAP
Pipelined laundry takes 3.5 hours for 4 loads
Speedup = 6/3.5 = 1.7
A
B
C
D
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20

## Slide 6: Pipelining Lessons
Latency vs. Throughput
Question
  What is the latency in both cases ?
  What is the throughput in both cases ?
Pipelining doesn’t reduce latency of single task,
It increases throughput of entire workload
A
B
C
D
30
40
40
40
40
20

## Slide 7: Pipelining Lessons [cont’d…]
Question
  What is the fastest operation in the example ?
  What is the slowest operation in the example
Pipeline rate limited by slowest pipeline stage
A
B
C
D
30
40
40
40
40
20

## Slide 8: Pipelining Lessons [cont’d…]
Washing takes 30 minutes
Drying takes 40 minutes
“Folding” takes 20 minutes
Question
  Would it matter if “folding” also took 40 minutes
Unbalanced lengths of pipe stages reduce speedup

## Slide 9: Pipelining Lessons [cont’d…]
A
B
C
D
30
40
40
40
40
20
Multiple tasks operating simultaneously using different resources

## Slide 10: Pipelining Lessons [contd…]
Question
  Would the speedup increase if we had more steps ?
A
B
C
D
30
40
40
40
40
20
Potential Speedup = Number of pipe stages
More steps = Deeper pipeline

## Slide 11: Pipelining Lessons [cont’d…]
A
B
C
D
30
40
40
40
40
20
Time to “fill” pipeline and time to “drain” it reduce speedup

## Slide 12: Pipelining in Computation
Comp.
R
E
G
30ns
3ns
Clock
Delay = 33ns
Throughput = 30MHz
Time
Unpipelined
System
Op1
Op2
Op3
  One operation must complete before next can begin
  Operations spaced 33ns apart

## Slide 13: 3 Stage Pipelining
  Space operations 13ns apart
  3 operations occur simultaneously
R
E
G
Clock
Comp.
R
E
G
Comp.
R
E
G
Comp.
10ns
3ns
10ns
3ns
10ns
3ns
Delay = 39ns
Throughput = 77MHz
Time
Op1
Op2
Op3
Op4

## Slide 14: Limitation: Non-uniform Pipelining
Clock
R
E
G
Comp.
R
E
G
Comp.
R
E
G
Comp.
5ns
3ns
15ns
3ns
10ns
3ns
Delay = 18 * 3 = 54 ns
Throughput = 55MHz
  Throughput limited by slowest stage
    Delay determined by clock period * number of stages
  Must attempt to balance stages

## Slide 15: Limitation: Deep Pipelines
  Diminishing returns as add more pipeline stages
  Register delays become limiting factor
    Increased latency
    Small throughput gains
    More hazards
Delay = 48ns, Throughput = 128MHz
Clock
R
E
G
Comp.
5ns
3ns
R
E
G
Comp.
5ns
3ns
R
E
G
Comp
5ns
3ns
R
E
G
Comp.
5ns
3ns
R
E
G
Comp.
5ns
3ns
R
E
G
Comp.
5ns
3ns

## Slide 16: Computer (Processor) Pipelining
It is one KEY method of achieving High-Performance in modern microprocessors
A major advantage of pipelining over “parallel processing” is that it is not visible to the programmer
An instruction execution pipeline involves a number of steps, where each step completes a part of an instruction.
  Each step is called a pipe stage or a pipe segment.

## Slide 17: Pipelining
Instr 2
Multiple instructions overlapped in execution
Throughput increased
Doesn’t reduce time for individual instructions
Instr 1
Stage 2
Stage 3
Stage 4
Stage 5
Stage 6
Stage 7
Stage 1
Instr 7
Instr 6
Instr 5
Instr 4
Instr 3
Instr 2
Instr 1
Stage 2
Stage 3
Stage 4
Stage 5
Stage 6
Stage 7
Stage 1

## Slide 18: Computer Pipelining
The stages or steps are connected one to the next to form a pipe -- instructions enter at one end and progress through the stage and exit at the other end.
Throughput of an instruction pipeline is determined by how often an instruction exits the pipeline.
An instruction moves one step down the pipeline after every time interval C, where C equals to the cycle time or machine cycle (1/Clock Rate) and is determined by the stage with the longest processing delay (slowest pipeline stage).

## Slide 19: Pipelining: Design Goals
An important pipeline design consideration is to balance the length of each pipeline stage.
If all stages are perfectly balanced, then the time per instruction on a pipelined machine (assuming ideal conditions with no stalls):
Time per instruction on unpipelined machine
Number of pipe stages

## Slide 20: Pipelining: Design Goals
Under these ideal conditions:
  Speedup from pipelining equals the number of pipeline stages: n
  One instruction is completed every cycle, CPI = 1 .
  This is an asymptote of course, but +10% is commonly achieved
  Difference is due to difficulty in achieving balanced stage design
Two ways to view the performance mechanism
  Reduced CPI (i.e. non-piped to piped change)
    Close to 1 instruction/cycle if you’re lucky
  Reduced cycle-time (i.e. increasing pipeline depth)
    Work split into more stages
    Simpler stages result in faster clock cycles

## Slide 21: Implementation of MIPS
We use the MIPS processor as an example to demonstrate the concepts of computer pipelining.
MIPS ISA design reflects careful measurements and informed architectural decisions.
The design of its pipeline needs to answer the following questions
How are instructions executed?
How to pipeline them?

## Slide 22: How to Execute an Instruction?
“Vēnī, vīdī, vīcī ”
Bring the instruction to the processor – “Fetch”
– “I came, I saw, I conquered”
Examine the instruction – “Decode”
Do the work – “Execute, Memory-Access, Writeback”
IF, ID, EX, MEM, WB

## Slide 23: A Basic Multi-Cycle Implementation of MIPS
Instruction fetch cycle (IF):
    IR ¬ Mem[PC]
    NPC ¬ PC + 4
Note: IR (instruction register), NPC (next sequential program counter register)
16
6
5
5
Immediate
rt
rs
Opcode
6
26
Opcode
Offset added to PC
J - Type instruction
R - type instruction
I - type instruction
0 5 6 10 11 15 16 31
0 5 6 31
6
5
5
5
5
Opcode
rs
rt
rd
func
6
shamt
0 5 6 10 11 15 16 20 21 25 26 31

## Slide 24: A Basic Multi-Cycle Implementation of MIPS
Instruction decode/register fetch cycle (ID):
    Parse instruction
    Read:
    A ¬ Regs[rs];
    B ¬ Regs[rt];
    Imm ¬ ((IR16)16##IR 16..31) sign-extended immediate field of IR
Note: A, B, Imm are temporary registers
16
6
5
5
Immediate
rt
rs
Opcode
6
26
R - type instruction
I - type instruction
6
5
5
5
5
Opcode
rs
rt
rd
func
6
shamt
0 5 6 10 11 15 16 20 21 25 26 31

## Slide 25: A Basic Implementation of MIPS (continued)
Execution/Effective address cycle (EX):
  Memory reference:
    ALUOutput ¬ A + Imm;
  Register-Register ALU instruction:
    ALUOutput ¬ A op B;
  Register-Immediate ALU instruction:
    ALUOutput ¬ A op Imm;
  Branch (simplification – only consider BEQZ):
    ALUOutput ¬ NPC + Imm;
    cond ¬ (A == 0)

## Slide 26: A Basic Implementation of MIPS (continued)
Memory access/branch completion cycle (MEM):
  Memory reference:
    LMD ¬ Mem[ALUOutput] or
    Mem[ALUOutput] ¬ B;
  Branch:
    if (cond) PC ¬ ALUOutput else PC ¬ NPC
  Note: LMD (load memory data) register

## Slide 27: A Basic Implementation of MIPS (continued)
Write-back cycle (WB):
  Register-Register ALU instruction:
    Regs[rd] ¬ ALUOutput;
  Register-Immediate ALU instruction:
    Regs[rt] ¬ ALUOutput;
  Load instruction:
    Regs[rt] ¬ LMD;
Note: LMD (load memory data) register

## Slide 28
Basic MIPS Integer Datapath Implementation

## Slide 29: Datapath for Instruction Fetch
IR <- MEM[PC]
PC <- PC + 4
RD
Memory
ADDR
PC
IR
4
ADD

## Slide 30: Datapath for R-Type Instructions
add rd, rs, rt
R[rd] <- R[rs] + R[rt];

## Slide 31: Datapath for Load/Store Instructions
lw rt, offset(rs)
R[rt] <- MEM[R[rs] + s_extend(offset)];

## Slide 32: Datapath for Load/Store Instructions
sw rt, offset(rs)
MEM[R[rs] + sign_extend(offset)] <- R[rt]

## Slide 33: Datapath for Branch Instructions
beq rs, r0, offset
  if (R[rs] == 0) then PC <- PC+4 + s_extend(offset<<2)

## Slide 34: Basic MIPS Processor (More Details)
IF
Instruction Fetch
ID
Instruction Decode
EX
Execute/ Address Calc.
MEM
Memory Access
WB
Write Back
Taken?
5
5
16
RD1
RD2
RN1
RN2
WN
WD
Register File
ALU
E
X
T
N
D
16
32
RD
WD
Data
Memory
ADDR
5
Instruction
I
32
M
U
X
<<2
RD
Instruction
Memory
ADDR
PC
4
ADD
ADD
M
U
X
32

## Slide 35: Pipelining - Key Idea
Question: What happens if we break execution into multiple cycles?
Answer: in the best case, we can start executing a new instruction on each clock cycle - this is pipelining
Pipelining stages:
  IF - Instruction Fetch
  ID - Instruction Decode
  EX - Execute / Address Calculation
  MEM - Memory Access (read / write)
  WB - Write Back (results into register file)

## Slide 36: Simple MIPS Pipelined Integer Instruction Processing
Clock Number Time in clock cycles ®
Instruction Number 1 2 3 4 5 6 7 8 9
Instruction I IF ID EX MEM WB
Instruction I+1 IF ID EX MEM WB
Instruction I+2 IF ID EX MEM WB
Instruction I+3 IF ID EX MEM WB
Instruction I +4 IF ID EX MEM WB
Time to fill the pipeline
MIPS Pipeline Stages:
IF = Instruction Fetch
ID = Instruction Decode
EX = Execution
MEM = Memory Access
WB = Write Back
First instruction, I
Completed
Last instruction,
I+4 completed
  How to design the datapaths to support pipelining?

## Slide 37: Basic MIPS Processor (More Details)
IF
Instruction Fetch
ID
Instruction Decode
EX
Execute/ Address Calc.
MEM
Memory Access
WB
Write Back
Taken?
5
5
16
RD1
RD2
RN1
RN2
WN
WD
Register File
ALU
E
X
T
N
D
16
32
RD
WD
Data
Memory
ADDR
5
Instruction
I
32
M
U
X
<<2
RD
Instruction
Memory
ADDR
PC
4
ADD
ADD
M
U
X
32

## Slide 38: Pipeline Registers
Need pipeline registers (latches) between stages to hold data for instructions
Pipeline registers are named with 2 stages (the stages that the register is “between.”)
ANY information needed in a later pipeline stage MUST be passed via a pipeline register
  Example:IF/ID register gets
    instruction
    PC+4
No register is needed after WB. Results from the WB stage are already stored in the register file.

## Slide 39: Basic Pipelined Processor
IF
ID
EX
MEM
WB
Taken?
5
5
16
RD1
RD2
RN1
RN2
WN
WD
Register File
ALU
E
X
T
N
D
16
32
RD
WD
Data
Memory
ADDR
5
Instruction
I
32
M
U
X
<<2
RD
Instruction
Memory
ADDR
PC
4
ADD
ADD
M
U
X
32
IF/ID
Pipeline Registers
ID/EX
EX/MEM
MEM/WB

## Slide 40: Non-Pipelined vs. Pipelined Execution
Non-Pipelined
Pipelined

## Slide 41: Pipelined Example - Executing Multiple Instructions
Consider the following instruction sequence:
    lw $r0, 10($r1)
    sw $sr3, 20($r4)
    add $r5, $r6, $r7
    sub $r8, $r9, $r10

## Slide 42: Executing Multiple Instructions Clock Cycle 1
LW

## Slide 43: Executing Multiple Instructions Clock Cycle 2
LW
SW

## Slide 44: Executing Multiple Instructions Clock Cycle 3
LW
SW
ADD
5
RD1
RD2
RN1
RN2
WN
WD
Register
File
ALU
E
X
T
N
D
16
32
RD
WD
Data
Memory
ADDR
32
M
U
X
<<2
RD
Instruction
Memory
ADDR
PC
4
ADD
ADD
M
U
X
5
5
5
IF/ID
ID/EX
EX/MEM
MEM/WB
Zero

## Slide 45: Executing Multiple Instructions Clock Cycle 4
LW
SW
ADD
SUB

## Slide 46: Executing Multiple Instructions Clock Cycle 5
LW
SW
ADD
SUB

## Slide 47: Executing Multiple Instructions Clock Cycle 6
SW
ADD
SUB

## Slide 48: Executing Multiple Instructions Clock Cycle 7
ADD
SUB

## Slide 49: Executing Multiple Instructions Clock Cycle 8
SUB

## Slide 50: Alternative View - Multicycle Diagram
IM
REG
ALU
DM
REG
lw $r0, 10($r1)
sw $r3, 20($r4)
add $r5, $r6, $r7
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
IM
REG
ALU
DM
REG
IM
REG
ALU
DM
REG
sub
$r8, $r9, $r10
IM
REG
ALU
DM
REG
Cycle 8

## Slide 51
How much does pipelining improve the performance? How to calculate throughput and latency of a pipelined processor?
How to design the pipeline to increase speedup?
…
Pipeline Performance
Throughput, latency, hazards

## Slide 52: Pipelining Performance Example
Example: For an unpipelined CPU:
  Clock cycle = 1ns, 4 cycles for ALU operations and branches and 5 cycles for memory operations with instruction frequencies of 40%, 20% and 40%, respectively.
  If pipelining adds 0.2 ns to the machine clock cycle then the speedup in instruction execution from pipelining is:
Non-pipelined Average instruction execution time = Clock cycle x Average CPI
= 1 ns x ((40% + 20%) x 4 + 40%x 5) = 1 ns x 4.4 = 4.4 ns
In the 5-stage pipelined implementation, the latency is 6ns, but the average instruction execution time is: 1 ns + 0.2 ns = 1.2 ns
Speedup from pipelining = Instruction time unpipelined
Instruction time pipelined
= 4.4 ns / 1.2 ns = 3.7 times faster

## Slide 53: Pipeline Throughput and Latency: A More realistic Examples
IF
ID
EX
MEM
WB
5 ns
4 ns
5 ns
10 ns
4 ns
Consider the pipeline above with the indicated
delays. We want to know what the pipeline
throughput and the pipeline latency are.
Pipeline throughput: instructions completed per second.
Pipeline latency: how long does it take to execute a
single instruction in the pipeline.

## Slide 54: Pipeline Throughput and Latency
IF
ID
EX
MEM
WB
5 ns
4 ns
5 ns
10 ns
4 ns
Pipeline latency: how long does it take to execute an
instruction in the pipeline.
?

## Slide 55: Pipeline Throughput and Latency
IF
ID
EX
MEM
WB
5 ns
4 ns
5 ns
10 ns
4 ns
Simply adding the latencies to compute the pipeline
latency only would work for an isolated instruction
L(I5) = 43ns
IF
MEM
ID
I1
L(I1) = 28ns
EX
WB
MEM
ID
IF
I2
L(I2) = 33ns
EX
WB
MEM
ID
IF
I3
L(I3) = 38ns
EX
WB
MEM
ID
IF
I4
EX
WB
We are in trouble! The latency is not constant.
This happens because this is an unbalanced
pipeline. The solution is to make every state
the same length as the longest one.

## Slide 56: Synchronous Pipeline Throughput and Latency
IF
ID
EX
MEM
WB
5 ns
4 ns
5 ns
10 ns
4 ns
The slowest pipeline stage also limits the latency!!
IF
MEM
ID
I1
L(I1) = L(I2) = L(I3) = L(I4) = 50ns
EX
WB
IF
MEM
ID
I2
L(I2) = 50ns
EX
WB
IF
MEM
ID
EX
WB
IF
MEM
ID
EX
0
10
20
30
40
50
60
I3
I4

## Slide 57: Pipeline Throughput and Latency
IF
ID
EX
MEM
WB
5 ns
4 ns
5 ns
10 ns
4 ns
Pipeline throughput: how often an instruction is completed.
IF
ID
EX
MEM
WB
10 ns
10 ns
10 ns
10 ns
10 ns

## Slide 58: Pipeline Throughput and Latency
How long does it take to execute (issue) 20000 instructions
in this pipeline? (disregard latency, bubbles caused by
branches, cache misses, hazards, fill, drain)
How long would it take using the same modules
without pipelining?
IF
ID
EX
MEM
WB
5 ns
4 ns
5 ns
10 ns
4 ns
IF
ID
EX
MEM
WB
10 ns
10 ns
10 ns
10 ns
10 ns

## Slide 59: Pipeline Throughput and Latency
IF
ID
EX
MEM
WB
5 ns
4 ns
5 ns
10 ns
4 ns
Thus the speedup that we got from the pipeline is:
How can we improve this pipeline design?
We need to reduce the unbalance to increase
the clock speed.

## Slide 60: Pipeline Throughput and Latency
IF
ID
EX
MEM1
WB
5 ns
4 ns
5 ns
5 ns
4 ns
Now we have one more pipeline stage, but the
maximum latency of a single stage is reduced in half.
MEM2
5 ns
The new latency for a single instruction is:

## Slide 61: Pipeline Throughput and Latency
IF
ID
EX
MEM1
WB
5 ns
4 ns
5 ns
5 ns
4 ns
MEM2
5 ns
IF
MEM1
ID
I1
EX
WB
MEM2
IF
MEM1
ID
I2
EX
WB
MEM2
IF
MEM1
ID
I3
EX
WB
MEM2
IF
MEM1
ID
I4
EX
WB
MEM2
IF
MEM1
ID
I5
EX
WB
MEM2
IF
MEM1
ID
I6
EX
WB
MEM2
IF
MEM1
ID
I7
EX
WB
MEM2

## Slide 62: Pipeline Throughput and Latency
IF
ID
EX
MEM1
WB
5 ns
4 ns
5 ns
5 ns
4 ns
MEM2
5 ns
How long does it take to execute 20000 instructions
in this pipeline? (disregard bubbles caused by
branches, cache misses, etc, for now)
Thus the speedup that we get from the pipeline is:

## Slide 63: Pipeline Throughput and Latency
IF
ID
EX
MEM1
WB
5 ns
4 ns
5 ns
5 ns
4 ns
MEM2
5 ns
What have we learned from this example?
1. It is important to balance the delays in the
stages of the pipeline
2. The throughput of a pipeline is 1/max(stage_delay).
3. The latency is Nmax(stage_delay), where N is the
number of stages in the pipeline.