## Slide 1: Warehouse-Scale Computers to Exploit Request-Level and Data-Level Parallelism
Lin Gu CSE, HKUST
COMP4611: Design and Analysis of Computer Architectures

## Slide 2: Server Computers
Applications are increasingly run on servers
  Web search, office apps, virtual worlds, …
Requires large data center servers
  Multiple processors, networks connections, massive storage
  Space and power constraints
Rack server equipment often in units of 1.75” (1U).
  E.g., a 1U switch, a 2U server

## Slide 3: Rack-Mounted Servers
Sun Fire x4150 1U server

## Slide 4: Scalability Vs. Cost
SMP
Super Server
Departmental
Server
Personal
System
Cluster
of PCs
MPP

## Slide 5: Motivations of using Clusters over Specialized Parallel Computers
Individual PCs are becoming increasingly powerful
Communication bandwidth between PCs is increasing and latency is decreasing (Gigabit Ethernet, Myrinet)
PC clusters are easier to integrate into existing networks
Typical low user utilization of PCs (<10%)
Development tools for workstations and PCs are mature
PC clusters are a cheap and readily available
Clusters can be easily grown

## Slide 6: Cluster Architecture
Sequential Applications
Parallel Applications
Parallel Programming Environment
Cluster Middleware
(Single System Image and Availability Infrastructure)
Cluster Interconnection Network/Switch
PC/Workstation
Network Interface Hardware
Communications
Software
PC/Workstation
Network Interface Hardware
Communications
Software
PC/Workstation
Network Interface Hardware
Communications
Software
PC/Workstation
Network Interface Hardware
Communications
Software
Sequential Applications
Sequential Applications
Parallel Applications
Parallel Applications

## Slide 7: How Can we Benefit From Clusters?
Given a certain user application
Phase 1
  If the application can be run fast enough on a single PC, there is no need to do anything else
  Otherwise go to Phase 2
Phase 2
  Try to put the whole application on the DRAM to avoid going to the disk.
  If that is not possible, use the DRAM of the other idle workstations
  Network DRAM is 5 to 10 times faster than local disk

## Slide 8: Remote Memory Paging
Background
  Application’s working sets have increased dramatically
  Applications require more memory than a single workstation can provide.
Solution
  Inserts the Network DRAM in the memory hierarchy between local memory and the disk
  Swaps the page to remote memory
Cache
Main Memory
Disk
Cache
Main Memory
Disk
Network RAM

## Slide 9: How Can we Benefit From Clusters?
In this case, the DRAM of the networked PCs behave like a huge cache system for the disk
Otherwise go to Phase 3
512 MB
512 MB + Disk
All DRAM
Networked DRAM
Problem size
Time

## Slide 10: How Can we Benefit From Clusters?
Phase 3
  If the network DRAM is not large enough, try using all the disks in the network in parallel for reading and writing data and program code (e.g., RAID) to speedup the I/O
  Or, go to Phase 4
File
Cache
P
File
Cache
P
File
Cache
P
File
Cache
P
File
Cache
P
File
Cache
P
File
Cache
P
File
Cache
P
Communication Network
Network RAID striping
Local
Cache
Cluster
Caching

## Slide 11: How Can we Benefit From Clusters?
Phase 4
  Execute the program on a multiple number of workstations (PCs) at the same time – Parallel processing
Tools
  There are many tools that do all these phases in a transparent way (except parallelizing the program) as well as load-balancing and scheduling.
    Beowulf (CalTech and NASA) - USA
    Condor - Wisconsin State University, USA
    MPI (MPI Forum, MPICH is one of the popular implementations)
    NOW (Network of Workstations) - Berkeley, USA
    PVM - Oak Ridge National Lab./UTK/Emory, USA

## Slide 12: What network should be used?
 | Fast Ethernet | Gigabit Ethernet | Myrinet | 10GbE
Latency | ~120s | ~120 s | ~7 s | 10s of s’s
Bandwidth | ~100Mbps peak | ~1Gbps peak | ~1.98Gbps real | 10Gbps peak

## Slide 13: 2007 Top500 List
Clusters are the fastest growing category of supercomputers in the TOP500 List.
  406 clusters (81%) in November 2007 list
  130 clusters (23%) in the June 2003 list
  80 clusters (16%) in the June 2002 list
  33 clusters (6.6%) in the June 2001 list
4% of the supercomputers in the November 2007 TOP500 list use Myrinet technology!
54% of the supercomputers in the November 2007 TOP500 list Gigabit Ethernet technology!

## Slide 14: Introduction
Warehouse-scale computer (WSC)
  Provides Internet services
    Search, social networking, online maps, video sharing, online shopping, email, cloud computing, etc.
  Differences with HPC “clusters”:
    Clusters have higher performance processors and network
    Clusters emphasize thread-level parallelism, WSCs emphasize request-level parallelism
  Differences with datacenters:
    Datacenters consolidate different machines and software into one location
    Datacenters emphasize virtual machines and hardware heterogeneity in order to serve varied customers

## Slide 15: Introduction
Important design factors for WSC:
  Cost-performance
    Small savings add up
  Energy efficiency
    Affects power distribution and cooling
    Work per joule
  Dependability via redundancy
  Network I/O
  Interactive and batch processing workloads
  Ample computational parallelism is not important
    Most jobs are totally independent
    “Request-level parallelism”
  Operational costs count
    Power consumption is a primary, not secondary, constraint when designing system
  Scale and its opportunities and problems
    Can afford to build customized systems since WSC require volume purchase

## Slide 16: Google
1. The user enters a query on a web form sent to the Google web server.
2. The web server sends the query to the Index Server cluster, which matches the query to documents.
3. The match is sent to the Doc Server cluster, which retrieves the documents to generate abstracts and cached copies.
4. The list, with abstracts, is displayed by the web server to the user, sorted (using a secret formula involving PageRank).

## Slide 17: Google Requirements
Google: search engine that scales at Internet growth rates
Search engines: 24x7 availability
Google : 600M queries/day, or AVERAGE of 7500 queries/s all day (old data)
Google crawls WWW and puts up new index every 2 weeks (old data)
Storage: 5.3 billion web pages, 950 million newsgroup messages, and 925 million images indexed, Millions of videos (very old data)
Response time goal: < 0.5 s per search (old data)

## Slide 18: Google (Based on old data)
Require high amounts of computation per request
A single query on Google (on average)
  reads hundreds of megabytes of data
  consumes tens of billions of CPU cycles
A peak request stream on Google
  requires an infrastructure comparable in size to largest supercomputer installations
Typical google Data center: 15000 PCs (Linux), 30000 disks: almost 3 petabyte!
Google application affords easy parallelization
  Different queries can run on different processors
  A single query can use multiple processors
    because the overall index is partitioned

## Slide 19: Prgrm’g Models and Workloads
Batch processing framework: MapReduce
  Map: applies a programmer-supplied function to each logical input record
    Runs on thousands of computers
    Provides new set of key-value pairs as intermediate values
  Reduce: collapses values using another programmer-supplied function

## Slide 20: Prgrm’g Models and Workloads
Example:
  map (String key, String value):
    // key: document name
    // value: document contents
    for each word w in value
      EmitIntermediate(w,”1”); // Produce list of all words
  reduce (String key, Iterator values):
    // key: a word
    // value: a list of counts
    int result = 0;
    for each v in values:
      result += ParseInt(v); // get integer from key-value pair
    Emit(AsString(result));

## Slide 21: Prgrm’g Models and Workloads
MapReduce runtime environment schedules map and reduce task to WSC nodes
Availability:
  Use replicas of data across different servers
  Use relaxed consistency:
    No need for all replicas to always agree
Workload demands
  Often vary considerably

## Slide 22: Computer Architecture of WSC
WSC often use a hierarchy of networks for interconnection
Each rack holds dozens of servers connected to a rack switch
Rack switches are uplinked to switch higher in hierarchy
  Uplink has 48 / n times lower bandwidth, where n = # of uplink ports
    “Oversubscription”
  Goal is to maximize locality of communication relative to the rack

## Slide 23: Storage
Storage options:
  Use disks inside the servers, or
  Network attached storage through Infiniband
  WSCs generally rely on local disks
  Google File System (GFS) uses local disks and maintains at least three replicas

## Slide 24: Array Switch
Switch that connects an array of racks
  Array switch should have 10 X the bisection bandwidth of rack switch
  Cost of n-port switch grows as n2
  Often utilize content addressible memory chips and FPGAs

## Slide 25: WSC Memory Hierarchy
Servers can access DRAM and disks on other servers using a NUMA-style interface

## Slide 26: Infrastructure and Costs of WSC
Location of WSC
  Proximity to Internet backbones, electricity cost, property tax rates, low risk from earthquakes, floods, and hurricanes
Power distribution

## Slide 27: Infrastructure and Costs of WSC
Cooling
  Air conditioning used to cool server room
  64 F – 71 F
    Keep temperature higher (closer to 71 F)
  Cooling towers can also be used
    Minimum temperature is “wet bulb temperature”

## Slide 28: Infrastructure and Costs of WSC
Cooling system also uses water (evaporation and spills)
  E.g. 70,000 to 200,000 gallons per day for an 8 MW facility
Power cost breakdown:
  Chillers: 30-50% of the power used by the IT equipment
  Air conditioning: 10-20% of the IT power, mostly due to fans
How man servers can a WSC support?
  Each server:
    “Nameplate power rating” gives maximum power consumption
    To get actual, measure power under actual workloads
  Oversubscribe cumulative server power by 40%, but monitor power closely

## Slide 29: Measuring Efficiency of a WSC
Power Utilization Effectiveness (PEU)
  = Total facility power / IT equipment power
  Median PUE on 2006 study was 1.69
Performance
  Latency is important metric because it is seen by users
  Bing study: users will use search less as response time increases
  Service Level Objectives (SLOs)/Service Level Agreements (SLAs)
    E.g. 99% of requests be below 100 ms

## Slide 30: Cost of a WSC
Capital expenditures (CAPEX)
  Cost to build a WSC
Operational expenditures (OPEX)
  Cost to operate a WSC

## Slide 31: Cloud Computing
WSCs offer economies of scale that cannot be achieved with a datacenter:
  5.7 times reduction in storage costs
  7.1 times reduction in administrative costs
  7.3 times reduction in networking costs
  This has given rise to cloud services such as Amazon Web Services
    “Utility Computing”
    Based on using open source virtual machine and operating system software