## Slide 1: Pipelining LLP, Dynamic Scheduling Lin Gu CSE, HKUST
COMP4611: Design and Analysis of Computer Architectures

## Slide 2: Loop-Level Parallelism (LLP) Analysis
Loop-Level Parallelism (LLP) analysis focuses on whether data accesses in later iterations of a loop are data dependent on data values produced in earlier iterations.
e.g. in for (i=1; i<=1000; i++)
x[i] = x[i] + s;
The computation in each iteration is independent of the previous iterations and the loop is thus parallel. The use of x[i] twice is within a single iteration.
    Thus loop iterations are independent from each other
Loop-carried Dependence: A data dependence between different loop iterations (data produced in earlier iteration used in a later one) – limits parallelism.
Instruction level parallelism (ILP) analysis, on the other hand, is usually done when instructions are generated by the compiler.

## Slide 3: LLP Analysis Example 1
In the loop:
for (i=1; i<=100; i=i+1) {
A[i+1] = A[i] + C[i]; /* S1 */
B[i+1] = B[i] + A[i+1];} /* S2 */
}
(Where A, B, C are distinct non-overlapping arrays)
  S2 uses the value A[i+1], computed by S1 in the same iteration. This data dependence is within the same iteration (not a loop-carried dependence).
    does not prevent loop iteration from being parallelized.
  S1 uses a value computed by S1 in an earlier iteration, since iteration i computes A[i+1] read in iteration i+1 This is thus loop-carried dependence, and limits parallelism. The same applies for S2 for B[i] and B[i+1]
    These two dependences are loop-carried spanning more than one iteration

## Slide 4: LLP Analysis Example 2
In the loop:
for (i=1; i<=100; i=i+1) {
A[i] = A[i] + B[i]; /* S1 */
B[i+1] = C[i] + D[i]; /* S2 */
}
  S1 uses the value B[i] computed by S2 in the previous iteration (loop-carried dependence)
  This dependence is not circular:
    S1 depends on S2 but S2 does not depend on S1.
  Can be made parallel by replacing the code with the following:
  A[1] = A[1] + B[1];
  for (i=1; i<=99; i=i+1) {
  B[i+1] = C[i] + D[i];
  A[i+1] = A[i+1] + B[i+1];
  }
  B[101] = C[100] + D[100];
Loop Start-up code
Loop Completion code

## Slide 5: LLP Analysis Example 2
Original Loop:
A[100] = A[100] + B[100];
B[101] = C[100] + D[100];
A[1] = A[1] + B[1];
B[2] = C[1] + D[1];
A[2] = A[2] + B[2];
B[3] = C[2] + D[2];
A[99] = A[99] + B[99];
B[100] = C[99] + D[99];
A[100] = A[100] + B[100];
B[101] = C[100] + D[100];
A[1] = A[1] + B[1];
B[2] = C[1] + D[1];
A[2] = A[2] + B[2];
B[3] = C[2] + D[2];
A[99] = A[99] + B[99];
B[100] = C[99] + D[99];
for (i=1; i<=100; i=i+1) {
A[i] = A[i] + B[i]; /* S1 */
B[i+1] = C[i] + D[i]; /* S2 */
}
  A[1] = A[1] + B[1];
  for (i=1; i<=99; i=i+1) {
  B[i+1] = C[i] + D[i];
  A[i+1] = A[i+1] + B[i+1];
  }
  B[101] = C[100] + D[100];
Modified Parallel Loop:
Iteration 1
Iteration 2
Iteration 100
Iteration 99
Loop-carried
Dependence
Loop Start-up code
Loop Completion code
Iteration 1
Iteration 98
Iteration 99
Not Loop
Carried
Dependence
. . . . . .
. . . . . .
. . . .

## Slide 6: Dynamic Scheduling Through Hardware Schemes

## Slide 7: Static vs. Dynamic Scheduling
Static Scheduling by compiler
  Code scheduling for LD delay slots and branch delay slots
  Avoiding data hazards
  In-order instruction issue:
    If an instruction is stalled, no later instructions can proceed.
    Multiple copies of a unit may be idle – inefficiency
    Static scheduling cannot help
Dynamic Scheduling by Hardware
  Allow Out-of-order execution, Out-of-order “completion”
  Even though an instruction is stalled, later instructions, with no data dependencies with the instructions which are stalled and causing the stall, can proceed
  Efficient utilization of functional unit with multiple units

## Slide 8: Dynamic Pipeline Scheduling: The Concept
Dynamic pipeline scheduling overcomes the limitations of in-order execution by allowing out-of-order instruction execution.
  Works when dependencies are unknown at compile time
  Simpler compiler
Instructions are allowed to start executing out-of-order as soon as their operands are available.
Example:
This implies allowing out-of-order instruction “completion’.
In the case of in-order execution
SUBD must wait for DIVD to complete
which stalled ADDD before starting execution
In out-of-order execution SUBD can start as soon
as the values of its operands F8, F14 are available.
DIVD F0, F2, F4
ADDD F10, F0, F8
SUBD F12, F8, F14

## Slide 9: Dynamic Pipeline Scheduling
Dynamic instruction scheduling can be accomplished by:
  Dividing the Instruction Decode ID stage into two stages:
    Issue: Decode instructions, check for structural hazards.
    Read operands: Wait until data hazard conditions, if any, are resolved, then read operands when available.
    (All instructions pass through the issue stage in order but can be stalled or pass each other in the read operands stage).
  In the instruction fetch stage IF, fetch an additional instruction every cycle into a latch or several instructions into an instruction queue.
  Increase the number of functional units to meet the demands of the additional instructions in their EX stage.

## Slide 10: Dynamic Pipeline Scheduling
Two dynamic scheduling approaches exist:
  Dynamic scheduling with a Scoreboard used first in CDC6600
  The Tomasulo approach pioneered by the IBM 360/91
Most of the modern microprocessors use similar techniques

## Slide 11: Dynamic Scheduling With A Scoreboard
The scoreboard is a hardware mechanism that maintains an execution rate of one instruction per cycle by executing an instruction as soon as its operands are available and no hazard conditions prevent it.
It replaces ID, EX, WB with four stages: ID1, ID2, EX, WB
Every instruction goes through the scoreboard where a record of data dependencies is constructed (corresponds to instruction issue).
A system with a scoreboard is assumed to have several functional units with their status information reported to the scoreboard.

## Slide 12: Dynamic Scheduling With A Scoreboard
If the scoreboard determines that an instruction cannot execute immediately it executes another instruction and keeps monitoring hardware units’ status and decide when the blocked instruction can proceed to execute
The scoreboard also decides when an instruction can write its results to registers
Hazard detection and resolution is centralized in the scoreboard

## Slide 13: Scoreboard Implications
Out-of-order execution ==> WAR, WAW hazards?
    DIVD F0, F2, F4
    ADDD F10, F0, F8
    SUBD F8, F8, F14
If the pipeline executes SUBD before ADDD, it will yield incorrect execution
A WAW hazard would occur. We must detect the hazard and stall until other completes.
DIVD F0, F2, F4
    ADDD F10, F0, F8
    SUBD F10, F8, F14

## Slide 14: Scoreboard Specifics
Several functional units
  several floating-point units, integer units, and memory reference units
Data dependencies (hazards) are detected when an instruction reaches the scoreboard
  corresponding to instruction issue replacing part of the ID stage
Scoreboard determines
  when the instruction is ready for execution
  based on when its operands and functional unit become available
  where results are written

## Slide 15
The basic structure of a MIPS processor with a scoreboard

## Slide 16: Instruction Execution Stages with A Scoreboard
Issue (ID1): If a functional unit for the instruction is available, the scoreboard issues the instruction to the functional unit and updates its internal data structure; structural and WAW hazards are resolved here. (this replaces part of ID stage in the conventional MIPS pipeline).
Read operands (ID2): The scoreboard monitors the availability of the source operands. A source operand is available when no earlier active instruction writes it. When all source operands are available the scoreboard tells the functional unit to read all operands from the registers (no forwarding supported) and start execution (RAW hazards resolved here dynamically). This completes ID.
Execution (EX): The functional unit starts execution upon receiving operands. When the results are ready it notifies the scoreboard (replaces EX, MEM in MIPS).
Write result (WB): Once the scoreboard senses that a functional unit completed execution, it checks for WAR hazards and stalls the completing instruction if needed otherwise the write-back is completed.

## Slide 17: Three Parts of the Scoreboard
Instruction status: Which of 4 steps the instruction is in.
Functional unit status: Indicates the state of the functional unit (FU). Nine fields for each functional unit:
  Busy Indicates whether the unit is busy or not
  Op Operation to perform in the unit (e.g., ADD.D or SUB.D)
  Fi Destination register
  Fj, Fk Source-register numbers
  Qj, Qk Functional units producing source registers Fj, Fk
  Rj, Rk Flags indicating when Fj, Fk are ready
  (set to Yes after operand is available to read)
Register result status: Indicates which functional unit will write to each register, if one exists. Blank when no pending instructions will write that register.

## Slide 18: A Scoreboard Example
The following code is run on the MIPS with a scoreboard given earlier with:
    L.D F6, 34(R2)
    L.D F2, 45(R3)
    MUL.D F0, F2, F4
    SUB.D F8, F6, F2
    DIV.D F10, F0, F6
    ADD.D F6, F8, F2
Functional Unit (FU) # of FUs EX Latency
Integer 1 0
Floating Point Multiply 2 10
Floating Point Add 1 2
Floating point Divide 1 40
All functional units are not pipelined

## Slide 19: Dependency Graph For Example Code
L.D F6, 34(R2)
L.D F2, 45(R3)
MUL.D F0, F2, F4
SUB.D F8, F6, F2
DIV.D F10, F0, F6
ADD.D F6, F8, F2
1
2
3
4
5
6
L.D F6, 34 (R2)
1
L.D F2, 45 (R3)
2
MUL.D F0, F2, F4
3
DIV.D F10, F0, F6
5
SUB.D F8, F6, F2
4
ADD.D F6, F8, F2
6
Date Dependence:
(1, 4) (1, 5) (2, 3) (2, 4)
(2, 6) (3, 5) (4, 6)
Output Dependence:
(1, 6)
Anti-dependence:
(5, 6)
Example Code
Real Data Dependence (RAW)
Anti-dependence (WAR)
Output Dependence (WAW)

## Slide 20: Scoreboard Example: Cycle 1
Instruction status
Read
Execution
Write
Instruction
j
k
Issue
operands
complete
Result
L.D
F6
34+
R2
1
L.D
F2
45+
R3
MUL.D
F0
F2
F4
SUB.D
F8
F6
F2
DIV.D
F10
F0
F6
ADD.D
F6
F8
F2
Functional unit status
dest
S1
S2
FU for j
FU for k
Fj?
Fk?
Time
Name
Busy
Op
Fi
Fj
Fk
Qj
Qk
Rj
Rk
Integer
Yes
Load
F6
R2
Yes
Mult1
No
Mult2
No
Add
No
Divide
No
Register result status
Clock
F0
F2
F4
F6
F8
F10
F12
...
F30
1
FU
Integer
FP Latency: Add = 2 cycles, Multiply = 10, Divide = 40

## Slide 21: Scoreboard Example: Cycle 2
FP Latency: Add = 2 cycles, Multiply = 10, Divide = 40
Instruction status
Read
Execution
Write
Instruction
j
k
Issue
operands
complete
Result
L.D
F6
34+
R2
1
L.D
F2
45+
R3
MUL.D
F0
F2
F4
SUB.D
F8
F6
F2
DIV.D
F10
F0
F6
ADD.D
F6
F8
F2
Functional unit status
dest
S1
S2
FU for j
FU for k
Fj?
Fk?
Time
Name
Busy
Op
Fi
Fj
Fk
Qj
Qk
Rj
Rk
Integer
Yes
Load
F6
R2
Yes
Mult1
No
Mult2
No
Add
No
Divide
No
Register result status
Clock
F0
F2
F4
F6
F8
F10
F12
...
F30
2
FU
Integer
2
Issue second L.D? No, stall on structural hazard

## Slide 22: Scoreboard Example: Cycle 3
Issue MUL.D? In-order issue !!!
Instruction status
Read
Execution
Write
Instruction
j
k
Issue
operands
complete
Result
L.D
F6
34+
R2
1
2
3
L.D
F2
45+
R3
MUL.D
F0
F2
F4
SUB.D
F8
F6
F2
DIV.D
F10
F0
F6
ADD.D
F6
F8
F2
Functional unit status
dest
S1
S2
FU for j
FU for k
Fj?
Fk?
Time
Name
Busy
Op
Fi
Fj
Fk
Qj
Qk
Rj
Rk
Integer
Yes
Load
F6
R2
Yes
Mult1
No
Mult2
No
Add
No
Divide
No
Register result status
Clock
F0
F2
F4
F6
F8
F10
F12
...
F30
3
FU
Integer
?

## Slide 23: Scoreboard Example: Cycle 4
Instruction status
Read
Execution
Write
Instruction
j
k
Issue
operands
complete
Result
L.D
F6
34+
R2
1
2
3 4
L.D
F2
45+
R3
MUL.D
F0
F2
F4
SUB.D
F8
F6
F2
DIV.D
F10
F0
F6
ADD.D
F6
F8
F2
Functional unit status
dest
S1
S2
FU for j
FU for k
Fj?
Fk?
Time
Name
Busy
Op
Fi
Fj
Fk
Qj
Qk
Rj
Rk
Integer
Yes
Load
F6
R2
Yes
Mult1
No
Mult2
No
Add
No
Divide
No
Register result status
Clock
F0
F2
F4
F6
F8
F10
F12
...
F30
4
FU
Integer

## Slide 24: Scoreboard Example: Cycle 5
Instruction status
Read
Execution
Write
Instruction
j
k
Issue
operands
complete
Result
F6
34+
R2
1
2
3 4
F2
45+
R3
F0
F2
F4
F8
F6
F2
F10
F0
F6
L.D
L.D
MUL.D
SUB.D
DIV.D
ADD.D
F6
F8
F2
Functional unit status
dest
S1
S2
FU for j
FU for k
Fj?
Fk?
Time
Name
Busy
Op
Fi
Fj
Fk
Qj
Qk
Rj
Rk
Integer
Yes
Load
F2
R3
Yes
Mult1
No
Mult2
No
Add
No
Divide
No
Register result status
Clock
F0
F2
F4
F6
F8
F10
F12
...
F30
5
FU
Integer
5

## Slide 25: Scoreboard Example: Cycle 6
Instruction status
Read
Execution
Write
Instruction
j
k
Issue
operands
complete
Result
F6
34+
R2
1
2
3 4
F2
45+
R3
F0
F2
F4
F8
F6
F2
F10
F0
F6
F6
F8
F2
Functional unit status
dest
S1
S2
FU for j
FU for k
Fj?
Fk?
Time
Name
Busy
Op
Fi
Fj
Fk
Qj
Qk
Rj
Rk
Integer
Yes
Load
F2
R3
Yes
Mult1
Mult2
No
Add
No
Divide
No
Register result status
Clock
F0
F2
F4
F6
F8
F10
F12
...
F30
6
FU
Integer
Yes Mult F0 F2 F4 Integer No Yes
5 6
6
Mult1
L.D
L.D
MUL.D
SUB.D
DIV.D
ADD.D

## Slide 26: Scoreboard Example: Cycle 7
Instruction status
Read
Execution
Write
Instruction
j
k
Issue
operands
complete
Result
F6
34+
R2
1
2
3 4
F2
45+
R3
F0
F2
F4
F8
F6
F2
F10
F0
F6
F6
F8
F2
Functional unit status
dest
S1
S2
FU for j
FU for k
Fj?
Fk?
Time
Name
Busy
Op
Fi
Fj
Fk
Qj
Qk
Rj
Rk
Integer
Yes
Load
F2
R3
Yes
Mult1
Mult2
No
Add
Divide
No
Register result status
Clock
F0
F2
F4
F6
F8
F10
F12
...
F30
7
FU
Integer
5 6 7
6
Yes Mult F0 F2 F4 Integer No Yes
Yes Sub F8 F6 F2 Integer Yes No
Mult1
Add
7
Read multiply operands?
L.D
L.D
MUL.D
SUB.D
DIV.D
ADD.D

## Slide 27: Scoreboard Example: Cycle 8a (First half of cycle 8)
Instruction status
Read
Execution
Write
Instruction
j
k
Issue
operands
complete
Result
F6
34+
R2
1
2
3 4
F2
45+
R3
F0
F2
F4
F8
F6
F2
F10
F0
F6
F6
F8
F2
Functional unit status
dest
S1
S2
FU for j
FU for k
Fj?
Fk?
Time
Name
Busy
Op
Fi
Fj
Fk
Qj
Qk
Rj
Rk
Integer
Yes
Load
F2
R3
Yes
Mult1
Mult2
No
Add
Divide
Register result status
Clock
F0
F2
F4
F6
F8
F10
F12
...
F30
8
FU
Integer
5 6 7
6
Yes Mult F0 F2 F4 Integer No Yes
Yes Sub F8 F6 F2 Integer Yes No
Mult1
Add Divide
7
8
Yes Div F10 F0 F6 Mult1 No Yes
L.D
L.D
MUL.D
SUB.D
DIV.D
ADD.D

## Slide 28: Scoreboard Example: Cycle 8b (Second half of cycle 8)
Instruction status
Read
Execution
Write
Instruction
j
k
Issue
operands
complete
Result
F6
34+
R2
1
2
3 4
F2
45+
R3
F0
F2
F4
F8
F6
F2
F10
F0
F6
F6
F8
F2
Functional unit status
dest
S1
S2
FU for j
FU for k
Fj?
Fk?
Time
Name
Busy
Op
Fi
Fj
Fk
Qj
Qk
Rj
Rk
Integer
No
Mult1
Mult2
No
Add
Divide
Register result status
Clock
F0
F2
F4
F6
F8
F10
F12
...
F30
8
FU
5 6 7 8
6
Yes Mult F0 F2 F4 Yes Yes
Yes Sub F8 F6 F2 Yes Yes
Mult1
Add Divide
7
8
Yes Div F10 F0 F6 Mult1 No Yes
L.D
L.D
MUL.D
SUB.D
DIV.D
ADD.D

## Slide 29: Scoreboard Example: Cycle 9
FP Latency: Add = 2 cycles, Multiply = 10, Divide = 40
Instruction status
Read
Execution
Write
Instruction
j
k
Issue
operands
complete
Result
F6
34+
R2
1
2
3 4
F2
45+
R3
F0
F2
F4
F8
F6
F2
F10
F0
F6
F6
F8
F2
Functional unit status
dest
S1
S2
FU for j
FU for k
Fj?
Fk?
Time
Name
Busy
Op
Fi
Fj
Fk
Qj
Qk
Rj
Rk
Integer
No
10 Mult1
Mult2
No
2 Add
Divide
Register result status
Clock
F0
F2
F4
F6
F8
F10
F12
...
F30
9
FU
5 6 7 8
6 9
Yes Mult F0 F2 F4 Yes Yes
Yes Sub F8 F6 F2 Yes Yes
Mult1
Add Divide
7 9
8
Yes Div F10 F0 F6 Mult1 No Yes
Read operands for MUL.D & SUB.D? Issue ADD.D?
?
L.D
L.D
MUL.D
SUB.D
DIV.D
ADD.D

## Slide 30: Scoreboard Example: Cycle 11
Instruction status
Read
Execution
Write
Instruction
j
k
Issue
operands
complete
Result
F6
34+
R2
1
2
3 4
F2
45+
R3
F0
F2
F4
F8
F6
F2
F10
F0
F6
F6
F8
F2
Functional unit status
dest
S1
S2
FU for j
FU for k
Fj?
Fk?
Time
Name
Busy
Op
Fi
Fj
Fk
Qj
Qk
Rj
Rk
Integer
No
8 Mult1
Mult2
No
0 Add
Divide
Register result status
Clock
F0
F2
F4
F6
F8
F10
F12
...
F30
11
FU
5 6 7 8
6 9
Yes Mult F0 F2 F4 Yes Yes
Yes Sub F8 F6 F2 Yes Yes
Mult1
Add Divide
7 9 11
8
Yes Div F10 F0 F6 Mult1 No Yes
L.D
L.D
MUL.D
SUB.D
DIV.D
ADD.D

## Slide 31: Scoreboard Example: Cycle 12
Instruction status
Read
Execution
Write
Instruction
j
k
Issue
operands
complete
Result
F6
34+
R2
1
2
3 4
F2
45+
R3
F0
F2
F4
F8
F6
F2
F10
F0
F6
F6
F8
F2
Functional unit status
dest
S1
S2
FU for j
FU for k
Fj?
Fk?
Time
Name
Busy
Op
Fi
Fj
Fk
Qj
Qk
Rj
Rk
Integer
No
7 Mult1
Mult2
No
Add
Divide
Register result status
Clock
F0
F2
F4
F6
F8
F10
F12
...
F30
12
FU
5 6 7 8
6 9
Yes Mult F0 F2 F4 Yes Yes
No
Mult1
Divide
7 9 11 12
8
Yes Div F10 F0 F6 Mult1 No Yes
Read operands for DIV.D?
L.D
L.D
MUL.D
SUB.D
DIV.D
ADD.D

## Slide 32: Scoreboard Example: Cycle 13
Instruction status
Read
Execution
Write
Instruction
j
k
Issue
operands
complete
Result
F6
34+
R2
1
2
3 4
F2
45+
R3
F0
F2
F4
F8
F6
F2
F10
F0
F6
F6
F8
F2
Functional unit status
dest
S1
S2
FU for j
FU for k
Fj?
Fk?
Time
Name
Busy
Op
Fi
Fj
Fk
Qj
Qk
Rj
Rk
Integer
No
6 Mult1
Mult2
No
Add
Divide
Register result status
Clock
F0
F2
F4
F6
F8
F10
F12
...
F30
13
FU
5 6 7 8
6 9
Yes Mult F0 F2 F4 Yes Yes
Mult1 Add
Divide
7 9 11 12
8
Yes Div F10 F0 F6 Mult1 No Yes
Yes Add F6 F8 F2 Yes Yes
13
L.D
L.D
MUL.D
SUB.D
DIV.D
ADD.D

## Slide 33: Scoreboard Example: Cycle 17
Instruction status
Read
Execution
Write
Instruction
j
k
Issue
operands
complete
Result
F6
34+
R2
1
2
3
4
F2
45+
R3
5
6
7
8
F0
F2
F4
6
9
F8
F6
F2
7
9
11
12
F10
F0
F6
8
F6
F8
F2
13
14
16
Functional unit status
dest
S1
S2
FU for j
FU for k
Fj?
Fk?
Time
Name
Busy
Op
Fi
Fj
Fk
Qj
Qk
Rj
Rk
Integer
No
2
Mult1
Yes
Mult
F0
F2
F4
Yes
Yes
Mult2
No
Add
Yes
Add
F6
F8
F2
Yes
Yes
Divide
Yes
Div
F10
F0
F6
Mult1
No
Yes
Register result status
Clock
F0
F2
F4
F6
F8
F10
F12
...
F30
17
FU
Mult1
Add
Divide
Write result of ADD.D? No, WAR hazard
L.D
L.D
MUL.D
SUB.D
DIV.D
ADD.D
?

## Slide 34: Scoreboard Example: Cycle 20
Instruction status
Read
Execution
Write
Instruction
j
k
Issue
operands
complete
Result
F6
34+
R2
1
2
3
4
F2
45+
R3
5
6
7
8
F0
F2
F4
6
9 19 20
F8
F6
F2
7
9
11
12
F10
F0
F6
8
F6
F8
F2
13
14
16
Functional unit status
dest
S1
S2
FU for j
FU for k
Fj?
Fk?
Time
Name
Busy
Op
Fi
Fj
Fk
Qj
Qk
Rj
Rk
Integer
No
Mult1
Mult2
No
Add
Yes
Add
F6
F8
F2
Yes
Yes
Divide
Yes
Div
F10
F0
F6
Yes
Yes
Register result status
Clock
F0
F2
F4
F6
F8
F10
F12
...
F30
20
FU
Add
Divide
No
L.D
L.D
MUL.D
SUB.D
DIV.D
ADD.D

## Slide 35: Scoreboard Example: Cycle 21
Instruction status
Read
Execution
Write
Instruction
j
k
Issue
operands
complete
Result
F6
34+
R2
1
2
3
4
F2
45+
R3
5
6
7
8
F0
F2
F4
6
9 19 20
F8
F6
F2
7
9
11
12
F10
F0
F6
8 21
F6
F8
F2
13
14
16
Functional unit status
dest
S1
S2
FU for j
FU for k
Fj?
Fk?
Time
Name
Busy
Op
Fi
Fj
Fk
Qj
Qk
Rj
Rk
Integer
No
Mult1
Mult2
No
Add
Yes
Add
F6
F8
F2
Yes
Yes
Divide
Yes
Div
F10
F0
F6
Yes
Yes
Register result status
Clock
F0
F2
F4
F6
F8
F10
F12
...
F30
21
FU
Add
Divide
No
L.D
L.D
MUL.D
SUB.D
DIV.D
ADD.D

## Slide 36: Scoreboard Example: Cycle 22
Instruction status
Read
Execution
Write
Instruction
j
k
Issue
operands
complete
Result
F6
34+
R2
1
2
3
4
F2
45+
R3
5
6
7
8
F0
F2
F4
6
9 19 20
F8
F6
F2
7
9
11
12
F10
F0
F6
8 21
F6
F8
F2
13
14
16 22
Functional unit status
dest
S1
S2
FU for j
FU for k
Fj?
Fk?
Time
Name
Busy
Op
Fi
Fj
Fk
Qj
Qk
Rj
Rk
Integer
No
Mult1
Mult2
No
Add
No
40 Divide
Yes
Div
F10
F0
F6
Yes
Yes
Register result status
Clock
F0
F2
F4
F6
F8
F10
F12
...
F30
22
FU
Divide
No
L.D
L.D
MUL.D
SUB.D
DIV.D
ADD.D

## Slide 37: Scoreboard Example: Cycle 61
Instruction status
Read
Execution
Write
Instruction
j
k
Issue
operands
complete
Result
F6
34+
R2
1
2
3
4
F2
45+
R3
5
6
7
8
F0
F2
F4
6
9 19 20
F8
F6
F2
7
9
11
12
F10
F0
F6
8 21 61
F6
F8
F2
13
14
16 22
Functional unit status
dest
S1
S2
FU for j
FU for k
Fj?
Fk?
Time
Name
Busy
Op
Fi
Fj
Fk
Qj
Qk
Rj
Rk
Integer
No
Mult1
Mult2
No
Add
No
0 Divide
Yes
Div
F10
F0
F6
Yes
Yes
Register result status
Clock
F0
F2
F4
F6
F8
F10
F12
...
F30
61
FU
Divide
No
L.D
L.D
MUL.D
SUB.D
DIV.D
ADD.D

## Slide 38: Scoreboard Example: Cycle 62
Instruction status
Read
Execution
Write
Instruction
j
k
Issue
operands
complete
Result
F6
34+
R2
1
2
3
4
F2
45+
R3
5
6
7
8
F0
F2
F4
6
9
19
20
F8
F6
F2
7
9
11
12
F10
F0
F6
8
21
61
62
F6
F8
F2
13
14
16
22
Functional unit status
dest
S1
S2
FU for j
FU for k
Fj?
Fk?
Time
Name
Busy
Op
Fi
Fj
Fk
Qj
Qk
Rj
Rk
Integer
No
Mult1
No
Mult2
No
Add
No
0
Divide
No
Register result status
Clock
F0
F2
F4
F6
F8
F10
F12
...
F30
62
FU
Instruction
Block done
We have:
  In-oder issue,
  Out-of-order execute and commit
L.D
L.D
MUL.D
SUB.D
DIV.D
ADD.D

## Slide 39: Where have all the transistors gone?
Superscalar (multiple instructions per clock cycle)
Execution
Icache
D
cache
branch
TLB
Intel Pentium III (10M transistors)
2 Bus Intf
Out-Of-Order
SS
Branch prediction (predict outcome of decisions)
3 levels of cache
Out-of-order execution (executing instructions in different order than programmer wrote them)

## Slide 40: Pipelining The Tomasulo’s Algorithm

## Slide 41: The Tomasulo’s Algorithm
From IBM 360/91
Goal: High Performance using a limited number of registers without a special compiler
  4 double-precision FP registers on 360
  Uses register renaming
Why Study a 1966 Computer?
  The descendants of this include: Alpha 21264, HP 8000, MIPS 10000, Pentium III, PowerPC 604, …

## Slide 42: Tomasulo Algorithm
Control & buffers are distributed with Function Units (FU)
  FU buffers called “reservation stations (RS)”
  Contain information about instructions, including operands
  More reservation stations than registers, so can do optimizations compilers can’t
Registers in instructions replaced by values or pointers to reservation stations
  form of register renaming
  avoids WAR, WAW hazards
Results to FU from RS, not through registers (equivalent of forwarding). A Common Data Bus (CDB) broadcasts results to all FUs (their RSes)
Loads and Stores treated as FUs with RSes as well

## Slide 43: Tomasulo Organization
FP adders
Add1
Add2
Add3
FP multipliers
Mult1
Mult2
From Mem
FP Registers
Reservation
Stations
Common Data Bus (CDB)
To Mem
FP Op
Queue
Load Buffers
Store
Buffers
Load1
Load2
Load3
Load4
Load5
Load6
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 44: Reservation Station Components
Busy: Indicates reservation station or FU is busy
Op: Operation to perform in the unit (e.g., + or –)
Vj, Vk: Value of Source operands
Qj, Qk: Reservation stations producing source registers (value to be written)
  Note: Qj,Qk=0 => ready
A: effective address
Tomasulo Organization

## Slide 45
Register result status— Qi
  Indicates which functional unit will write each register, if one exists. Blank when no pending instructions that will write that register
Common data bus
  Normal data bus: data + destination (“go to” bus)
  CDB: data + source (“come from” bus)
    64 bits of data + 4 bits of Functional Unit source address
    Write if matches expected Functional Unit (produces result)
    Does the broadcast
Tomasulo Organization

## Slide 46: Three Stages of Tomasulo Algorithm
1. Issue—get instruction from FP Op Queue
  If reservation station free (no structural hazard), control issues the instruction & sends operands (renames registers).
2. Execute—operate on operands (EX)
  When both operands ready then execute; if not ready, watch Common Data Bus for result
3. Write result—finish execution (WB)
  Write on Common Data Bus to all awaiting units; mark reservation station available

## Slide 47: Tomasulo Loop Example
Loop: LD F0, 0(R1)
MULTD F4, F0, F2
SD F4, 0(R1)
SUBI R1, R1, #8
BNEZ R1, Loop
This time assume multiply takes 4 clock cycles in the execution stage
Assume 1st load takes 8 clock cycles (L1 cache miss) in the execution stage, 2nd load takes 1 extra cycle (hit)
Assume store takes 3 cycles in the execution stage
To be clear, will show clocks for SUBI, BNEZ
Show about 2 iterations

## Slide 48: Loop Example using simplified presentation for load/store components
Added Store Buffers
Value of Register used for address, iteration control
Instruction Loop
Iter-
ation
Count
Instruction status:
Exec
Write
ITER
Instruction
j
k
Issue
Comp
Result
Busy
Addr
Qk
1
LD
F0
0
R1
Load1
No
1
MULTD
F4
F0
F2
Load2
No
1
SD
F4
0
R1
Load3
No
2
LD
F0
0
R1
Store1
No
2
MULTD
F4
F0
F2
Store2
No
2
SD
F4
0
R1
Store3
No
Reservation Stations:
S1
S2
RS
Time
Name
Busy
Op
Vj
Vk
Qj
Qk
Code:
Add1
No
LD
F0
0
R1
Add2
No
MULTD
F4
F0
F2
Add3
No
SD
F4
0
R1
Mult1
No
SUBI
R1
R1
#8
Mult2
No
BNEZ
R1
Loop
Register result status
Clock
R1
F0
F2
F4
F6
F8
F10
F12
...
F30
0
80
Qi

## Slide 49: Loop Example Cycle 1

## Slide 50: Loop Example Cycle 2

## Slide 51: Loop Example Cycle 3

## Slide 52: Loop Example Cycle 4
Dispatching SUBI Instruction (not in FP queue)

## Slide 53: Loop Example Cycle 5
And, BNEZ instruction (not in FP queue)

## Slide 54: Loop Example Cycle 6
Notice that F0 never sees Load from location 80

## Slide 55: Loop Example Cycle 7
Register file completely detached from computation
First and Second iteration completely overlapped

## Slide 56: Loop Example Cycle 8

## Slide 57: Loop Example Cycle 9
Load1 completing: who is waiting?
Note: Dispatching SUBI

## Slide 58: Loop Example Cycle 10
Load2 completing: who is waiting?
Note: Dispatching BNEZ
Instruction status:
Exec
Write
ITER
Instruction
j
k
Issue
Comp
Result
Busy
Addr
Qk
1
LD
F0
0
R1
1
9
10
Load1
No
1
MULTD
F4
F0
F2
2
Load2
Yes
72
1
SD
F4
0
R1
3
Load3
No
2
LD
F0
0
R1
6
10
Store1
Yes
80
Mult1
2
MULTD
F4
F0
F2
7
Store2
Yes
72
Mult2
2
SD
F4
0
R1
8
Store3
No
Reservation Stations:
S1
S2
RS
Time
Name
Busy
Op
Vj
Vk
Qj
Qk
Code:
Add1
No
LD
F0
0
R1
Add2
No
MULTD
F4
F0
F2
Add3
No
SD
F4
0
R1
4
Mult1
Yes
Multd
M[80]
R(F2)
SUBI
R1
R1
#8
Mult2
Yes
Multd
R(F2)
Load2
BNEZ
R1
Loop
Register result status
Clock
R1
F0
F2
F4
F6
F8
F10
F12
...
F30
10
64
Qi
Load2
Mult2

## Slide 59: Tomasulo Organization
FP adders
Add1
Add2
Add3
FP multipliers
Mult1
Mult2
From Mem
FP Registers
Reservation
Stations
Common Data Bus (CDB)
To Mem
FP Op
Queue
Load Buffers
Store
Buffers
Load1
Load2
Load3
Load4
Load5
Load6

## Slide 60: Loop Example Cycle 11
Next load in sequence

## Slide 61: Loop Example Cycle 12
Why not issue third multiply?

## Slide 62: Loop Example Cycle 13
Why not issue third store?

## Slide 63: Loop Example Cycle 14
Mult1 completing. Who is waiting?

## Slide 64: Loop Example Cycle 15
Mult2 completing. Who is waiting?

## Slide 65: Loop Example Cycle 16

## Slide 66: Loop Example Cycle 17

## Slide 67: Loop Example Cycle 18

## Slide 68: Loop Example Cycle 19

## Slide 69: Loop Example Cycle 20
Once again: In-order issue, out-of-order execution and out-of-order completion.

## Slide 70: Why can Tomasulo overlap iterations of loops?
Register renaming
  Multiple iterations use different physical destinations for registers (dynamic loop unrolling).
Reservation stations
  Buffer old values of registers - avoiding the WAR stall that we saw in the scoreboard.
Other perspective: Tomasulo builds data flow dependency graph on the fly.

## Slide 71: Tomasulo’s scheme offers 2 major advantages
the distribution of the hazard detection logic
  Distributed reservation stations and the CDB
  If multiple instructions waiting on single result, the instructions can be released simultaneously by broadcast on CDB
  If a centralized register file were used, the units would have to read their results from the registers when register buses are available.
(2) the elimination of stalls for WAW and WAR hazards

## Slide 72: Recall from Pipelining
Pipeline CPI = Ideal pipeline CPI + Structural Stalls + Data Hazard Stalls + Control Stalls
  Ideal pipeline CPI: measure of the maximum performance attainable by the implementation
  Structural hazards: HW cannot support this combination of instructions
  Data hazards: Instruction depends on result of prior instruction still in the pipeline
  Control hazards: Caused by delay between the fetching of instructions and decisions about changes in control flow (branches and jumps)

## Slide 73: Techniques to Reduce Stalls and Increase ILP
Hardware Schemes to Reduce:
  Structural hazards
    Memory: Separate instruction and data memory
    Registers: Write 1st half of cycle and read 2nd half of cycle
Mem
ALU
Reg
Mem
Reg

## Slide 74: Techniques to Reduce Stalls
Hardware Schemes to Reduce:
  Data Hazards
    Forwarding
  Control Hazards
    Moving the branch resolution earlier in the pipeline

## Slide 75: Techniques to Reduce Stalls and Increase ILP
Hardware Schemes to increase ILP:
  Scoreboarding
    Allows out-of-order execution of instructions

## Slide 76: Techniques to Reduce Stalls and Increase ILP
Hardware Schemes to increase ILP:
  Scoreboarding
    Allows out-of-order execution of instructions
Instruction status
Read
Execution
Write
Instruction
j
k
Issue
operands
complete
Result
F6
34+
R2
1
2
3
4
F2
45+
R3
5
6
7
8
F0
F2
F4
6
9
19
20
F8
F6
F2
7
9
11
12
F10
F0
F6
8
21
61
62
F6
F8
F2
13
14
16
22
We have:
  In-oder issue,
  Out-of-order execute and “completion”
L.D
L.D
MUL.D
SUB.D
DIV.D
ADD.D

## Slide 77: Techniques to Reduce Stalls and Increase ILP
Hardware Schemes to reduce stalls
  The Tomasulo’s Algorithm
    Similar to scoreboarding but more advanced (e.g., register renaming)
  Control Hazards
    Dynamic branch prediction (using buffer lookup schemes)

## Slide 78: Techniques to Reduce Stalls and Increase ILP
Software Schemes to Reduce:
  Data Hazards
    Compiler Scheduling: reduce load stalls
Scheduled code with no stalls:
LD Rb,b
LD Rc,c
LD Re,e
DADD Ra,Rb,Rc
LD Rf,f
SD Ra,a
DSUB Rd,Re,Rf
SD Rd,d
Original code with stalls:
LD Rb,b
LD Rc,c
DADD Ra,Rb,Rc
SD Ra,a
LD Re,e
LD Rf,f
DSUB Rd,Re,Rf
SD Rd,d
Stall
Stall

## Slide 79: Techniques to Reduce Stalls and Increase ILP
Software Schemes to Reduce:
  Data Hazards
    Compiler Scheduling: register renaming to eliminate WAW and WAR hazards

## Slide 80: Techniques to Reduce Stalls and Increase ILP
Software Schemes to Reduce:
  Control Hazards
    Branch prediction
      Example : choosing backward branches (loop) as taken and forward branches (if) as not taken
      Tracing Program behaviour

## Slide 81: Techniques to Reduce Stalls and Increase ILP
Software Schemes to Reduce:
  Control Hazards
    Loop unrolling
4n iterations
n iterations
4 iterations
4 iterations

## Slide 82: Techniques to Reduce Stalls and Increase ILP
Software Schemes to Reduce:
  Control Hazards
    Increase loop-level parallelism
for (i=1; i<=100; i=i+1) {
A[i] = A[i] + B[i]; /* S1 */
B[i+1] = C[i] + D[i]; /* S2 */
}
  Can be made parallel by replacing the code with the following:
  A[1] = A[1] + B[1];
  for (i=1; i<=99; i=i+1) {
  B[i+1] = C[i] + D[i];
  A[i+1] = A[i+1] + B[i+1];
  }
  B[101] = C[100] + D[100];