## Slide 1
Lin Gu CSE, HKUST
COMP4611: Design and Analysis of Computer Architectures
Multiprocessors

## Slide 2: Multi-Core Technology
2004 2005 2007
Single Core Dual Core Multi-Core
+ Cache
+
Cache
Cache
Core
4 or more cores
+ Cache
Core
Cache
2 or more cores
+ Cache
2X more
cores
2010 Many Core

## Slide 3
10
100
1
2003
2005
2007
2009
2011
2013
Increasing HW
Threads
HT
Multi-core Era
Scalar and Parallel
Applications
Many-core Era
Massively Parallel
Applications
Multiprocessing within a chip: Many-Core
Intel predicts 100’s of cores on a chip in 2015

## Slide 4: Instruction-level parallelism
Parallelism at the machine-instruction level
The processor can re-order, pipeline instructions, split them into microinstructions, do aggressive branch prediction, etc.
Instruction-level parallelism enabled rapid increases in processor speeds over the last 15 years
Notes: 4

## Slide 5: Why multi-core ?
Difficult to make single-core clock frequencies even higher
Deeply pipelined circuits:
  Heat problems
  Clock problems
  Efficiency (Stall) problems
Doubling issue rates above today’s 3-6 instructions per clock, say to 6 to 12 instructions, is extremely difficult
  issue 3 or 4 data memory accesses per cycle,
  rename and access more than 20 registers per cycle, and
  fetch 12 to 24 instructions per cycle.
Many new applications are multithreaded
A general trend in computer architecture is to shift towards more parallelism through more processors or processor cores
Notes: 5

## Slide 6: What applications benefit from multi-core?
Database servers
Web servers (Web commerce)‏
Multimedia applications
Scientific applications, CAD/CAM
In general, applications with Thread-level parallelism (as opposed to instruction-level parallelism)‏
Each can run on its own core
Notes: 6

## Slide 7: Thread-level parallelism (TLP)‏
This is parallelism on a more coarse scale
Server can serve each client in a separate thread (Web server, database server)‏
A computer game can do AI, graphics, and sound in three separate threads
Single-core superscalar processors cannot fully exploit TLP
Multi-core architectures are the next step in processor evolution: explicitly exploiting TLP
Notes: 7

## Slide 8: Thread-Level Parallelism
Notes: 8

## Slide 9: Introduction
Thread-Level parallelism
  Have multiple program counters
  Uses MIMD model
  Targeted for tightly-coupled shared-memory multiprocessors
For n processors, need n threads
Amount of computation assigned to each thread = grain size
  Threads can be used for data-level parallelism, but the overheads may outweigh the benefit

## Slide 10: How to exploit TLP?
Execute instructions from multiple threads on a single processor
  Coarse-grain, fine-grain, SMT (Simultaneous Multi-Threading)
Execute multiple threads on multiple processors
  “Anything that can be threaded today will map efficiently to multi-core”
Notes: 10

## Slide 11: SMT – Simultaneous Multi-Threading
A variation on multithreading that uses the resources of a multiple-issue, dynamically scheduled processor (superscalar) to exploit both program ILP and thread-level parallelism (TLP)
With register renaming and dynamic scheduling, multiple instructions from independent threads can be issued in one cycle without regard to dependencies among them
Need separate rename tables (ROBs) for each thread
Need the capability to commit from multiple threads (i.e., from multiple ROBs) in one cycle
Notes: 11

## Slide 12: TLP a 4-issue superscalar processor
Thread A
Thread B
Thread C
Thread D
Time
Issue slots
SMT
Fine MT
Coarse MT
Notes: 12

## Slide 13: Core 2 Duo Microarchitecture
Notes: 13

## Slide 14: Without SMT, only a single thread can run at any given time
BTB and I-TLB
Decoder
Trace Cache
Rename/Alloc
Uop queues
Schedulers
Integer
Floating Point
L1 D-Cache D-TLB
uCode ROM
BTB
L2 Cache and Control
Bus
Thread 1: floating point
Notes: 14

## Slide 15: Without SMT, only a single thread can run at any given time
BTB and I-TLB
Decoder
Trace Cache
Rename/Alloc
Uop queues
Schedulers
Integer
Floating Point
L1 D-Cache D-TLB
uCode ROM
BTB
L2 Cache and Control
Bus
Thread 2: integer operation
Notes: 15

## Slide 16: SMT processor: both threads can run concurrently
BTB and I-TLB
Decoder
Trace Cache
Rename/Alloc
Uop queues
Schedulers
Integer
Floating Point
L1 D-Cache D-TLB
uCode ROM
BTB
L2 Cache and Control
Bus
Thread 1: floating point
Thread 2: integer operation
Notes: 16

## Slide 17: But: Can’t simultaneously use the same functional unit
BTB and I-TLB
Decoder
Trace Cache
Rename/Alloc
Uop queues
Schedulers
Integer
Floating Point
L1 D-Cache D-TLB
uCode ROM
BTB
L2 Cache and Control
Bus
Thread 1
Thread 2
This scenario is impossible with SMT on a single core (assuming a single integer unit)‏
IMPOSSIBLE
Notes: 17

## Slide 18: Multi-core: threads can run on separate cores
BTB and I-TLB
Decoder
Trace Cache
Rename/Alloc
Uop queues
Schedulers
Integer
Floating Point
L1 D-Cache D-TLB
uCode ROM
BTB
L2 Cache and Control
Bus
BTB and I-TLB
Decoder
Trace Cache
Rename/Alloc
Uop queues
Schedulers
Integer
Floating Point
L1 D-Cache D-TLB
uCode ROM
BTB
L2 Cache and Control
Bus
Thread 1
Thread 2
Notes: 18

## Slide 19: Multi-core: threads can run on separate cores
BTB and I-TLB
Decoder
Trace Cache
Rename/Alloc
Uop queues
Schedulers
Integer
Floating Point
L1 D-Cache D-TLB
uCode ROM
BTB
L2 Cache and Control
Bus
BTB and I-TLB
Decoder
Trace Cache
Rename/Alloc
Uop queues
Schedulers
Integer
Floating Point
L1 D-Cache D-TLB
uCode ROM
BTB
L2 Cache and Control
Bus
Thread 3
Thread 4
Notes: 19

## Slide 20: Combining Multi-core and SMT
Cores can be SMT-enabled (or not)‏
The different combinations:
  Single-core, non-SMT: standard uniprocessor
  Single-core, with SMT
  Multi-core, non-SMT
  Multi-core, with SMT
The number of SMT threads: 2, 4, or sometimes 8 simultaneous threads
Intel calls them “hyper-threads”
Notes: 20

## Slide 21: SMT Dual-core: all four threads can run concurrently
BTB and I-TLB
Decoder
Trace Cache
Rename/Alloc
Uop queues
Schedulers
Integer
Floating Point
L1 D-Cache D-TLB
uCode ROM
BTB
L2 Cache and Control
Bus
BTB and I-TLB
Decoder
Trace Cache
Rename/Alloc
Uop queues
Schedulers
Integer
Floating Point
L1 D-Cache D-TLB
uCode ROM
BTB
L2 Cache and Control
Bus
Thread 1
Thread 3
Thread 2
Thread 4
Notes: 21

## Slide 22: High-Performance Computing
Notes: 22

## Slide 23: Processor Performance
We have looked at various ways of increasing a single processor performance (Excluding VLSI techniques):
      Pipelining
      ILP
      Superscalars
      Out-of-order execution (Scoreboarding, Tomasulo)
      VLIW
      Cache (L1, L2, L3)
      Interleaved memories
      Compilers (Loop unrolling, branch prediction, etc.)
      RAID
      Etc …
However, quite often even the best microprocessors are not fast enough for certain applications !!!

## Slide 24: Example: How far will ILP go?
Infinite resources and fetch bandwidth, perfect branch prediction and renaming

## Slide 25: When Do We Need High Performance Computing?
Case1
  To do a time-consuming operation in less time
    I am an aircraft engineer
    I need to run a simulation to test the stability of the wings at high speed
    I’d rather have the result in 5 minutes than in 5 days so that I can complete the aircraft final design sooner.

## Slide 26: When Do We Need High Performance Computing?
Case 2
  To do a high number of operations per seconds
    I am an engineer of Amazon.com
    My Web server gets 10,000 hits per seconds
    I’d like my Web server and my databases to handle 10,000 transactions per seconds so that customers do not experience bad delays
      Amazon does “process” several GBytes of data per seconds

## Slide 27: The need for High-Performance Computers some examples
Automotive design:
  Major automotive companies use large systems (500+ CPUs) for:
    CAD-CAM, crash testing, structural integrity and aerodynamics.
  Savings: approx. $1 billion per company per year.
Semiconductor industry:
  Semiconductor firms use large systems (500+ CPUs) for
    device electronics simulation and logic validation
  Savings: approx. $1 billion per company per year.
Airlines:
  System-wide logistics optimization systems on parallel systems.
  Savings: approx. $100 million per airline per year.

## Slide 28: Grand Challenges
10 MB
100 MB
1 GB
10 GB
100 GB
1 TB
100 MFLOPS
1 GFLOPS
10 GFLOPS
100 GFLOPS
1 TFLOPS
2D airfoil
48-hour
weather
oil reservoir
modelling
3D plasma modelling
72-hour
weather
vehicle dynamics
chemical dynamics
pharmaceutical design
structural biology
Computational Performance Requirements
Storage Requirements

## Slide 29: Weather Forecasting
Suppose the whole global atmosphere divided into cells of size 1 km  1 km  1 km to a height of 10 km (10 cells high) - about 5  108 cells.
Suppose each cell calculation requires 200 floating point operations. In one time step, 1011 floating point operations are necessary.
To forecast the weather over 7 days using 1-minute intervals, a computer operating at 1Gflops (109 floating point operations/s) – similar to the Pentium 4 - takes 106 seconds or over 10 days.
To perform calculation in 5 minutes requires a computer operating at 3.4 Tflops (3.4  1012 floating point operations/sec).

## Slide 30: Multiprocessing
Multiprocessing (Parallel Processing): Concurrent execution of tasks (programs) using multiple computing, memory and interconnection resources.
  Use multiple resources to solve problems faster
Provides alternative to faster clock for performance
  Assuming a doubling of effective processor performance every 2 years, 1024-Processor system (assuming linear performance gain) can get you the performance that it would take 20 years for a single-processor system to deliver
Using multiple processors to solve a single problem
  Divide problem into many small pieces
  Distribute these small problems to be solved by multiple processors simultaneously

## Slide 31: Multiprocessing
For the last 30+ years multiprocessing has been seen as the best way to produce orders of magnitude performance gains.
  Double the number of processors, get (theoretically) double performance (less than 2 times the cost).
It turns out that the ability to develop and deliver software for multiprocessing systems induces impediment to wide adoption.

## Slide 32: Amdahl’s Law
A parallel program has a sequential part (e.g., I/O) and a parallel part
  T1 = T1 + (1-)T1
  Tp = T1 + (1-)T1 / p
Therefore:
Speedup(p) = 1 / ( + (1-)/p)
= p / ( p + 1 - )
 1 / 
Example: if a code is 10% sequential (i.e.,  = .10), the speedup will always be lower than 1 + 90/10 = 10, no matter how many processors are used!

## Slide 34: Performance Potential Using Multiple Processors
Amdahl's Law is pessimistic (in this case)
  Let s be the serial part
  Let p be the part that can be parallelized n ways
  Serial: SSPPPPPP
  6 processors: SSP
  P
  P
  P
  P
  P
  Speedup = 8/3 = 2.67
  T(n) =
  As n  , T(n) 
Pessimistic
1
s+p/n
1
s

## Slide 35
10%
20%
30%
40%
50%
60%
70%
80%
90%
99%
0
5
10
15
20
25
Speedup
% Serial
1000 CPUs
16 CPUs
4 CPUs
Amdahl’s Law

## Slide 36: Example

## Slide 37: Performance Potential: Another view
Gustafson view (more widely adopted for multiprocessors)
  Parallel portion increases as the problem size increases
    Serial time fixed (at s)
    Parallel time proportional to problem size (true most of the time)
    Gustafson’s Law: Speedup(N) = N - (N-1)
      N: number of processors,  : weight of non-parallelizable part
Old Serial: SSPPPPPP
6 processors: SSPPPPPP
PPPPPP
PPPPPP
PPPPPP
PPPPPP
PPPPPP
Hypothetical Serial:
SSPPPPPP PPPPPP PPPPPP PPPPPP PPPPPP PPPPPP
  Speedup(6) = (8+5*6)/8 = 4.75
     =? in this calculation?
  Speedup(N) = N(1- ) + ; Speedup'()  !!!!

## Slide 38
0
20
40
60
80
100
10%
20%
30%
40%
50%
60%
70%
80%
90%
99%
% Serial
Speedup
Gustafson-Barsis
Amdhal
Amdahl vs. Gustafson-Barsis

## Slide 39: TOP 5 Most computers in the world – must be multiprocessors
http://www.top500.org/
No | Site Country | # of cores | Manufacturer, Model, Architecture | Rmax (TFlops)
1 | DOE/NNSA/LANL, USA | 129600 | IBM, BladeCenter QS22/LS21 Cluster, PowerXCell 8i 3.2 Ghz / Opteron DC 1.8 GHz , Voltaire Infiniband | 1105
2 | Oak Ridge National Laboratory, USA | 150152 | Cray XT5 QC 2.3 GHz | 1059
3 | NASA/Ames Research Center/NAS, USA | 51200 | SGI Altix ICE 8200EX, Xeon QC 3.0/2.66 GHz | 487
4 | DOE/NNSA/LLNL, USA | 212992 | IBM, eServer Blue Gene Solution | 478
5 | Argonne National Laboratory, USA | 163840 | IBM, Blue Gene/P Solution | 450
Site/Country/Year | # of cores | Manufacturer, Model, Architecture | Rmax (TFlops)
DOE/SC/Oak Ridge National Laboratory | 560640 | Titan - Cray XK7 , Opteron 6274 16C 2.200GHz, Cray Gemini interconnect, NVIDIA K20x | 17590
DOE/NNSA/LLNL | 1572864 | Sequoia - BlueGene/Q, Power BQC 16C 1.60 GHz | 16324
RIKEN Advanced Institute for Computational Science (AICS) | 705024 | K computer, SPARC64 VIIIfx 2.0GHz, Tofu interconnect | 10510
DOE/SC/Argonne National Laboratory | 786432 | Mira - BlueGene/Q, Power BQC 16C 1.60GHz | 8162
Forschungszentrum Juelich (FZJ) | 393216 | JUQUEEN - BlueGene/Q, Power BQC 16C 1.600GHz, Custom Interconnect | 4141
2008
Nov. 2012

## Slide 40: A Few Types
Symmetric multiprocessors (SMP)
  Small number of cores
  Share single memory with uniform memory latency
Distributed shared memory (DSM)
  Memory distributed among processors
  Non-uniform memory access/latency (NUMA)
  Processors connected via direct (switched) and non-direct (multi-hop) interconnection networks

## Slide 41: Flynn’s Taxonomy of Computing
SISD (Single Instruction, Single Data):
  Typical uniprocessor systems that we’ve studied throughout this course.
  Uniprocessor systems can time share and still be SISD.
SIMD (Single Instruction, Multiple Data):
  Multiple processors simultaneously executing the same instruction on different data.
  Specialized applications (e.g., image processing).
MIMD (Multiple Instruction, Multiple Data):
  Multiple processors autonomously executing different instructions on different data.
  Keep in mind that the processors are working together to solve a single problem.
  This is a more general form of multiprocessing, and can be used in numerous applications

## Slide 42: SIMD Systems
Processor
Memory
P
M
P
M
P
M
P
M
P
M
P
M
P
M
P
M
P
M
P
M
P
M
P
M
P
M
P
M
P
M
P
M
von Neumann Computer
Some Interconnection Network
One control unit
Lockstep
All Ps do the same or nothing

## Slide 43: MIMD Architecture
43
Unlike SIMD, MIMD computer works asynchronously.
    Shared memory (tightly coupled) MIMD
    Distributed memory (loosely coupled) MIMD
Processor
A
Processor
B
Processor
C
Data Input
stream A
Data Input
stream B
Data Input
stream C
Data Output
stream A
Data Output
stream B
Data Output
stream C
Instruction
Stream A
Instruction
Stream B
Instruction
Stream C

## Slide 44: MIMD Shared Memory Systems
Interconnection Networks
M
M
M
M
P
P
P
P
P
P
C
P
C
P
C
P
C
M
M
M
M
Global Memory
P
C
P
C
P
C
One global memory
Cache Coherence
All Ps have equal access to memory

## Slide 45: Cache Coherent NUMA
Interconnection Network
M
C
P
M
C
P
M
C
P
M
C
P
Each P has part of the shared memory
Non uniform memory access

## Slide 46: MIMD Distributed Memory Systems
Interconnection Networks
M
M
M
M
P
P
P
P
1110 1111
1010 1011
0110 0111
0010 0011
1100 1101
1000 1001
0100 0101
0000 0001
LAN/WAN
No shared memory
Message Passing
Topology

## Slide 47: Cluster Architecture
M
C
P
I/O
OS
M
C
P
I/O
OS
M
C
P
I/O
OS
Middleware
Programming Environment
Interconnection Network
Home cluster

## Slide 48: Grids
Internet
Dependable, consistent, pervasive, and inexpensive access to high end computing.
Geographically distributed platforms.

## Slide 49: SIMD
Notes: 49

## Slide 50
50
SIMD Parallel Computing
It can be a stand-alone multiprocessor
Or
Embedded in a single processor for specific applications (MMX)

## Slide 51: SIMD Applications
51
  Database, image processing, and signal processing.
  Image processing maps very naturally onto SIMD systems.
    Each processor (Execution unit) performs operations on a single pixel or neighborhood of pixels.
    The operations performed are fairly straightforward and simple.
    Data could be streamed into the system and operated on in real-time or close to real-time.

## Slide 52: SIMD Operations
52
Image processing on SIMD systems.
  Sequential pixel operations take a very long time to perform.
    A 512x512 image would require 262,144 iterations through a sequential loop with each loop executing 10 instructions. That translates to 2,621,440 clock cycles (if each instruction is a single cycle) plus loop overhead.
512x512 image
Each pixel is operated on
sequentially one after
another.

## Slide 53: SIMD Operations
53
Image processing on SIMD systems.
  On a SIMD system with 64x64 processors (e.g., very simple ALUs) the same operations would take 640 cycles, where each processor operates on an 8x8 set of pixels plus loop overhead.
512x512 image
Each processor operates on
an 8x8 set of pixels in
parallel.
Speedup due to parallelism:
2,621,440/640 = 4096 =
64x64 (number of proc.)
loop overhead ignored.

## Slide 54: SIMD Operations
54
Image processing on SIMD systems.
  On a SIMD system with 512x512 processors (which is not unreasonable on SIMD machines) the same operation would take 10 cycles.
512x512 image
Each processor operates on
a single pixel in parallel.
Speedup due to parallelism:
2,621,440/10 = 262,144 =
512x512 (number of proc.)!
Notice no loop overhead!

## Slide 55: Pentium MMX MultiMedia eXtentions
55
57 new instructions
Eight 64-bit wide MMX registers
First available in 1997
Supported on:
  Intel Pentium-MMX, Pentium II, Pentium III, Pentium IV
  AMD K6, K6-2, K6-3, K7 (and later)
  Cyrix M2, MMX-enhanced MediaGX, Jalapeno (and later)
Gives a large speedup in many multimedia applications

## Slide 56: MMX SIMD Operations
56
Example: consider an image pixel data represented as bytes.
  with MMX, eight of these pixels can be packed together in a 64-bit quantity and moved into an MMX register
  MMX instruction performs the arithmetic or logical operation on all eight elements in parallel
PADD(B/W/D): Addition
PADDB MM1, MM2
adds 64-bit contents of MM2 to MM1,
byte-by-byte any carries generated
are dropped, e.g., byte A0h + 70h = 10h
PSUB(B/W/D): Subtraction

## Slide 57: MMX: Image Dissolve Using Alpha Blending
57
Example: MMX instructions speed up image composition
A flower will dissolve a swan
Alpha (a standard scheme) determines the intensity of the flower
The full intensity, the flower’s 8-bit alpha value is FFh, or 255
The equation below calculates each pixel:
Result_pixel =Flower_pixel *(alpha/255) + Swan_pixel * [1-(alpha/255)]
For alpha 230, the resulting pixel is 90% flower and 10% swan

## Slide 58: SIMD Multiprocessing
58
Traditional vector computers are typical SIMD systems
In the late 80s and early 90s, many SIMD machines were commercially available (e.g., Connection machine has 64K ALUs, and MasPar has 16K ALUs)
GPU revives the SIMD computation, and is widely used in high-performance computers
SPMD—Single Program, Multiple Data

## Slide 59: Cache Coherence
Notes: 59

## Slide 60: Shared Memory Multiprocessor
60
Memory
Disk & other IO
Registers
Caches
Processor
Registers
Caches
Processor
Registers
Caches
Processor
Registers
Caches
Processor
Interconnect
Memory: centralized with Uniform Memory Access time (“uma”) and bus interconnect, I/O
Examples: Sun Enterprise 6000, SGI Challenge, Intel SystemPro
Notes: 60

## Slide 61: Shared Memory Programming Model
61
Process
Process
System
X
load(X)
store(X)
Processor
Memory
Shared variable

## Slide 62: Shared Memory Model
62
Virtual address spaces for a collection of processes communicating via shared addresses
Machine physical address space
Shared portion of address space
Private portion of address space
Pn private
Common physical addresses
P2 private
P1 private
P0 private
Store
Load

## Slide 63: Cache Coherence Problem
63
Processor 3 does not see the value written by processor 0
X:42
R: X
$
MEM
P0
$
P1
$
P2
$
P3
X:42
X:17
W: X = 17
R: X
X:42

## Slide 64: Write Through does not help
64
Processor 3 sees 42 in cache (does not get the correct value (17) from memory.
X:42
R: X
$
MEM
P0
$
P1
$
P2
$
P3
X:42
X:17
W: X = 17
R: X
X:42
X:17
R: X

## Slide 65: Why Don’t Processors Share Cache
65
Advantages
Cache placement identical to single cache
  only one copy of any cached block
Disadvantages
Bandwidth limitation
P
1
Switch
Main memory
P
n
(Interleaved)
(Interleaved)
First-level $
Shared Cache
Notes: 65

## Slide 66: Cache Coherence
Coherence
  All reads by any processor must return the most recently written value
  Writes to the same location by any two processors are seen in the same order by all processors
Consistency
  When a written value will be returned by a read
  If a processor writes location A followed by location B, any processor that sees the new value of B must also see the new value of A

## Slide 67: Enforcing Coherence
Coherent caches provide:
  Migration: movement of data
  Replication: multiple copies of data
Cache coherence protocols
  Directory based
    Sharing status of each block kept in one location
  Snooping
    Each core tracks sharing status of each block

## Slide 68: Distributed Cache: Snoopy Cache-Coherence Protocols
68
Bus is a broadcast medium & caches know what they have
  bus protocol: arbitration, command/addr, data
  => Every device observes every transaction
State
Address
Data

## Slide 69: Snooping Cache Coherency
69
Cache Controller “snoops” all transactions on the shared bus
  A transaction is a relevant transaction if it involves a cache block currently contained in this cache
    take action to ensure coherence (invalidate, update, or supply value)

## Slide 70
Hardware Cache Coherence
write-invalidate
write-update (also called distributed write)
P
P
X -> X’
invalidate -->
X -> Inv
P
X -> Inv
. . . . .
memory
P
P
X -> X’
update -->
X -> X’
P
X -> X’
. . . . .
memory

## Slide 71: An Example Snoopy Protocol
Invalidation protocol, write-back cache
  “invalidate” request on memory bus
Each cache block is in one state (track these):
  Shared : multiple caches potentially have copies of the block; the block can be read
  OR Modified : this cache has the only copy of the block; the block is writeable and dirty
  OR Invalid : the block contains no valid data

## Slide 72: An Example Snoopy Protocol
CPU | Read hit | Shared, modified | Normal hit | Read hit in cache
CPU | Read miss | Invalid | Normal miss | Place read miss on bus
CPU | Read miss | Shared | Replacement | Place read miss on bus
CPU | Read miss | Modified | Replacement | Write back block, then place read miss on bus
Source Request State of block Cache action Function and explanation

## Slide 73: Snoopy Coherence Protocols
Write invalidate
  On write, invalidate all other copies
  Use bus itself to serialize
    Write cannot complete until bus access is obtained
Write update
  On write, update all copies

## Slide 74: An Example Snoopy Protocol
CPU | Write hit | Modified | Normal hit | Write data in cache
CPU | Write hit | Shared | Coherence | Place invalidate on bus
CPU | Write miss | Invalid | Normal miss | Place write miss on bus
CPU | Write miss | Shared | Replacement | Place write miss on bus
CPU | Write miss | Modified | Replacement | Write back block, then place write miss on bus
Source Request State of block Cache action Function and explanation

## Slide 75: An Example Snoopy Protocol
Bus | Read miss | Shared | No action | Allow memory to service the miss
Bus | Read miss | Modified | Coherence | Place cache block on bus
Bus | Invalidate | Shared | Coherence | Invalidate the block
Bus | Write miss | Shared | Coherence | Invalidate the block
Bus | Write miss | Modified | Replacement | Write back block, invalidate the block
Source Request State of block Cache action Function and explanation

## Slide 76: Snoopy Coherence Protocols
Locating an item when a read miss occurs
  In write-back cache, the updated value must be sent to the requesting processor
Cache lines marked as shared or exclusive/modified
  Only writes to shared lines need an invalidate broadcast
    After this, the line is marked as exclusive

## Slide 77: Snoopy Coherence Protocols

## Slide 78: Snoopy Coherence Protocols

## Slide 79: Snoopy-Cache State Machine
State machine for CPU requests for each cache block and for bus requests for each cache block
Place read miss on bus
Invalid
Shared
(read only)
Exclusive
(modified)
CPU: Read
CPU: Write miss
CPU: Read hit
Place Write Miss on bus
CPU: read miss
Write back block, Place read miss on bus
CPU Write miss
Place Write Miss on Bus
CPU: Read miss
Place read miss
on bus
CPU: Write Miss
Write back data,
Place write miss on bus
CPU: Write hit
CPU: Read hit
Write Back
Block
Bus: Write miss
Bus:Read miss
Write Back Block
Bus: Invalidate
CPU: Write hit Place invalidate on Bus
Bus: Write miss

## Slide 80: Snoopy Coherence Protocols
Complications for the basic MSI protocol:
  Operations are not atomic
    E.g. detect miss, acquire bus, receive a response
    Creates possibility of deadlock and races
    One solution: processor that sends invalidate can hold bus until other processors receive the invalidate
Extensions:
  Add exclusive state to indicate clean block in only one cache (MESI protocol)
    Prevents needing to write invalidate on a write
  Owned state

## Slide 81: Performance
Coherence influences cache miss rate
  Coherence misses
    True sharing misses
      Write to shared block (transmission of invalidation)
      Read an invalidated block
    False sharing misses
      Read an unmodified word in an invalidated block

## Slide 82: Performance Study: Commercial Workload

## Slide 83: Performance Study: Commercial Workload

## Slide 84: Performance Study: Commercial Workload

## Slide 85: Performance Study: Commercial Workload

## Slide 86: Revisit: Coherency Solutions
Snooping Solution (Snoopy Bus):
  Send all requests for data to all caches
  Requires broadcast, works well with bus (natural broadcast medium)
  Dominates for small scale machines (most of the market)
Directory-Based Schemes
  Keep track of what is being shared in 1 centralized place (logically)
  Send point-to-point requests to processors via network
  Scales better than Snooping

## Slide 87: Directory Protocols
Directory keeps track of every block
  Which caches have each block
  Dirty status of each block
Implement in shared L3 cache
  Keep bit vector of size = # cores for each block in L3
  Not scalable beyond shared L3
Implement in a distributed fashion:

## Slide 88: Directory Protocols
For each block, maintain state:
  Shared
    One or more nodes have the block cached, value in memory is up-to-date
    Set of node IDs
  Uncached
  Modified
    Exactly one node has a copy of the cache block, value in memory is out-of-date
    Owner node ID
Directory maintains block states and sends invalidation messages

## Slide 89: Messages

## Slide 90: Directory Protocols

## Slide 91: Directory Protocols
For uncached block:
  Read miss
    Requesting node is sent the requested data and is made the only sharing node, block is now shared
  Write miss
    The requesting node is sent the requested data and becomes the sharing node, block is now exclusive
For shared block:
  Read miss
    The requesting node is sent the requested data from memory, node is added to sharing set
  Write miss
    The requesting node is sent the value, all nodes in the sharing set are sent invalidate messages, sharing set only contains requesting node, block is now exclusive

## Slide 92: Directory Protocols
For exclusive block:
  Read miss
    The owner is sent a data fetch message, block becomes shared, owner sends data to the directory, data written back to memory, sharers set contains old owner and requestor
  Data write back
    Block becomes uncached, sharer set is empty
  Write miss
    Message is sent to old owner to invalidate and send the value to the directory, requestor becomes new owner, block remains exclusive

## Slide 93: Synchronization
Basic building blocks:
  Atomic exchange
    Swaps register with memory location
  Test-and-set
    Sets under condition
  Fetch-and-increment
    Reads original value from memory and increments it in memory
  Requires memory read and write in uninterruptable instruction
  load linked/store conditional
    If the contents of the memory location specified by the load linked are changed before the store conditional to the same address, the store conditional fails

## Slide 94: Implementing Locks
Spin lock
  If no coherence:
DADDUI R2,R0,#1
lockit: EXCH R2,0(R1) ;atomic exchange
BNEZ R2,lockit ;already locked?
  If coherence:
lockit: LD R2,0(R1) ;load of lock
BNEZ R2,lockit ;not available-spin
DADDUI R2,R0,#1 ;load locked value
EXCH R2,0(R1) ;swap
BNEZ R2,lockit ;branch if lock wasn’t 0

## Slide 95: Implementing Locks
Advantage of this scheme: reduces memory traffic

## Slide 96: Models of Memory Consistency
Processor 1:
A=0
…
A=1
if (B==0) …
Processor 2:
B=0
…
B=1
if (A==0) …
Should be impossible for both if-statements to be evaluated as true
  Delayed write invalidate?
Sequential consistency:
  Result of execution should be the same as long as:
    Accesses on each processor were kept in order
    Accesses on different processors were arbitrarily interleaved

## Slide 97: Implementing Locks
To implement, delay completion of all memory accesses until all invalidations caused by the access are completed
  Reduces performance!
Alternatives:
  Program-enforced synchronization to force write on processor to occur before read on the other processor
    Requires synchronization object for A and another for B
      “Unlock” after write
      “Lock” after read

## Slide 98: Relaxed Consistency Models
Rules:
  X → Y
    Operation X must complete before operation Y is done
    Sequential consistency requires:
      R → W, R → R, W → R, W → W
  Relax W → R
    “Total store ordering”
  Relax W → W
    “Partial store order”
  Relax R → W and R → R
    “Weak ordering” and “release consistency”

## Slide 99: Relaxed Consistency Models
Consistency model is multiprocessor specific
Programmers will often implement explicit synchronization
Speculation gives much of the performance advantage of relaxed models with sequential consistency
  Basic idea: if an invalidation arrives for a result that has not been committed, use speculation recovery

## Slide 100: Interconnect
Notes: 100

## Slide 101: Limits of Bus-Based Shared Memory
101
I/O
MEM
MEM
° ° °
PROC
cache
PROC
cache
° ° °
Assume:
1 GHz processor
=> 4 GB/s inst BW per processor (32-bit)
=> 1.2 GB/s data BW at 30% load-store
Suppose 98% inst hit rate and 95% data hit rate
=> 80 MB/s inst BW per processor
=> 60 MB/s data BW per processor
140 MB/s combined BW
Assuming 1 GB/s bus bandwidth
\ 8 processors will saturate the memory bus
5.2 GB/s
140 MB/s
Notes: 101

## Slide 102: Coherence Protocols: Extensions
Shared memory bus and snooping bandwidth is bottleneck for scaling symmetric multiprocessors
  Duplicating tags
  Place directory in outermost cache
  Use crossbars or point-to-point networks with banked memory

## Slide 103: Coherence Protocols
AMD Opteron:
  Memory directly connected to each multicore chip in NUMA-like organization
  Implement coherence protocol using point-to-point links
  Use explicit acknowledgements to order operations

## Slide 104: Scalable Shared Memory Architectures Crossbar Switch
104
Mem
Mem
Mem
Mem
Cache
P
I/O
Cache
P
I/O
Used in SUN entreprise 10000

## Slide 105: Scalable Shared Memory Architectures
105
Used in IBM SP Multiprocessor
0
1
1
P
0
P
1
P
2
P
3
P
4
P
5
P
6
P
7
M
0
M
1
M
2
M
3
M
4
M
5
M
6
M
7
000
001
010
011
100
101
110
111

## Slide 106: Approaches to Building Parallel Machines
106
P
1
Switch
Main memory
P
n
(Interleaved)
(Interleaved)
First-level $
P
1
$
Inter
connection network
$
P
n
Mem
Mem
P
1
$
Inter
connection network
$
P
n
Mem
Mem
Shared Cache
Distributed Memory
Scale

## Slide 107: Scales of Multiprocessors
Small size multiprocessors ( < 10 processors)
  Use shared memory with shared bus
  Not expensive
  Commercially available, and highly used as small servers
Medium size multiprocessors ( < 64 processors)
  Use shared memory with crossbar switch
  Commercially available
  Used as high-end servers and computing engines
Large size multiprocessors ( > 64 processors)
  Use distributed memory with custom-made interconnection network
  Very powerful computing machines
  Extremely expensive