## Slide 1: Pipelining Exploiting instruction-Level Parallelism Lin Gu CSE, HKUST
COMP4611: Design and Analysis of Computer Architectures

## Slide 2: Instruction-Level Parallelism (ILP)
Pipelining increases performance by overlapping the execution of independent instructions or independent operations in instructions—Instruction-Level Parallelism
The CPI of a pipeline is given by:
Pipeline CPI = Ideal Pipeline CPI + Structural Stalls + RAW Stalls
+ WAR Stalls + WAW Stalls + Control Stalls
The amount of parallelism in an instruction sequence is limited by the hardware resources and the dependence among instructions.

## Slide 3: A Model of an Ideal Processor
  No structural hazards
  Register renaming—infinite registers and all WAW & WAR hazards avoided
  Processor with perfect prediction
    Branch prediction—perfect; no mispredictions
    Jump prediction—all jumps perfectly predicted
  Also, perfect memory address alias analysis, perfect caches
There are only true data dependences left!
I: add r1,r2,r3
J: sub r4,r1,r3

## Slide 4: Upper Bound on ILP
Integer: 18 - 60
FP: 75 - 150

## Slide 5: More Realistic: Branch Impact
Window: 2000 instructions
Max 64 instr/cycle issue

## Slide 6: Renaming Register impact
Window: 2000 instructions
Max 64 instr/cycle issue
Tournament branch predictor

## Slide 7: Window Impact
Max 64 instr/cycle issue
Tournament branch predictor

## Slide 8: How do we take advantage of this large number of ILP
Superscalar processors
VLIW (Very Long Instruction Word) processors
All high-performance modern processors (e.g., Pentium, Sparc, Itanium) use one of the above techniques.
Let’s first look at a more sophisticated pipeline where more instructions travel in it and the instructions have a diverse range of latencies…

## Slide 9
Multicycle Operations in the EX Stage

## Slide 10: Multicycle Operations in the EX Stage
Completion of MIPS EX stage floating point arithmetic operations in one or two cycles is impractical since it requires:
    A much longer CPU clock cycle, and/or
    An enormous amount of logic.
Instead, the floating-point pipeline will allow for a longer latency.
Floating-point operations have the same pipeline stages as the integer instructions with the following differences:
  The EX cycle may be repeated many times as needed.
  There may be multiple floating-point functional units.
  A stall will occur if the instruction to be issued causes either a structural hazard for the functional unit or a data hazard.

## Slide 11
Extending The MIPS Pipeline to Handle Floating-Point
Operations:
Adding Non-Pipelined Floating Point Units
(In Appendix C)

## Slide 12
The extended pipeline system with some pipelined functional units and some unpipelined functional units
(In Appendix C)

## Slide 13: Floating Point/Multicycle Pipelining in MIPS
The latency of functional units is defined as the number of intervening cycles between an instruction producing the result and the instruction that uses the result (usually equals stall cycles with forwarding used).
The initiation or repeat interval is the number of cycles that must elapse between issuing an instruction of a given type.

## Slide 14
Extending The MIPS Pipeline:
Multiple Outstanding Floating Point Operations
Latency = 0
Initiation Interval = 1
Latency = 3
Initiation Interval = 1
Pipelined
Latency = 6
Initiation Interval = 1
Pipelined
Latency = 24
Initiation Interval = 25
Non-pipelined
Integer Unit
Floating Point (FP)/Integer Multiply
FP/Integer Divider
IF
ID
WB
MEM
FP Adder
EX
Hazards:
RAW, WAW possible
WAR Not Possible
Structural: Possible
Control: Possible

## Slide 15: Latencies and Initiation Intervals For Functional Units
Functional Unit Latency Initiation Interval
Integer ALU 0 1
Data Memory 1 1
(Integer and FP Loads)
FP add 3 1
FP multiply 6 1
(also integer multiply)
FP divide 24 25
(also integer divide)
Latency usually equals stall cycles when full forwarding is used

## Slide 16: Pipeline Characteristics With FP
Instructions are still processed in-order in IF, ID, EX at the rate of one instruction per cycle, ideally.
Longer RAW hazard stalls likely due to long FP latencies.
Structural hazards possible due to varying instruction times and FP latencies:
  FP unit may not be available; divide in this case.
  MEM, WB reached by several instructions simultaneously.
WAW hazards can occur since it is possible for instructions to reach WB out-of-order.
WAR hazards impossible, since register reads occur in-order in ID.
Instructions are allowed to complete out-of-order requiring special measures to enforce precise exceptions.

## Slide 17: FP Operations Pipeline Timing
All above instructions are assumed independent
IF
ID
A1
A4
A3
A2
MEM
WB
IF
ID
M1
M6
M7
M2
M3
M4
M5
MEM
WB
IF
ID
MEM
EX
WB
IF
ID
MEM
EX
WB
MUL.D
L.D
ADD.D
S.D
CC 1
CC 2
CC 3
CC 8
CC 9
CC 4
CC 5
CC 6
CC 7
CC 10
CC 11

## Slide 18: FP RAW Hazard and Stalls (with full data forwarding in place)
IF
MEM
ID
EX
WB
IF
ID
M1
M6
M7
M2
M3
M4
M5
MEM
WB
IF
ID
A1
A4
A3
A2
MEM
WB
CC 1
CC 2
CC 3
CC 8
CC 9
CC 4
CC 5
CC 6
CC 7
CC 10
CC 11 CC12 CC13 CC14 CC15 CC16 CC17 CC18
IF
ID
MEM
EX
WB
STALL
STALL
STALL
STALL
STALL
STALL
STALL
STALL
STALL
STALL
STALL
STALL
STALL
STALL
STALL
STALL
STALL
L.D F4, 0(R2)
MUL.D F0, F4, F6
ADD.D F2, F0, F8
S.D F2, 0(R2)
Third stall due
to structural hazard
in MEM stage
6 stall cycles which equals latency of FP add functional unit

## Slide 19: Dealing with RAW
Longer latency pipes cause the frequency of RAW stalls to go up.
More complicated forwarding
Frequent compiler scheduling
More advanced techniques to be covered later

## Slide 20: FP Code Structural Hazards Example
IF
ID
A1
A4
A3
A2
MEM
WB
IF
ID
M1
M6
M7
M2
M3
M4
M5
MEM
WB
IF
ID
MEM
EX
WB
IF
ID
MEM
EX
WB
MULTD F0, F4, F6
LD F2, 0(R2)
ADDD F2, F4, F6
CC 1
CC 2
CC 3
CC 8
CC 9
CC 4
CC 5
CC 6
CC 7
CC 10
CC 11
IF
ID
MEM
EX
WB
IF
ID
MEM
EX
WB
IF
ID
MEM
EX
WB
. . . (integer)
. . . (integer)
. . . (integer)
. . . (integer)

## Slide 21: Dealing with Structural Hazards
Option 1: Track the use of the write port; stall instruction in ID if there is a collision.
  Maintain the property of stalling instruction only in ID.
  Extra HW (e.g., write conflict logic).
Option 2: Stall a conflict instruction at MEM/WB entry.
  Flexible in choose a instruction to be stalled (give priority to the longest latency).
  Complicates pipeline control (stalls can arise from two places).
    Stalling at the entrance of MEM would probably cause EX, Mx, Ax, DIV to back up

## Slide 22: Dealing with WAW Hazards
Option 1: Delay LD until ADDD enter MEM
Option 2: Stamp out the result of ADDD.
WAW
Hazards

## Slide 23: Deeper pipelines

## Slide 24: Superpipelining: MIPS R4000 Integer pipeline
8 Stage Pipeline:
  IF–first half of fetching of instruction; PC selection happens here as well as initiation of instruction cache access.
  IS–second half of access to instruction cache.
  RF–instruction decode and register fetch, hazard checking and also instruction cache hit detection

## Slide 25: Superpipelining: MIPS R4000 Integer pipeline
8 Stage Pipeline:
  EX–execution, which includes effective address calculation, ALU operation, and branch target computation and condition evaluation.
  DF–data fetch, first half of access to data cache.
  DS–second half of access to data cache.
  TC–tag check, determine whether the data cache access hit.
  WB–write back for loads and register-register operations.
8 Stages: How many delayed branch slots does the pipeline need?
  3 slots (branch outcome decided at EX)
  1 delayed slot instruction plus 2 predict-not-taken instructions

## Slide 26: Stalls in MIPS R4000
IF
IS
IF
RF
IS
IF
EX
RF
IS
IF
DF
EX
RF
IS
IF
DS
DF
EX
RF
IS
IF
TC
DS
DF
EX
RF
IS
IF
WB
TC
DS
DF
EX
RF
IS
IF
TWO Cycle
Load Latency
IF
IS
IF
RF
IS
IF
EX
RF
IS
IF
DF
EX
RF
IS
IF
DS
DF
EX
RF
IS
IF
TC
DS
DF
EX
RF
IS
IF
WB
TC
DS
DF
EX
RF
IS
IF
THREE Cycle
Branch Latency
(conditions evaluated
during EX phase)
Delay slot plus two instructions
from the not-taken branch

## Slide 27: Instruction Level Parallelism Loop Unrolling

## Slide 28: Pipelining and Exploiting Instruction-Level Parallelism (ILP)
A basic instruction block is a straight-line code sequence with no branches in, except at the entry point, and no branches out except at the exit point of the sequence .
The amount of parallelism in a basic block is limited by instruction dependence present and size of the basic block.
In a typical integer code, dynamic branch frequency is about 15% (average basic block size of 7 instructions).

## Slide 29: Increasing Instruction-Level Parallelism
A common way to increase parallelism among instructions is to exploit parallelism among iterations of a loop
  (i.e Loop Level Parallelism, LLP).
This is accomplished by unrolling the loop either statically by the compiler, or dynamically by hardware, which increases the size of the basic block present.
In this loop every iteration can overlap with any other iteration. Overlap within each iteration is minimal.
for (i=1000; i>0; i=i-1;)
x[i] = x[i] + s;

## Slide 30: MIPS Loop Unrolling Example
For the loop:
for (i=1000; i>0; i--) x[i] = x[i] + s;
The straightforward MIPS assembly code is given by:
Loop: L.D F0, 0 (R1) ;F0=array element
ADD.D F4, F0, F2 ;add scalar in F2
S.D F4, 0(R1) ;store result
SUBI R1, R1, # 8 ;decrement pointer 8 bytes
BNZ R1,Loop ; branch R1!=zero
R1 is initially the address of the element with highest address.
BNZ R1, Loop is a simplification saying x[0]’s address is 0.

## Slide 31: FP Loop: Where are the Hazards?
Loop: LD F0,0(R1) ;F0=vector element
ADDD F4,F0,F2 ;add scalar from F2
SD 0(R1),F4 ;store result
SUBI R1,R1,8 ;decrement pointer 8B (DW)
BNZ R1,Loop ;branch R1!=zero
Instruction Instruction Latency in producing result using result clock cycles
FP ALU op Another FP ALU op 3
FP ALU op Store double 2
Load double FP ALU op 1
Load double Store double 0
Integer op Integer op 0
Where are the stalls?

## Slide 32: FP Loop Showing Stalls
9 clock cycles per loop iteration.
Rewrite code to minimize stalls?
1 Loop: LD F0,0(R1) ;F0=vector element
2 stall ;stall one cycle between LD and FP ALU op
3 ADDD F4,F0,F2 ;add scalar in F2
4 stall ;stall two cycles between FP ALU op and SD
5 stall
6 SD 0(R1),F4 ;store result
7 SUBI R1,R1,8 ;decrement pointer 8B (DW)
8 BNZ R1,Loop ;branch R1!=zero
9 stall ;delayed branch slot

## Slide 33: Revised FP Loop Minimizing Stalls
Code now takes 6 clock cycles per loop iteration
Speedup = 9/6 = 1.5
Unroll loop 4 times to make faster?
1 Loop: LD F0,0(R1)
2 stall
3 ADDD F4,F0,F2
4 SUBI R1,R1,8
5 BNZ R1,Loop ;delayed branch
6 SD 8(R1),F4 ;altered when move past SUBI
Swap BNZ and SD by changing address of SD

## Slide 34: Unroll Loop Four Times (straightforward way)
Rewrite loop to minimize stalls?
1 Loop: LD F0,0(R1)
2 ADDD F4,F0,F2
3 SD 0(R1),F4 ;drop SUBI & BNEZ
4 LD F6,-8(R1)
5 ADDD F8,F6,F2
6 SD -8(R1),F8 ;drop SUBI & BNEZ
7 LD F10,-16(R1)
8 ADDD F12,F10,F2
9 SD -16(R1),F12 ;drop SUBI & BNEZ
10 LD F14,-24(R1)
11 ADDD F16,F14,F2
12 SD -24(R1),F16
13 SUBI R1,R1,#32 ;alter to 4*8
14 BNZ R1,LOOP
14 + 4 x (2 + 1) + 1= 27 clock cycles, or 6.8 cycles per iteration (2 stalls for SDs, 1 stall for LDs, 1 stall for BNZ)

## Slide 35: Unrolled Loop That Minimizes Stalls
What assumptions made when moved code?
  OK to move store past SUBI even though SUBI changes register
  OK to move loads before stores: get right data?
  When is it safe for compiler to make such changes?
1 Loop: LD F0,0(R1)
2 LD F6,-8(R1)
3 LD F10,-16(R1)
4 LD F14,-24(R1)
5 ADDD F4,F0,F2
6 ADDD F8,F6,F2
7 ADDD F12,F10,F2
8 ADDD F16,F14,F2
9 SD 0(R1),F4
SD -8(R1),F8
SD -16(R1),F8
13 SUBI R1,R1,#32
12 BNZ R1,LOOP
14 SD 8(R1),F16 ;8-32 = -24
14 clock cycles or 3.5 clock cycles per iteration

## Slide 36: Summary of Loop Unrolling Example
Determine that it was legal to move the SD after the SUBI and BNZ, and find the amount to adjust the SD offset.
Determine that unrolling the loop would be useful by finding that the loop iterations are independent, except for the loop maintenance code.
Use extra registers to avoid unnecessary constraints that would be forced by using the same registers for different computations.

## Slide 37: Summary of Loop Unrolling Example
Eliminate the extra tests and branches and adjust the loop maintenance code.
Determine that the loads and stores in the unrolled loop can be interchanged by observing that the loads and stores from different iterations are independent. This requires analyzing the memory addresses and finding that they do not refer to the same address.
Schedule the code, preserving any dependences needed to yield the same result as the original code.

## Slide 38: Superscalar and VLIW Processors

## Slide 39: Multiple Instruction Issue: CPI < 1
To improve a pipeline’s CPI to be better [less] than one, and to utilize ILP better, a number of independent instructions have to be issued in the same pipeline cycle.
Anticipated success of multiple instructions leads to Instructions Per Clock cycle (IPC) vs. CPI

## Slide 40: Multiple Instruction Issue: CPI < 1
Multiple instruction issue processors are of two types:
  Superscalar: A number of instructions (2-8) is issued in the same cycle, scheduled statically by the compiler or dynamically (scoreboarding, Tomasulo).
    Pentium, PowerPC, Sun UltraSparc, Alpha, HP 8000 ...
  VLIW (Very Long Instruction Word):
  A fixed number of instructions (3-16) are formatted as one long instruction word or packet (statically scheduled by the compiler).
      Joint HP/Intel (Itanium).
      Intel Architecture-64 (IA-64) 64-bit processor:
        Explicitly Parallel Instruction Computer (EPIC): Itanium.

## Slide 41: Multiple Instruction Issue: CPI < 1
Limitations of the approaches:
  Available ILP in the program (both).
  Specific hardware implementation difficulties (superscalar).
  VLIW optimal compiler design issues.

## Slide 42: Superscalar Processors
0-8 instruction per cycle
Pipeline control logic will check hazards between the instructions in execution phase and the new instruction sequences.
Issue HW
Pipeline
Instruction
Memory
Issue Packet
Complexity of HW
This stage is pipelined in all dynamic super scalar system

## Slide 43
Cache/
Memory
Fetch
Unit
EU
EU
EU
Register File
Multi Operation
Multiple Instruction
Instruction
Basic Superscalar Approach
Decode/
Issue
Unit

## Slide 44: Example: Superscalar of degree 3 fetch decode execute write back

## Slide 45: Simple Statically Scheduled Superscalar Pipeline
Two instructions can be issued per cycle (two-issue superscalar).
One of the instructions is integer (including load/store, branch). The other instruction is a floating-point operation.
  This restriction reduces the complexity of hazard checking.
  Fetch 64-bits/clock cycle; Int on left, FP on right
  – Can only issue 2nd instruction if 1st instruction issues
Hardware must fetch and decode two instructions per cycle.
Then it determines whether zero (a stall), one or two instructions can be issued per cycle.

## Slide 46: Simple Statically Scheduled Superscalar Pipeline
MEM
EX
EX
EX
ID
ID
IF
IF
EX
EX
ID
ID
IF
IF
WB
WB
EX
MEM
EX
EX
EX
WB
WB
EX
MEM
EX
WB
WB
EX
ID
ID
IF
IF
WB
EX
MEM
EX
EX
EX
ID
ID
IF
IF
Integer Instruction
Integer Instruction
Integer Instruction
Integer Instruction
FP Instruction
FP Instruction
FP Instruction
FP Instruction
1 2 3 4 5 6 7 8
Instruction Type
2-Issue pipeline (Integer & FP)‏

## Slide 47: Unrolled Loop that Minimizes Stalls for Scalar
1 Loop: LD F0,0(R1)‏
2 LD F6,-8(R1)‏
3 LD F10,-16(R1)‏
4 LD F14,-24(R1)‏
5 ADDD F4,F0,F2
6 ADDD F8,F6,F2
7 ADDD F12,F10,F2
8 ADDD F16,F14,F2
9 SD 0(R1),F4
10 SD -8(R1),F8
11 SD -16(R1),F12
12 SUBI R1,R1,#32
13 BNEZ R1,LOOP
14 SD 8(R1),F16 ; 8-32 = -24
14 clock cycles, or 3.5 per iteration
LD to ADDD: 1 Cycle
ADDD to SD: 2 Cycles
Notes: 47

## Slide 48: Loop Unrolling in Superscalar
Integer instruction FP instruction Clock cycle
Loop: LD F0,0(R1) 1
LD F6,-8(R1) 2
LD F10,-16(R1) ADDD F4,F0,F2 3
LD F14,-24(R1) ADDD F8,F6,F2 4
LD F18,-32(R1) ADDD F12,F10,F2 5
SD 0(R1),F4 ADDD F16,F14,F2 6
SD -8(R1),F8 ADDD F20,F18,F2 7
SD -16(R1),F12 8
SD -24(R1),F16 9
SUBI R1,R1,#40 10
BNEZ R1,LOOP 11
SD -32(R1),F20 12
12 cycles, or 2.4 cycles per iteration
Notes: 48

## Slide 49: Multiple Issue Challenges
While Integer/FP split is simple for the HW, get CPI of 0.5 only for programs with:
  Exactly 50% FP operations AND No hazards
If more instructions issue at same time, greater difficulty of decode and issue:
  Even 2-issue => examine 2 opcodes, 6 register specifiers, & decide if 1 or 2 instructions can issue;
Reducing the stalls becomes extremely difficult.
  Use all the techniques we covered and more advanced ones.

## Slide 50: VLIW Processors
Very Long Instruction Word (VLIW) processors
  Tradeoff instruction space for simple decoding
  The long instruction word has room for many operations
  Traditionally, all the operations the compiler puts in the long instruction word can execute in parallel
    E.g., 2 integer operations, 2 FP ops, 2 Memory refs, 1 branch
      16 to 24 bits per field => 7*16 or 112 bits to 7*24 or 168 bits wide
    Not necessarily true for recent VLIW processors
Need compiling technique that identify the operations to be put into long instruction words

## Slide 51: Loop Unrolling in VLIW
Memory Memory FP FP Int. op/ Clock reference 1 reference 2 operation 1 op. 2 branch
LD F0,0(R1) LD F6,-8(R1) 1
LD F10,-16(R1) LD F14,-24(R1) 2
LD F18,-32(R1) LD F22,-40(R1) ADDD F4,F0,F2 ADDD F8,F6,F2 3
LD F26,-48(R1) ADDD F12,F10,F2 ADDD F16,F14,F2 4
ADDD F20,F18,F2 ADDD F24,F22,F2 5
SD 0(R1),F4 SD -8(R1),F8 ADDD F28,F26,F2 6
SD -16(R1),F12 SD -24(R1),F16 7
SD -32(R1),F20 SD -40(R1),F24 SUBI R1,R1,#48 8
SD -0(R1),F28 BNEZ R1,LOOP 9
Unrolled 7 times to avoid delays
7 results in 9 clock cycles, or 1.3 clocks cycles per iteration
Notes: 51

## Slide 52: Commercial Superscalar Processors

## Slide 53: Pentium 4 Pipeline Stages vs. Pentium 3 Pipeline Stages
1
Fetch
2
Fetch
3
Decode
4
Decode
5
Decode
6
Rename
7
ROB Rd
8
Rdy/Sch
9
Dispatch
10
Exec
3 4
TC Fetch
5
Drive
6
Alloc
9
Que
10
Sch
12
Sch
13
Disp
14
Disp
15
RF
16
RF
17
Ex
18
Flgs
19
BrCk
20
Drive
1 2
TC Nxt IP
7 8
Rename
11
Sch
Typical P6 Pipeline
Typical Pentium 4 Pipeline

## Slide 54: Pentium 3 Pipeline Architecture
It is a 3-way issue supersclar
It has 5 execution units (Integer ALU, integer multiply, FP multiply, FP add, FP divide)‏
Notes: 54
  out-of-order speculative pipelining w/ register renaming & reorder buffer

## Slide 55
Pentium 3 Pipeline stages
Exec
10
Dispatch
9
Rdy/Sch (Scheduling Instructions to be executed)‏
8
ROB (reordering instructions)‏
7
Rename registers
6
Decode
5
Decode
4
Decode
3
Fetch
2
Fetch
1

## Slide 56
Pentium 4 pipeline stages
Drive
20
Branch Check
19
Flags
18
Execute
17
Register Files
16
Register Files
15
Dispatch
14
Dispatch
13
Schedule
12
Schedule
11
Schedule
10
Queue
9
Rename
8
Rename
7
Allocation
6
Drive
5
Trace Cache fetch
4
Trace Cache fetch
3
Trace Cache next instruction pointer
2
Trace Cache next instruction pointer
1
Work
Stage
Increasing the number of pipeline stages increases the clock frequency
  It took the industry 28 years to hit 1 GHz and only 18 months to reach 2 GHz.
  The price paid for deeper pipelines is that it is very difficult to avoid stalls (That is why when Pentium 4 was introduced its performance was worse than Pentium 3.)‏
It is a 5-issue supersclar processor

## Slide 57
3 4
TC Fetch
5
Drive
6
Alloc
9
Que
10
Sch
12
Sch
13
Disp
14
Disp
15
RF
16
RF
17
Ex
18
Flgs
19
BrCk
20
Drive
1 2
TC Nxt IP
7 8
Rename
11
Sch
3.2 GB/s System Interface
L2 Cache and Control
BTB
BTB & I-TLB
Decoder
Trace Cache
Rename/Alloc
op Queues
Schedulers
Integer RF
FP RF
Code
ROM
Store
AGU
Load
AGU
ALU
ALU
ALU
ALU
FP move
FP store
Fmul
Fadd
MMX
SSE
L1 D-Cache and D-TLB
TC Nxt IP: Trace cache next instruction pointer
Pointer indicating location of next instruction.

## Slide 58
3.2 GB/s System Interface
L2 Cache and Control
BTB
BTB & I-TLB
Decoder
Trace Cache
Rename/Alloc
op Queues
Schedulers
Integer RF
FP RF
Code
ROM
Store
AGU
Load
AGU
ALU
ALU
ALU
ALU
FP move
FP store
Fmul
Fadd
MMX
SSE
L1 D-Cache and D-TLB
3 4
TC Fetch
5
Drive
6
Alloc
9
Que
10
Sch
12
Sch
13
Disp
14
Disp
15
RF
16
RF
17
Ex
18
Flgs
19
BrCk
20
Drive
1 2
TC Nxt IP
7 8
Rename
11
Sch
TC Fetch: Trace cache fetch
Read the decoded instructions (uOPs)‏

## Slide 59
3.2 GB/s System Interface
L2 Cache and Control
BTB
BTB & I-TLB
Decoder
Trace Cache
Rename/Alloc
op Queues
Schedulers
Integer RF
FP RF
Code
ROM
Store
AGU
Load
AGU
ALU
ALU
ALU
ALU
FP move
FP store
Fmul
Fadd
MMX
SSE
L1 D-Cache and D-TLB
3 4
TC Fetch
5
Drive
6
Alloc
9
Que
10
Sch
12
Sch
13
Disp
14
Disp
15
RF
16
RF
17
Ex
18
Flgs
19
BrCk
20
Drive
1 2
TC Nxt IP
7 8
Rename
11
Sch
Drive: Wire delay
Drive the uOPs to the allocator

## Slide 60
3.2 GB/s System Interface
L2 Cache and Control
BTB
BTB & I-TLB
Decoder
Trace Cache
Rename/Alloc
op Queues
Schedulers
Integer RF
FP RF
Code
ROM
Store
AGU
Load
AGU
ALU
ALU
ALU
ALU
FP move
FP store
Fmul
Fadd
MMX
SSE
L1 D-Cache and D-TLB
3 4
TC Fetch
5
Drive
6
Alloc
9
Que
10
Sch
12
Sch
13
Disp
14
Disp
15
RF
16
RF
17
Ex
18
Flgs
19
BrCk
20
Drive
1 2
TC Nxt IP
7 8
Rename
11
Sch
Alloc: Allocate resources required for execution. The
resources include Load buffers, Store buffers, etc..

## Slide 61
3.2 GB/s System Interface
L2 Cache and Control
BTB
BTB & I-TLB
Decoder
Trace Cache
Rename/Alloc
op Queues
Schedulers
Integer RF
FP RF
Code
ROM
Store
AGU
Load
AGU
ALU
ALU
ALU
ALU
FP move
FP store
Fmul
Fadd
MMX
SSE
L1 D-Cache and D-TLB
3 4
TC Fetch
5
Drive
6
Alloc
9
Que
10
Sch
12
Sch
13
Disp
14
Disp
15
RF
16
RF
17
Ex
18
Flgs
19
BrCk
20
Drive
1 2
TC Nxt IP
7 8
Rename
11
Sch
Rename: Register renaming

## Slide 62
3.2 GB/s System Interface
L2 Cache and Control
BTB
BTB & I-TLB
Decoder
Trace Cache
Rename/Alloc
op Queues
Schedulers
Integer RF
FP RF
Code
ROM
Store
AGU
Load
AGU
ALU
ALU
ALU
ALU
FP move
FP store
Fmul
Fadd
MMX
SSE
L1 D-Cache and D-TLB
3 4
TC Fetch
5
Drive
6
Alloc
9
Que
10
Sch
12
Sch
13
Disp
14
Disp
15
RF
16
RF
17
Ex
18
Flgs
19
BrCk
20
Drive
1 2
TC Nxt IP
7 8
Rename
11
Sch
Que: Write into the uOP Queue
uOPs are placed into the queues, where they are held until there is room in the schedulers

## Slide 63
3.2 GB/s System Interface
L2 Cache and Control
BTB
BTB & I-TLB
Decoder
Trace Cache
Rename/Alloc
op Queues
Schedulers
Integer RF
FP RF
Code
ROM
Store
AGU
Load
AGU
ALU
ALU
ALU
ALU
FP move
FP store
Fmul
Fadd
MMX
SSE
L1 D-Cache and D-TLB
3 4
TC Fetch
5
Drive
6
Alloc
9
Que
10
Sch
12
Sch
13
Disp
14
Disp
15
RF
16
RF
17
Ex
18
Flgs
19
BrCk
20
Drive
1 2
TC Nxt IP
7 8
Rename
11
Sch
Sch: Schedule
Write into the schedulers and compute dependencies. Watch for dependency to resolve.

## Slide 64
3.2 GB/s System Interface
L2 Cache and Control
BTB
BTB & I-TLB
Decoder
Trace Cache
Rename/Alloc
op Queues
Schedulers
Integer RF
FP RF
Code
ROM
Store
AGU
Load
AGU
ALU
ALU
ALU
ALU
FP move
FP store
Fmul
Fadd
MMX
SSE
L1 D-Cache and D-TLB
3 4
TC Fetch
5
Drive
6
Alloc
9
Que
10
Sch
12
Sch
13
Disp
14
Disp
15
RF
16
RF
17
Ex
18
Flgs
19
BrCk
20
Drive
1 2
TC Nxt IP
7 8
Rename
11
Sch
Disp: Dispatch
Send the uOPs to the appropriate execution unit.

## Slide 65
3.2 GB/s System Interface
L2 Cache and Control
BTB
BTB & I-TLB
Decoder
Trace Cache
Rename/Alloc
op Queues
Schedulers
Integer RF
FP RF
Code
ROM
Store
AGU
Load
AGU
ALU
ALU
ALU
ALU
FP move
FP store
Fmul
Fadd
MMX
SSE
L1 D-Cache and D-TLB
3 4
TC Fetch
5
Drive
6
Alloc
9
Que
10
Sch
12
Sch
13
Disp
14
Disp
15
RF
16
RF
17
Ex
18
Flgs
19
BrCk
20
Drive
1 2
TC Nxt IP
7 8
Rename
11
Sch
RF: Register File
Read the register file. These are the source(s) for the pending operation (ALU or other).

## Slide 66
3.2 GB/s System Interface
L2 Cache and Control
BTB
BTB & I-TLB
Decoder
Trace Cache
Rename/Alloc
op Queues
Schedulers
Integer RF
FP RF
Code
ROM
Store
AGU
Load
AGU
ALU
ALU
ALU
ALU
FP move
FP store
Fmul
Fadd
MMX
SSE
L1 D-Cache and D-TLB
3 4
TC Fetch
5
Drive
6
Alloc
9
Que
10
Sch
12
Sch
13
Disp
14
Disp
15
RF
16
RF
17
Ex
18
Flgs
19
BrCk
20
Drive
1 2
TC Nxt IP
7 8
Rename
11
Sch
Ex: Execute
Execute the uOPs on the appropriate execution port.

## Slide 67
3.2 GB/s System Interface
L2 Cache and Control
BTB
BTB & I-TLB
Decoder
Trace Cache
Rename/Alloc
op Queues
Schedulers
Integer RF
FP RF
Code
ROM
Store
AGU
Load
AGU
ALU
ALU
ALU
ALU
FP move
FP store
Fmul
Fadd
MMX
SSE
L1 D-Cache and D-TLB
3 4
TC Fetch
5
Drive
6
Alloc
9
Que
10
Sch
12
Sch
13
Disp
14
Disp
15
RF
16
RF
17
Ex
18
Flgs
19
BrCk
20
Drive
1 2
TC Nxt IP
7 8
Rename
11
Sch
Flgs: Flags
Compute flags (zero, negative, etc..). These are typically input to a branch instruction.

## Slide 68
3.2 GB/s System Interface
L2 Cache and Control
BTB
BTB & I-TLB
Decoder
Trace Cache
Rename/Alloc
op Queues
Schedulers
Integer RF
FP RF
Code
ROM
Store
AGU
Load
AGU
ALU
ALU
ALU
ALU
FP move
FP store
Fmul
Fadd
MMX
SSE
L1 D-Cache and D-TLB
3 4
TC Fetch
5
Drive
6
Alloc
9
Que
10
Sch
12
Sch
13
Disp
14
Disp
15
RF
16
RF
17
Ex
18
Flgs
19
BrCk
20
Drive
1 2
TC Nxt IP
7 8
Rename
11
Sch
Br Ck: Branch Check
The branch operation compares result of actual branch direction with the prediction.

## Slide 69
3.2 GB/s System Interface
L2 Cache and Control
BTB
BTB & I-TLB
Decoder
Trace Cache
Rename/Alloc
op Queues
Schedulers
Integer RF
FP RF
Code
ROM
Store
AGU
Load
AGU
ALU
ALU
ALU
ALU
FP move
FP store
Fmul
Fadd
MMX
SSE
L1 D-Cache and D-TLB
3 4
TC Fetch
5
Drive
6
Alloc
9
Que
10
Sch
12
Sch
13
Disp
14
Disp
15
RF
16
RF
17
Ex
18
Flgs
19
BrCk
20
Drive
1 2
TC Nxt IP
7 8
Rename
11
Sch
Drive: Wire delay
Drive the result of the branch check to the front end of the machine.

## Slide 70: Evolution of Processor Performance
CPI > 10 1.1-10 0.5 - 1.1 .35 - .5 (?)
Pipelined
(single issue)
Multi-cycle
Multiple Issue (CPI <1)
Superscalar/VLIW